## Slide 1: Direct and Indirect Calorimetery
Lecture No.: 10-12

## Slide 2: Measuring the Body’s Heat Production
All of the body’s metabolic processes result in heat production
The rate of heat production operationally defines the rate of energy metabolism
The calorie is the basic unit of heat measurement
Calorimetry defines the measurement of heat transfer
  Direct calorimetry
  Indirect calorimetry
Notes: <number>

## Slide 3: Direct and indirect heat measurement

## Slide 4: Direct Calorimetry
Directly measures energy expenditure during rest and physical activity
Has considerable theoretical implications but limited practical applications in humans
  Accurate measurements of heat production in the calorimeter require considerable time and expense and formidable engineering expertise
  Calorimeters remain inapplicable for energy determinations for most sport, occupational, and recreational activities
Notes: <number>

## Slide 5: Human calorimeter

## Slide 6: Calorimeter Types
Airflow calorimeter: The temperature change in air that flows through an insulated space, multiplied by the air’s mass and specific heat, determines heat production
Water calorimeter: A change in temperature occurs in water flowing through coils in environmentally self-contained body suits worn by astronauts
Gradient layer calorimetry: Measures body heat that flows from subject through a sheet of insulating materials
Storage calorimetry: Subject sits in an insulated tank surrounded by a known mass of water at a constant temperature and the heat given off by the subject changes the temperature of the surrounding water

## Slide 7: Indirect Calorimetry
All energy-releasing reactions in humans depend on oxygen use so measuring oxygen consumption during physical activities provides an indirect yet accurate estimate of energy expenditure
Is simpler and less expensive
Yields results comparable to direct measurement in the human calorimeter
Two types:
  Closed-circuit spirometry
  Open-circuit spirometry

## Slide 8: Closed-Circuit Spirometry
Simple method and is able to directly measure O2 consumption but has limited practical applications
Procedure:
  Subject breathes 100% O2 from prefilled spirometer
  Is a closed system because the subject rebreathes only the gas in the spirometer
  A canister of potassium hydroxide placed in the breathing circuit absorbs CO2 in the exhaled air
  A drum attached to the spirometer revolves at a known speed to record O2 consumed from changes in the system’s total volume

## Slide 9: Closed-circuit method

## Slide 10: Closed-Circuit Spirometry cont’d
During exercise, closed-circuit spirometry measurement becomes problematic
  Subject must remain close to the bulky equipment
  Circuit offers considerable resistance to accommodate the large breathing volumes during exercise
  CO2 removal lags behind its production rate during intense exercise

## Slide 11: Open-Circuit Spirometry
  Provides a relatively simple, practical way to measure O2 consumption and infer energy expenditure
Procedure:
  Subject inhales ambient air with a constant composition (20.93% O2, 0.03% CO2 , 79.04% nitrogen)
  Changes in O2 and CO2 % in expired air compared with the % in inspired ambient air indirectly reflect the ongoing process of energy metabolism

## Slide 13: Indirect Open-Circuit Calorimetry Procedures
Portable spirometry
Bag technique
Computerized instrumentation

## Slide 14: Chemical Gas Analyzers for Calibration Purposes
Micro-Scholander technique: Measures oxygen and carbon dioxide concentration in expired air in about 10 minutes to an accuracy of ± 0.015 mL per 100 mL of gas
Haldane method: Uses a larger air sample and requires between 10 and 15 minutes to complete one analysis

## Slide 15: Micro-Scholander and Haldane gas analyzers

## Slide 16: Doubly Labeled Water Technique
Provides a safe way to estimate total daily energy expenditure in free-living conditions without the normal constraints imposed by laboratory procedures
Expensive and needs sophisticated measurement equipment

## Slide 17: Doubly Labeled Water Technique cont’d
Procedure:
  Subject consumes water with a known concentration of stable isotopes of hydrogen and O2
  Labeled hydrogen leaves the body in sweat, urine, and pulmonary water vapor, labeled O2 leaves as both water and CO2
  Differences between elimination rates of isotopes relative to the body’s normal levels estimate total CO2 production
    O2 consumption is estimated from CO2 production and an assumed respiratory quotient value of 0.85

## Slide 18: Doubly Labeled Water Technique cont’d
Within 3-5% compared to directly measured energy expenditure in controlled settings
Provides an ideal way to assess total energy expenditure over prolonged periods including bed rest and extreme activities
Drawbacks include the cost of the water and expense incurred in spectrometric analysis of both isotopes

## Slide 20: Respiratory Quotient
Carbohydrate, fat, and protein require different amounts of O2 for complete oxidation of each molecule’s carbon and hydrogen atoms to the CO2 and water end products
Respiratory quotient (RQ) describes this ratio of metabolic gas exchange
  RQ = CO2 produced ÷ O2 consumed
  Provides a convenient guide to approximate the nutrient mixture catabolized for energy during rest and aerobic exercise

## Slide 21: RQ for Macronutrients
Carbohydrate RQ=1.00 because gas exchange during glucose oxidation produces a number of CO2 molecules equal to the number of O2 molecules consumed
Fat RQ=0.70 because fat catabolism requires more O2 in relation to CO2 production
Protein RQ=0.82 because proteins require more oxygen in relation to carbon dioxide produced
RQ seldom reflects oxidation of one macronutrient, but instead a mixture with an RQ intermediate between 0.70-1.00

## Slide 22: Respiratory Exchange Ratio
Reflects the ratio of CO2 produced to O2 consumed when factors other than food combustion alter the exchange of O2 and CO2 in the lungs and the ratio of gas exchange no longer reflects only the substrate mixture of energy metabolism
Is computed in the same manner as RQ

## Slide 24
thanks