## Slide 1
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
The Study of Microbial Structure: Microscopy and Specimen Preparation

## Slide 2: Scale
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>

## Slide 3: Discovery of Microorganisms
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Antony van Leeuwenhoek (1632-1723)
  first person to observe and describe micro-organisms accurately
Figure 1.1b

## Slide 4: Lenses and the Bending of Light
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
light is refracted (bent) when passing from one medium to another
refractive index
  a measure of how greatly a substance slows the velocity of light
direction and magnitude of bending is determined by the refractive indexes of the two media forming the interface

## Slide 5: Lenses
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
focus light rays at a specific place called the focal point
distance between center of lens and focal point is the focal length
strength of lens related to focal length
  short focal length more magnification

## Slide 6
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.2

## Slide 7: The Light Microscope
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
many types
  bright-field microscope
  dark-field microscope
  phase-contrast microscope
  fluorescence microscopes
are compound microscopes
  image formed by action of 2 lenses

## Slide 8: The Bright-Field Microscope
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
produces a dark image against a brighter background
has several objective lenses
  parfocal microscopes remain in focus when objectives are changed
total magnification
  product of the magnifications of the ocular lens and the objective lens

## Slide 9
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.3

## Slide 10
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.4

## Slide 11: Microscope Resolution
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
ability of a lens to separate or distinguish small objects that are close together
wavelength of light used is major factor in resolution
  shorter wavelength  greater resolution

## Slide 12
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
working distance
  distance between the front surface of lens and surface of cover glass or specimen

## Slide 13
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.5

## Slide 14
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.6

## Slide 15: The Dark-Field Microscope
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
produces a bright image of the object against a dark background
used to observe living, unstained preparations

## Slide 16
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.7b

## Slide 17: The Phase-Contrast Microscope
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
enhances the contrast between intracellular structures having slight differences in refractive index
excellent way to observe living cells

## Slide 18
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.9

## Slide 19
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.10

## Slide 20: The Differential Interference Contrast Microscope
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
creates image by detecting differences in refractive indices and thickness of different parts of specimen
excellent way to observe living cells

## Slide 21: The Fluorescence Microscope
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
exposes specimen to ultraviolet, violet, or blue light
specimens usually stained with fluorochromes
shows a bright image of the object resulting from the fluorescent light emitted by the specimen

## Slide 22
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.12

## Slide 23
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.13c and d

## Slide 24: Preparation and Staining of Specimens
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
increases visibility of specimen
accentuates specific morphological features
preserves specimens

## Slide 25: Fixation
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
process by which internal and external structures are preserved and fixed in position
process by which organism is killed and firmly attached to microscope slide
  heat fixing
    preserves overall morphology but not internal structures
  chemical fixing
    protects fine cellular substructure and morphology of larger, more delicate organisms

## Slide 26: Dyes and Simple Staining
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
dyes
  make internal and external structures of cell more visible by increasing contrast with background
  have two common features
    chromophore groups
      chemical groups with conjugated double bonds
      give dye its color
    ability to bind cells

## Slide 27: Dyes and Simple Staining
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
simple staining
  a single staining agent is used
  basic dyes are frequently used
    dyes with positive charges
    e.g., crystal violet

## Slide 28: Differential Staining
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
divides microorganisms into groups based on their staining properties
  e.g., Gram stain
  e.g., acid-fast stain

## Slide 29: Gram staining
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
most widely used differential staining procedure
divides Bacteria into two groups based on differences in cell wall structure

## Slide 30
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.14
primary stain
mordant
counterstain
decolorization
positive
negative

## Slide 31
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.15c
Escherichia coli – a gram-negative rod

## Slide 32: Acid-fast staining
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
particularly useful for staining members of the genus Mycobacterium
    e.g., Mycobacterium tuberculosis – causes tuberculosis
    e.g., Mycobacterium leprae – causes leprosy
  high lipid content in cell walls is responsible for their staining characteristics

## Slide 33: Staining Specific Structures
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Negative staining
  often used to visualize capsules surrounding bacteria
  capsules are colorless against a stained background

## Slide 34: Staining Specific Structures
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Spore staining
  double staining technique
  bacterial endospore is one color and vegetative cell is a different color
Flagella staining
  mordant applied to increase thickness of flagella

## Slide 35: Electron Microscopy
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
beams of electrons are used to produce images
wavelength of electron beam is much shorter than light, resulting in much higher resolution
Figure 2.20

## Slide 36: The Transmission Electron Microscope
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
electrons scatter when they pass through thin sections of a specimen
transmitted electrons (those that do not scatter) are used to produce image
denser regions in specimen, scatter more electrons and appear darker

## Slide 37: EM
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.23

## Slide 38: Specimen Preparation
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
analogous to procedures used for light microscopy
for transmission electron microscopy, specimens must be cut very thin
specimens are chemically fixed and stained with electron dense material

## Slide 39: Other preparation methods
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
shadowing
  coating specimen with a thin film of a heavy metal
freeze-etching
  freeze specimen then fracture along lines of greatest weakness (e.g., membranes)

## Slide 40
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.25

## Slide 41: Ebola
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Notes: <number>
Ebola

## Slide 42: Fly head
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Notes: <number>
Fly head

## Slide 43: The Scanning Electron Microscope
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
uses electrons reflected from the surface of a specimen to create image
produces a 3-dimensional image of specimen’s surface features

## Slide 44
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.27

## Slide 45: Newer Techniques in Microscopy
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
confocal microscopy and scanning probe microscopy
have extremely high resolution
can be used to observe individual atoms
Figure 2.20

## Slide 46: Confocal Microscopy
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
confocal scanning laser microscope
laser beam used to illuminate spots on specimen
computer compiles images created from each point to generate a 3-dimensional image

## Slide 47
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.29

## Slide 48
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
Figure 2.30

## Slide 49: Scanning Probe Microscopy
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
scanning tunneling microscope
  steady current (tunneling current) maintained between microscope probe and specimen
  up and down movement of probe as it maintains current is detected and used to create image of surface of specimen

## Slide 50: Scanning Probe Microscopy
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
<number>
atomic force microscope
  sharp probe moves over surface of specimen at constant distance
  up and down movement of probe as it maintains constant distance is detected and used to create image