## Slide 1: Mozzarella Cheese
Originated in Italy
Soft and un-ripened variety of cheese
Smooth, moist surface and perfect sheen
Elastic and stringy body
Having good stretching and melting characteristics
Key ingredient for Pizza preparation

## Slide 2: Type of Mozzarella

## Slide 3: Mozzarella Cheese
Milk
¯
Filtration/Clarification
¯
Standardisation (3- 4% fat)
¯
Pasteurization (63°C/30 min.)
¯
Cooling (31°C)
¯
Starter addition
[Streptococcus thermophilus and Lactobacillus bulgaricus (1:1) @ 1-2%]
¯
Rennet addition (1.5 g/100 L milk)

## Slide 4
Cutting
¯
Cooking (42-44°C)
¯
Draining
¯
Cheddaring (0.70% acidity)
¯
Milling
¯
Plasticising /stretching under hot water (80-85°C)
¯
Moulding
¯
Brining (20-22% chilled brine)
¯
Packaging

## Slide 5
Direct Acid Method
Skim milk

Filtration/Clarification

Standardization

Pasteurization (63°c/30/min.)

Chilling (4-8°c)

Acidifying

Heating

Rennet addition

## Slide 6
Cutting

Cooking

Draining

Plasticizing/stretching under hot water (80-85°C)

Moulding

Brining (20-22%) chilled brine)

Packaging

Storage