## Slide 1: Dimensional Analysis and Its Applications
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Dimensional Analysis
Dimensional Analysis is a process of arranging various factors in a manner that it forms dimensionless number. Its principal use is to deduce the expression of dependent variable in terms of independent variables in a study.
An equation will be dimensionally homogeneous if the dimensions of various terms on the two sides of the equation are identical. A dimensionally homogeneous equation is independent of the fundamental units of measurement and is applicable to all systems of units.
T = 2π √l/g, Dimension on LHS and RHS same as [T] shows homogeneity of equation.
Utilized in developing of models to predict the mechanisms and economize the resources (6 Ms) requirements.
Utilized for hydraulic similitude of Prototype and model of physical structure, equipments, Machines and products for safe and efficient design.

## Slide 3: Application of Dimensional Analysis
Application of Dimensional Analysis
To determine the dimensional homogeneity of any equation which helps to determine the dimensions and thus the units of any quantity.
Units can be easily transformed from one system to another.
To establish relationship between number of variables.
To reduce equations by arranging variables in dimensionless forms.
The application of dimensional analysis to mathematically represent engineering problems consists of several steps.
Steps for Dimensional Analysis
Formulate a differential equations and/or algebraic expressions which adequately describe the problem, together with the required boundary conditions;
Select the appropriate dimensionless variables tor all independent and dependent variables involved, using arbitrary terms or boundary values for the denominator in each case;

## Slide 4: Steps for Dimensional Analysis
Substitute the new dimensionless variables into each differential equation and boundary condition to normalize them;
Group into functional form all dimensionless variables and those parameters generated;
Reduce the functionality to the minimum possible number of independent groups; and
Drop any groups in which the arbitrary terms can not be divided out using other groups of the functionality.

## Slide 5: Rayleigh’s Method for Dimensional Analysis
Independent variables are identified which will express the functional relationship most closely. A maximum of three to four variables must be selected.
If the dependent variable X is some function of the independent variables x1, x2, x3….,
The equation is written as:
X = f (x1, x2, x3 …)
Above equation may be written as:
X = C(x1a , x2 b , x3 c ,…), where C is a dimensionless coefficient to be determined through experiments Values of a, b, c etc are determined by comparing the powers on both sides.

## Slide 6: Buckingham’s π- method of Dimensional Analysis
It states that if there are ‘n’ variables in a dimensionally homogeneous equation and if these variables contain ‘m’ fundamental (primary) dimensions then the variables can be grouped into (n - m) dimensionless terms.
These dimensionless terms are called π Terms.
We use M L T fundamental quantities in fluid mechanics. Mathematically if x1 depends on other variables x2, x3, x4...xn the equation can be given as
x1 = f ( x2, x3, x4 ……………, xn)
f(x1, x2, x3, x4 ……………, xn) = 0 (i)
Where x are dimensional physical quantities such as velocity, density, pressure, area, diameter etc. Then the phenomenon given in equation (i) can be described by (n-m) dimensionless ‘π’ terms.
f (π1, π2,…………………. πn-m) = 0 where ‘m’ represents the fundamental dimensions such as mass, length and time.

## Slide 7: Numerical
The resistance R experienced by a partially submerged body depends upon the velocity V, length of the body l, viscosity of the fluid µ, density of the fluid ρ and gravitational acceleration g. Obtain a dimensionless express for resistance R.
Solution: Mathematically following relation can be given:
R = f (V, l, µ, ℓ, g)
f (R,V, l, µ, ℓ , g) = 0
No. of variables n = 6 and No. of fundamental variable m =3
Therefore No. of π terms = 6 -3 =3 π Terms
Choose length l, velocity V and density ℓ are three repeating variables.
Analysis of π- terms
Π1 = (la1, Vb1, ℓ c1, R)→ [M0L0T0] =[L]a1 [Lt-1 ]b1 [ml-3 ]c1 [MLT-2]
Π2 = (la2, Vb2, ℓ c2, µ)→ [M0L0T0]= [L]a2 [Lt-1 ]b2 [ml-3 ]c2 [ML-1T-1]
Π3 = (la3, Vb3, ℓc3, g)→ [M0L0T0] = [L]a3 [Lt-1 ]b3 [ml-3 ]c3 [LT-2]

## Slide 8: Numerical
On solution of equations:
Π1 = R/ l2 v2 ℓ
Π2 =µ/l V ℓ
Π3 = l g/ V2
The functional relationship can be given as:
Φ = f [Π1, Π2 , Π3 ] = 0
Φ = f [R/ l2 v2 ℓ, µ/l V ℓ, l g/ V2] = 0
R/ l2 v2 ℓ = Φ (µ/l V ℓ, l g/ V2)
R/ l2 v2 ℓ = Φ ( l V ℓ/ µ, V/√ l g) (Since reciprocal of π-term and its square root is non-dimensional)
R = l2 v2 ℓ Φ ( l V ℓ/ µ, V/√ l g)
R = l2 v2 ℓ Φ ( NRe, NFr) where Nre : Reynolds Number & NFr: Froud Number.
It is evident that resistance R is a function of Reynolds number and Froude’s number.

## Slide 9: Numerical
Derive a general functional relationship of a flow phenomenon which depends upoconstantn the following variables
f[ ℓ , µ, g, K, p, V, σ, l, D] = constant
Solution:
N=9 and m= 3, Therefore No. of π-terms = m-n=9-3=6
Taking ℓ , l , v as repeating variables and on solving the equation by homogeneity principle
Π1 =(la1, Vb1, ℓ c1, µ) = l V ℓ/ µ = NRe = Reynolds Number
Π2 = (la2, Vb2, ℓ c2, g) = V/√ l g = N Fr = Froud Number
Π3 = (la3, Vb3, ℓc3, k) = V/ √ K/ ℓ = NM = Mach No.
Π4 = (la4, Vb4, ℓc4, p) = V/ √ p/ ℓ = NE = Euler No.
Π5 = (la5, Vb5, ℓc5, σ) = V/ √ σ/ l ℓ = NWb =Weber No.
Π6 = (la6, Vb6, ℓc6, D) =D/l
Therefore general relationship can be written as:
f (NRe, NF, NM, NE, NWb, D/L) = Constant

## Slide 10
THANK YOU