## Slide 1: Hardness of Water
Notes: <number>

## Slide 2
Soap destroying power
Temporary (carbonates): Ca/Mg bicarbonates
Permanent (non-carbonates): Ca/Mg sulphates
Chlorides
Nitrates
Other less important
  Fe
  Mn Compounds but non-significant
  Al
Expressed in Milliequivalents per liter (mEq/liter)
1 mEq/liter = 50 mg CaCO3 (50ppm) in 1 liter water
Notes: <number>

## Slide 3
Class of water mEq/liter Hardness level
(Carbonate)
Soft water < 1 50 mg/l
Moderately hard 1-3 50-150 mg/l
Hard water 3-6 150-300 mg/l
Very hard >6 >300 mg/l
Drinking water should be moderately hard
Water with >3 mEq hardness needs treatment
Classification
Notes: <number>

## Slide 4
More soap or detergent needed
On heating carbonates precipitates causing
  furring
  scaling of boilers which cause
    greater fuel consumption
    loss of efficiency
    boil of explosion.
Adverse effect on cooking
  there is loss of natural colour and appearance
Short life of cloths
Unsuitable for many industry:
  Economic loss
  Shorten the life of pipes and fixture
Disadvantages
Notes: <number>

## Slide 5
Removal of Hardness of water
Temporary hardness Permanent hardness
Boiling Addition of Na2CO3
Addition of lime Base exchange process
Addition of Na2CO3
Notes: <number>

## Slide 6
There is oxygen expulsion
Calcium carbonate precipitation
Ca (HCO3)2  CaCO3 + H2O + CO2
Expensive for large scale use
Boiling
Notes: <number>

## Slide 7
1 oz quick lime / 700 gallons water /degree hardness
(14.25 ppm)
Absorption of carbon dioxide
Precipitation of calcium carbonate
Ca (OH)2 + Ca (HCO3)2  2 CaCO3 + 2 H2O
Addition of lime
Notes: <number>

## Slide 8
Addition of Sodium carbonate
Removes both temporary and permanent hardness
Na2CO3 + Ca (HCO3)2  2 NaHCO3 + CaCO3
CaSO4 + Na2CO3  CaCO3 + Na2SO4
Notes: <number>

## Slide 9
Water is soften to zero hardness
Permutit is regenerated
concentrated sodium chloride/brine
Base exchange process
Removes both temporary and permanent hardness
Sodium permutit  Sodium aluminium silica
(Na2Al2Si2O.H2O)
Sodium is exchanged with Ca/Mg
formation of Ca/Mg permutit
Notes: <number>

## Slide 10
Park’s Textbook of Preventive and Social Medicine, 24th Edition
By: K. Park, Banarsidas Bhanot Publishers.
Reference book