## Slide 1
Class Lecture
MICROBIOLOGICAL QUALITY OF MILK
FOR CHEESE MAKING
Dr. Sanjeev Kumar
Associate Professor
Department of Dairy Technology
SGIDT, Patna-14

## Slide 2
Microorganisms in Raw Milk
According to the main points of attack on the major milk constituents, the saprophytic bacteria --- subdivided as follows:
The change in milk composition may interfere with manufacture, if fermentation --- involved in the manufacture process, and this may affect the yield and quality of the product.
The flavor of the raw milk may be adversely influenced (e.g. rancidity) and this may directly affect the flavor of the product e.g. Cottage cheese.
Heat-stable bacterial enzymes may continue to act in the product, particularly during long storage, and adversely affect the stability and/or flavor of cream and UHT milk.

## Slide 3
Clean milk secreted from the udder of the healthy animal contains only few numbers of microorganism (< 10,000/ml).
Milk obtained from mastitis cow may contain high numbers of microorganism as well as leucocytes depending on the severity of infection
Milk --- held at around 4°C during transport an in cheese plant.

## Slide 4
Milk stored under such conditions contains predominantly psychotropic bacteria (over one million/ml).
The common genera encountered---Pseudomonas, Aeromonas, Alcaligenes, lactic acid bacteria, gram positive spore formers, coryne form group, enterococci and coli forms.
Somatic Cells
Milk used for preparation of cheese --- from healthy animal with a somatic cell count of < 50,000/ml
If raw milk contains > 50,000 somatic cells/ml results in phagocytosization of lactic acid bacteria (LAB) leads
To slow starter activity in cheese vat,
increase in rennet clotting time causing decreased curd firmness and
a loose final body and texture.

## Slide 5
Antibiotic Residues
Antimicrobial agents administered to cows in the course of lactation can pass to milk in various levels and inhibit starter activity
Disinfectants and Preservatives
Quaternary ammonium compounds (QAC’s) present more potential problems, because they maintain activity in milk, and LAB -- sensitive to low concentrations.
Amount of chemical sanitizer that might enter milk through lack of rinsing should not be sufficient to cause culture inhibition.
Bacteriophages
Bacteriophagic infection of starter cultures --- result in failure of the fermentation and loss of product

## Slide 6
Raw Milk Associated Inhibitors:
Lactoperoxidase system --- the most significant microbial inhibitor in raw milk,
but the presence of agglutinins -- an important problem in acid-coagulated cheeses.
Other naturally occurring microbial inhibitors in milk include
lysozyme and
lactoferrin

## Slide 7
CHILLING,STORAGE,CLARIFICATION AND BACTOFUGATION

## Slide 8
Chilling and Cold Storage
Raw milk --- sometimes cooled to about 4oC and
Stored in refrigerated tanks or storage tanks prior to its conversion into cheese.
Many properties change significantly like rennet coagulation time, firmness, moisture retention etc.
Rennet coagulation time increases, firmness decreases and moisture retention increases due to cold storage of milk

## Slide 9
Technological properties as a result of chilling and cold storage of the raw milk-- improved by adopting measures
1. Acidification of cheese milk with lactic acid to pH 6.5 2. Addition of calcium chloride @ 0.02% 3. Addition of more rennet within permissible limits 4. Use of higher renneting temperature 5. Use of higher cooking temperatures

## Slide 10
Clarification
Clarification --- one of the centrifugal processes
Used to remove leukocytes, cellular debris and particles from earth or fodder gaining entry into milk
Clarification
Decreases the tendency of fat to form aggregates on standing
Increases the rate of multiplication of starter organisms
May increase the fat losses in whey and
May also decrease the moisture and yield of cheese

## Slide 11
Bactofugation
The bactofuge system ---used in the cheese industry to remove spores from cheese milk that could cause late fermentation in semi-hard cheeses.
Effect of bactofugation on cheese making : • Effective method for preventing late blowing defect in semi-hard or hard varieties of cheeses as mainly due to removal of anaerobic microorganisms • Facilitates reduction or elimination in the use of nitrates (nitrates are added to prevent ‘late fermentation’ in cheese) • Weakens the coagulum during cheesemaking which ---- overcome by addition of calcium chloride