## Slide 1: Motion Study
Dairy Plant Management (DTT-421)
A K JHA

## Slide 2: Motion Study
Motion study is the systematic study of human motions used to perform an operation.
The purpose is to eliminate unnecessary motions and to identify the best sequence of motions for maximum efficiency.
Frank Gilbreth originated the concept in bricklaying trade.
  Av. no. of brick laid per hour increased 3 times

## Slide 3: Motion Study Techniques
The most used techniques are:
Motion Study Principles
Analysis of therbligs
Micromotion study
Charts

## Slide 4: Motion study principles
The work of Gilbreth laid the foundation of motion study principles, which are guidelines for designing motion-efficient work procedures.
The guidelines are divided into three categories:
  Principles for use of body
  Principles for arrangement of workplace
  And principles for design of tools and equipment
  Work methods that are motion-efficient
    Eliminate unnecessary motions.
    Combine activities
    Reduce fatigue.
    Improve the workplace arrangement.
    Improve the design of tool and equipment.

## Slide 5: Therbligs
Therbligs are the basic elemental motions.
The idea is to break jobs down into minute elements and base improvements on an analysis of these basic elements by eliminating, combining, or rearranging them.
Some basic Therbligs are:
  Search: hunting for an item with hands and/ or the eyes.
  Select: means to chose from a group of objects.
  Grasp: to take hold of an object.
  Hold refers to retention of an object after it has been grasped.
  Transport load means movemet of an object after hold.
  Relaese load means to deposit the load

## Slide 6: Micromotion Study
Frank Gilbreth andLlillian Gilbreth introduced motion pictures for studying motions, called micromotion study.