## Slide 1: Freezing Time by Neumann, Tao and Non dimensional Method
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Neumann Problem for Freezing Time
Solution given by Neumann for freezing time determinationin unsteady state heat transfer process for sudden cooling with freezing medium was published in Carslaw and Jaeger (1959). It is well known by Neumann Problem.
This approach utilizes one dimensional heat transfer in a semi-infinite body. There are three basic equations which describe the Neumann Problem. The first two are partial differential equations which describe the temperature distribution in the frozen and unfrozen portion of the semi-infinite body in one dimension.
These are as follows where subscripts 1 and 2 refers to the frozen and unfrozen portion of the body, respectively:
∂2 T1/ ∂ x2 = (ℓ1 Cp1/k1) (∂ T1/ ∂ t )
∂2 T2/ ∂ x2 = (ℓ2 Cp2/k2) (∂ T2/ ∂ t )
The third equation can be expressed as the difference in heat flux between the solid and liquid portions of a semi-infinite body which must be equal to the heat generated at the freezing front. This can be written as :
k1∂ T1/ ∂ x - k2 ∂ T2 / ∂ x = (ℓ ∆H dx/dt)

## Slide 3: Neumann Problem
The solution of these equations which describes the temperature distribution in the solid and liquid portions of the semi-infinite body is expressed in error function form.
The Neumann problem and the approach used for computation of freezing times represent slight improvement over Plank equation.
It is more accurate as it allows two different thermal conductivities and specific heats for unfrozen and frozen portions.
The Neumann problem assumes that the latent heat of fusion is removed at constant temperature Tf and does not provide the incorporation of convection heat transfer coefficient into freezing time computation. The application is limited to semi-infinite body geometry only. Due to use of Guass Error function curve/table, in general the procedure for calculation of freezing time is complex.
This approach is unlikely to be used when compared to other less complex procedures for calculation of freezing times.

## Slide 4: Tao Solutions for Freezing Time
Tao (1967) developed charts for infinite slab, infinite cylinder and sphere to determine Freezing times.
The dimensionless Numbers shown on these charts are:
Dimensionless time tf* = tf kI (TF – Tm)/ a2 ℓi L
Inverse Biot No. 1/ NBi = kI / hc . A
Modified Steffan No. Nste * = CpI (TF – Tm )/ L
For each shape the curve is drawn between dimensionless time and Inverse Biot number for different values of modified Steffan Number. Obtaining dimensionless Freezing time tf* , the freezing time can be calculated.
L = Latent heat x % water in food, ℓi = Density of Ice
kI = Thermal conductivity of ice, a = least dimension
NBi = Biot Number, CpI = specific heat of Ice
TF = Initial Freezing Temperature
Tm = Cooling medium temperature

## Slide 5: Cleland and Earle Non Dimensional Equation
NFO = P [ 1/ NBi Nste ] + R [ 1/ Nste ] , where
NFO = Fourier No. α . t /a2 , where t = freezing time and
α = kI / ℓi CpI i.e. thermal diffusivity
NBi = Biot Number = hc . A / KI
Nste = Steffan Number = CpI (TF – Tm )/ L
By Introducing Plank Number, the influence of Sensible heat above the initial freezing point can be incorporated.
NFO = f (NBi , Nste , Npk)
Where, Npk = CpI (Ti – TF )/ L
The empirical expressions were investigated by Cleland and Earle for slab, cylindrical and spherical shapes separately.

## Slide 6: Nagaoka et. al. (1955) Equation
tf = ∆H’ ℓ / (TF – Tm )[P. a /hc + R a2 / KI], where
∆H’ = [1 + 0.00445 (Ti – TF) ] [Cpu ( Ti – TF) + L + CpI (TF – T)]
The modification by Nagaoka has incorporated factors to account for sensible heat above and below the initial freezing temperature.
It still assumes that all latent heat is removed at constant temperature TF (i.e. IFT).

## Slide 7: Numericals
Solve Numerical: compute the temperature at which ice formation begins in an ice cream mix (10 % Fat, 12% SNF, 15 % Sucrose, 0.22 % stabilizer). Assume 25 % of SNF including sugar is bound water)
Free water = 100- (10 + 12 + 15 +0.22) – 0.25 x (12 +15)= 56.03
Calculate mole fraction of free water xw = (56/ 18)/ [56/18+ 15/342 +4.5/342 +2x1.5/58.5]
ln xw = {∆H/ R} [ 1/ T0 – 1/ TF]
Calculate unknown value from this equation , where R is a gas constant i.e. 1.9872 cal/g. mol. K or 4.8 x 19872 = 8.314 KJ/kg mol. K and ∆H = 80 x 18 = 1440 cal /g mol = 80 x 18 x 4.81= KJ/kg .mol
IFT TF = about -3.77 °C

## Slide 8
THANK YOU