## Slide 1: PREPARATION OF ICE CREAM MIX
Dairy Technology
B.K.Singh,
Dairy Technology

## Slide 2: Ice CrEam
Ice cream is a complex product containing milk components like emulsified fat, protein in colloidal form and a solution of lactose and salts along with or without cane sugar, eggs, fruit juices, fruits, flavours, colours, stabilizers and emulsifiers.

## Slide 3: Preparation of ice cream mix
Preparation of ice cream mix involves various essential steps viz.
Selection of ingredients
Formulation of ice cream mix
Blending of mix
Pasteurization of mix
Homogenization of mix
Cooling of mix
Ageing of mix

## Slide 4: Selection of Ingredients
Selection of ingredients depends on their
Availability
Perishability
Convenience in handling
Effect on flavour,
body and texture of ice cream
Cost
Equipments available etc

## Slide 5: Dairy Ingredients
Dairy products that supply fat and MSNF – Sweet cream,
Sweet milk,
fresh butter,
unsweetened,
condensed and evaporated milks ,
full-cream milk powder,
separated milk powder.

## Slide 6: Non-Dairy Ingredients
Sweetening agents – Cane sugar, beet sugar, corn sugar, corn syrup, invert sugar,saccharin
Stabilizers– Gelatin, sodium alginate, guar gum, etc.
Emulsifiers– Mono or di-glycerides of fat forming fatty acids
Flavours– Vanilla, chocolate, strawberry, pineapple, lemon, banana, mango, orange, etc.
Colours– Yellow, green, pink, etc.
Egg solids – Yolk solids
Fruits & nuts – Apple, banana, mango, pine apple, grape, almond, pistachio, cashew nut, walnut and groundnut.

## Slide 7: Formulations of Mix
The fundamental requirement of mix formulation is to obtain a well balanced mix which also satisfies
The legal standards.
A correct total solids to water ratio
There is inverse relation between fat and SNF in ice cream mix
A correct fat to sugar ratio

## Slide 8: Formulations of Mix
The following methods can be used to calculate the mixes:
Pearson square method
Serum point method
Formula tables / graphics method
Algebraic method
Computer developed formulations

## Slide 9: Standardization of Ice Cream Mix
In order to attain the desired composition of ice cream mix, the calculated quantities of ingredients (dairy and non dairy) is obtained through standardization. This is accomplished using either (a) Algaebraic method, (b) Serum Point method
In algebraic method the following three equations are used:
Quantity equation(W+C+P=100-NDP)
Fat equation (W×F1+C×F2+P×F3=Desired fat % ×100)
SNF equation(W×SNF1+C×SNF2+P×SNF3=Desired SNF%×100)

## Slide 10: Standardization of Ice Cream Mix
W=Whole milk
C=Cream
P=SMP
NDP=Non Dairy Product

## Slide 11: Blending of Mix
The ingredients to be blended are taken in a vat, where it can be heated to facilitate dissolving, blending and pasteurizing. Mixing process varies from a small batch operation type to a large scale automatic continuous type depending upon the amount of mix to be processed.
Liquid ingredients
Dry ingredients.
Sodium alginate
Sugar
Butter, plastic cream, frozen cream or other frozen products(melted form)

## Slide 12: Homogenizing Mix
Homogenization of ice cream mix is a most essential step to make a permanent and uniform suspension of the fat by reducing the size of the fat droplets to a very small diameter, preferably not more than 2 µm.
never allow the fat to form the cream layer
More uniform ice cream
Smoother texture
Improved whipping ability
Shorter ageing period
Less opportunity for churning to occur in freezer
Less stabilizer is required

## Slide 13: Homogenizing Mix
Homogenization of mix is usually done at temperature ranging from 63 to77°C. A pressure of 2000 to 2500 psi (135 to 170 kg/cm 2 ) with one valve or 2500 to 3000 psi (170 to 200 kg/cm 2 ) on the first and 500 psi(35 kg/cm 2 ) on the second stage will usually give good results for an average mix.

## Slide 14: Pasteurization of Mix
Pasteurization is done to destroy all the pathogenic bacteria in the mix so as to render the final product safe for human consumption
Advantages of pasteurization are:-
Renders the mix completely free of pathogenic bacteria.
Dissolves and helps to blend the ingredients of the mix.
Improves flavour.
Improves keeping quality.
Produces a more uniform product

## Slide 15: Cooling of Mix
Mix should be rapidly cooled to a temperature below 4°C using a plate heat exchanger. Unless the mix is cooled to a temperature of 4°C or lower, it will become very viscous and the ice cream will not melt down smoothly. Also, temperatures below 5°C retard the growth of bacteria.

## Slide 16: Ageing of Mix
Cooled mix is left to age preferably for a period of 24 h at 4°C.
Changes that occurs during ageing are
Hydration of milk proteins
Crystallization of fats
Absorption of water by any added hydrocolloids
Viscosity is increased largely due to the previously mentioned changes.
Ageing is substantially completed within 24 h and longer period should be avoided to control spoilage by psychrotrophs.

## Slide 17: Flavour Addition
Among the flavouring substances that play an important part in frozen desserts are vanilla, chocolate, strawberry, pineapple, lemon, banana, mango, orange etc. Type and intensity of flavours are important characteristics in ice cream where delicate flavours are preferred to harsh flavours.
Examples:-
Vanilla
True Vanilla Extract, Concentrated vanilla Extract, True vanilla powder, Vanilla paste
Chocolate and Cocoa
Chocolate liquor,Cocoa powder, chocolate blend etc.

## Slide 18: Colour Addition
Colours should correspond to the flavour.
Harmless
Edible
Legally Permitted