## Slide 1
BINITA RANI
ASSOCIATE PROFESSOR (DAIRY CHEMISTRY)
FACULTY OF DAIRY TECHNOLOGY
S.G.I.D.T., BVC CAMPUS,
P.O.- BVC, DIST.-PATNA-800014
FOOD CHEMISTRY DTC-321 Credit hours-3(2+1)
Reactions involved during
Deep frying of food

## Slide 2
Deep frying  food preparation  in home and in industry.
Food products  potato chips, meat, fish,  prepared by frying  into fat/oil heated to about 180 °C.
frying process  food article  sufficiently cooked  consumed.
Prolonged heating  high temperature  substantial changes  chemical and physical properties  fat or oil  affects the quality of fat/oil & quality of finished foods.
Short frying period  production of desirable flavour and aroma  organoleptic quality of product.
In continuous deep fat frying  large quantities of fat  absorbed by food  replenished by fresh frying oil  steady state condition wherein  it is unlikely that the oil deteriorates beyond a certain point.
In intermittent frying  fats remain hot for long periods  many heating and cooling cycles  more rapid destruction of fat  due to increase in hydroperoxides upon cooling  their decomposition  when fat is reheated.

## Slide 3
BEHAVIOUR OF FRYING OIL
Deep fat frying different classes of compounds :
1. Volatiles
Oxidative reactions lead to production of:
alcohols,
acids,
esters,
hydrocarbons,
Ketones,
lactones and
Saturated & unsaturated aldehydes,
Amounts of volatiles produced vary :
type of oil,
type of food and
extent of heat treatment

## Slide 4
2. Nonpolymeric polar compounds of moderate volatility
e.g. hydroxyl & epoxy acids produced  through oxidative pathways
3. Dimeric and polymeric acids and glycerides
Thermal and oxidative free radicals  polymerization  substantial increase in viscosity of the frying oil
4. Free fatty acids
Hydrolysis of triacylglycerol  in presence of heat and water.
These reactions  responsible  physical and chemical changes  frying oil
  Increase in foaming tendency and viscosity
  Changes in flavor and colour (dark)
  Decrease in surface tension and iodine value
  Changes in refractive indices

## Slide 5
Behaviour of food during frying
Water  food  hot oil  steam distillation effect  sweeping volatile oxidative products from oil.
Released moisture  agitates the oil  hastens hydrolysis.
Blanket of steam above the surface of oil tends to the amount of oxygen  oxidation
Volatiles develop in food itself and/or from interactions between food and oil.
Food absorbs varying amounts of oil – 5 to 40% e.g., potato chips  final fat content 35%
Food release its endogenous lipids  frying oil/fat e.g., fat from chicken
oxidative stability of new mixture  different from original frying oil/fat

## Slide 6
CHANGES IN FRYING MEDIUM
During deep fat frying :
Hydrolysis,
oxidation and
polymerization
Factors  proportions of breakdown components in vegetable oils :
Temperature Method of heat transfer
Presence of O2 Metals in contact with oil
Heating time Turnover
Frying capacity Nature of food being fried

## Slide 7
commonly observed chemical changes are:
OXIDATION AND DECOMPOSITION
Moisture, high temperature and atmospheric O2  favours the oxidation of frying medium.
oxygen introduced into the oil with food  oxidative changes.
peroxide content of food begins to increase after an initial induction period and finally decreases.
Major reactions during autoxidation  degradation reactions  formation of volatile compounds.
Autoxidation of PUFA  formation of conjugated hydroperoxides and peroxides  decompose  volatile acids, aldehydes, alcohols, ketones and hydrocarbons.

## Slide 8
THERMAL OXIDATION
In the presence of O2 when oil is heated at high temperature :
Formation of free fatty acids
Formation of hydroperoxides which may undergo :
1. Fission  form alcohol, aldehydes and acids  darkening of frying medium and flavour changes.
2. Dehydration  form ketones
3. Formation of free radicals  their combination to form dimers, trimers, epoxides, alcohols and hydrocarbons  increase viscosity of the oil.

## Slide 9
During deep frying  thermal and oxidative decomposition of oil  volatile and non-volatile products:
1. Volatile decomposition products:
Most of them (generated during frying)  removed by steam.
They (e.g. unsaturated lactones)  flavour
2. Non volatile decomposition products:
Formed  thermal oxidation and polymerization of unsaturated fatty acids (frying medium).
Include cyclic acids, fatty acids, polymeric triglycerides, and other oxidative products.
Accumulation of these products  changes:
increase in carbonyl value, FFA content, -OH content and saponification value and decrease in unsaturation  Iodine value.
Also increase in viscosity and refractive index.

## Slide 10
POLYMERIZATION
Oxidation and thermal alteration products  undergo polymerization  forming gums and residues.
Rks b/w FA of same/different triglycerides  cyclic and non-cyclic dimers and other polymeric compounds.
Thermal polymerization of PUFA  cyclic monomers, dimers, trimers and higher polymers.
Rate of polymerization with increase in unsaturation of TG and frying time.
This results  changes  darkening of colour, foaming, heat transfer rate, viscosity, molecular weight, and gum accumulation.
Polymerization  increased fat absorption by food  unpalatable and greasy.

## Slide 11
HYDROLYSIS :
Moisture from food during frying  hydrolysis of fat  increase in acidity  initial formation of FFAs, mono and diglycerides and glycerols.
Soaps of some fatty acids  formed  accelerate deterioration of frying medium.
Accumulation of alkaline material the interfacial tension b/w product and frying medium  decreases the food quality.
Liberation of FFAs  decrease in smoke point of oil.
Colour , iodine value and viscosity of hydrogenated oils  changes more rapidly at FFA levels of ~1.5%.