## Slide 1: Water Management and Economics in Dairy Industry
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Reasons of Water Use Economization
Increasing water costs
High water consumption is making effluent critical in some cases
Future regulations may require water conservation
Increased costs for waste water treatment and disposal for excessive wastewater generated due to indiscriminate use of water
High energy requirement and maintenance cost of Pumps
Higher Electrical KWH consumption and higher electrical bill

## Slide 3: Important Pillars of water conservation and increasing water use efficiency
Think of water as a raw material with a cost.
Make water conservation a management priority.
Set specific water conservation goals for your plant.
Reuse water where possible. Train employees how to use water efficiently.
Establish a recognition and reward program for employees and teams who do an outstanding job.
Higher costs of water and effluent disposal that have now been imposed to reflect environmental costs,

## Slide 4: Cost Economics of Effluent Treatment Plant of a Dairy handling 800 cu. m. per day
Segregating low BOD streams from High BOD streams.
  Cooling water from homogenizer, compressor, milk packaging machine, crate washer, cold storage etc. are low BOD streams.
Use of Anaerobic cum aerobic treatment plants
  For Product manufacturing plant of high BOD values, the effluent treatment plant based on USAB (Upflow Anaerobic Sludge blanket) technology followed by Aerobic treatment i.e. combination of offers huge savings.
  Such units not only reduce electrical consumption but also offer useful bio-gas. Treatment cost reduced because 80% BOD reduction takes place in anaerobic digester, which requires only 25% power consumption as compared to aerobic plant.
  Considering Effluent generation as 2.5 litre per litre of milk resulted milk handling capacity as 800 x1000 /2.5 = 3,20,000 litres per day when water consumption is regarded as 4.0 litre per litre of milk i.e. 4x 3,20,000=12, 80,000 litres per day=1280 cu.m. per day costing Rs. 1280 x 40 = Rs. 51,200 per day.

## Slide 5: Economic of ETP …contd.
Use of Concept of tertiary treatment facilities for treated water
  It comprise of activated carbon filters, chlorination arrangement, Ultr-violet (UV) treatment, water softner etc. to get water with cleanable, sanitizable and potable quality to meet the acute shortage of water with recycling and reuse.
Annual Power Consumption and Monetary savings
  Aerobic: 2, Anaerobic cum Aerobic:0.5 and saving:1.5 units/ cu. m. effluent
  Annual Power savings: 1.5x800x365 = 4.38 Lac Units
  Annual Monetary savings: Rs. 4.38 x 5.00 x 21.90 Lac per annum

## Slide 6: Economic of ETP …contd.
  Annual Savings from Bio-gas
    30 cu.m. bio-gas per day is produced and used to generate 50 Units per hour in a Dual Fuel Biogas Generator
    Savings per day : Rs. 50 x 12 x 5= Rs. 3000 per day
    Annual savings from bio-gas : Rs. 9.0 lacs per annum
    Annual Savings from tertiary treatment of treated water
      Approx. 300 cu.m. treated water is recycled after tertiary treatment
      Annual savings : Rs. 300x 40 x 365 = Rs. 43.80 lacs per annum

## Slide 7: Economic of ETP …contd.
Total Annual savings from waste water
  Rs. 21.90 + 9.0 + 43.80 = Rs. 74.70 Lac per annum
  Savings from Effective water consumption
    should be reduced from 4 to less than1 litre per litre of milk for further decreasing the water consumption cost and reducing the effluent treatment cost.
    Annual savings from reduction in water consumption from 4 to 1 litre per litre per litre of milk: Rs. 51, 200/4 = Rs. 12,800 per day
    Annual savings from reducing water consumption: Rs. 12,800 x 365 = Rs. 46.72 lacs per annum
    Total Savings from water management in approx. 3 lac l/day plant
      Rs. 74.70 + 46.72 = Rs. 121.42 lacs per annum approx.

## Slide 8: Identification of savings for water
Aggressively challenged to conserve water necessitating the need for not only reducing water consumption but also to employ measures for recovery and recycling of process water without compromising on the hygienic quality and safety of the products.
Measurement of water utilization and identification of savings. Installation of water meters across the different sites. Waste water calculation i.e. 2,5 to 3.0 litres per litr of milk processed and treatement plants to select and operate appropriately.
Recovery of steam condensate from evaporators to use condensate as boiler feed water, melting butter in a jacketed tank, preheating milk prior to entering evaporator, preheating drying air for spray dryers.
Preventing water overflow of cooling tower and overhead tanks
Re-circulating homogenizer water, crate wash water; reducing water for cleaning; repairing leaks; and reviewing truck washing practices for savingsReuse of Permeate from Reverse Osmosis plant of milk by disinfecting to use as potable water, CIP pre and intermediate rinsing instead of potable water use, cleaning of floors and walls of the building, external cleaning of milk transport vehicles and use as pump seal water.

## Slide 9: Managing the water scarcity
Installation of a nanofiltration regeneration unit to continuously regenerate caustic CIP solution thereby only draining the retentate of the nanofiltration.
The consumption of chemicals for the caustic CIP system and use of hot water will be reduced for annual net savings.
It is not advisable to drain the spent caustic solutions to reduce the load on Effluent treatment plant with the view of economic reasons.
In the past, abundant and inexpensive sources of water were taken for granted in the dairy processing industry and not much thought was given to economize its use.
Besides, indiscriminate use of water also results in excessive wastewater generation, which becomes a burden for the dairy in terms of treatment and disposal costs.

## Slide 10: AREAS OF WATER LOSS
RMRD:
Manual cleaning of cans with running water hoses
Water lubrication of conveyors
Process Section:
Operating pasteurizers for short durations
Condensate from pasteurizers allowed to drain
Water being allowed to overflow the balance tank when pasteurizers and other equipment are on rinse
Manual cleaning of separator with running water hoses
Cleaning of milk tanks by high pressure discharge points

## Slide 11: Areas of Water Losses and strategies to reduce consumption
Milk Filling Section
Manual cleaning of crates with running water hoses
Machine cooling water drained
Butter and Ghee Section
Draining of cooling water sprayed over butter churns
Draining of condensate from ghee boilers
Draining of cooling water from settling tanks
Evaporating and Drying Sections
Draining of condensate from evaporator
Operating evaporators for short durations and frequent cleaning
CIP Systems
CIP done without recirculation, or used CIP solutions being drained frequently
CIP systems not recovering final rinse water for reuse as pre-rinse water

## Slide 12: Areas of Water Losses
Refrigeration Sections
Draining of chilled water or leakages in chilled water system
Evaporation losses in atmospheric condensers
Other general areas
Inadvertent use of water at wash points
Frequent and excessive floor cleaning by high pressure discharge points
Draining of pump seal water

## Slide 13: Strategies to reduce water Consumption
Water wastage control in Manual cleaning:
Review cleaning practices, adopt dry cleaning, where possible
Use high pressure low volume cleaners for cleaning surfaces
Use automatic shut-off nozzles on all water hoses.
Pre-soak floors and equipment to loosen dirt before final clean
Avoid using water hoses as brooms.
Prevent spills of ingredients and of raw and finished product.
Always clean up spills before washing.
CIP systems
Reuse CIP solutions appropriately
Reuse final rinse water as pre-rinse for next CIP cycle.
Review regularly timers and settings for efficient CIP operations

## Slide 14: Strategies to reduce water Consumption
Processing:
Optimize process schedules e.g. prevent pasteurizers ‘circulating on water’, as water circulation often result in wastages due to overflows
Recirculate homogenizer and pump sealing water
Use continuous rather than batch processes to reduce the frequency of cleaning
Auxiliary use:
Operate boilers efficiently
Collect condensate for reuse
Cooling towers:
Maintain cooling towers in proper working condition
Remove scales
Prevent excess water loss from drift.

## Slide 15: Strategies to reduce water Consumption
Miscellaneous:
Install water meters and read them each shift
Prevent all water and steam leakages
The above details are not exhaustive, but provide a
brief insight of common focal points.
WATER REUSE
Besides preventing loss of water, optimization of water use in a dairy plant by water reuse, as appropriate, for specific applications. To reduce the demand on water supply and also reduce volumes of wastewater, the treatment and disposal of which is expensive.

## Slide 16: Reuse Water
Recirculated water: Water reused in a closed loop for the same processing operation (e.g. chilled water, condenser cooling water in circulation, pasteurizer cooling water in circulation etc.)
Reclaimed water: Water that was originally a constituent of food, has been removed from the food by a process step, and is intended to be subsequently reused in food processing operations (e.g. Condensates from milk evaporators).
Recycled water: Water, other than the first use or reclaimed water, that has been obtained from a food processing operation (e.g. permeate from reverse osmosis plant, CIP final rinse water etc.)

## Slide 17: Requirements for hygienic reuse of process water
Safe for its intended use and the safety of the product should not be lost through the introduction of chemical, microbiological or physical contaminants in amounts that represent a health risk to consumer.
Reuse water shall at least meet the microbiological and chemical specifications for potable water. In certain cases physical specifications may be appropriate.
Reuse water should not adversely affect the quality and suitability of the product.
Reuse water shall be subjected to ongoing monitoring and testing to ensure safety and quality.
Unless reconditioned to potable water quality, distribution of reuse water should be in clearly marked (e.g. different colours) systems, including piping and outlets
Proper maintenance of water reconditioning system is critical to avoid having the systems become source of contamination.

## Slide 18: Selection of optimum waste water treatment plants
Reconditioning of water should be undertaken with the knowledge of the types of contaminants the water may have acquired from its previous use. E.g. UV disinfection may have limited effectiveness for inactivating protozoan cysts, helminths or viruses. Similarly, the use of chlorine or ozone on organically enriched water may result in the formation of hazardous organic compounds.
The water treatment system(s) chosen should be such that it will provide the level of reconditioning appropriate for the intended water reuse. E.g. UV disinfection as the sole treatment is not appropriate for water that is turbid or contains particulates because the organisms in the shadow of particles or entrained within particles are protected from lethal effects of the irradiation.
Extremely large volumes of reuse water may justify the use of an advanced wastewater treatment system.

## Slide 19
THANK YOU