## Slide 1: Skin and Hides
(A part of Unit III- 3rd Prof. Year)
Dr. Gargi Mahapatra
Asst. Prof. cum Jnr. Sc.
Dept. of Livestock Products Technology
Bihar Veterinary College
BASU, Patna.

## Slide 2: Hide vs. Skin (one of the most important by-products)
Hide
Skin of Large Animal
Large, Thick and Heavy
Wt. > 30 lbs/ 13.62 kg
Av. yield 7.0% of live wt.
Skin
Skin of Small Animal or very young calf
Small, Thinner and Tighter
Wt. < 20lbs/9.1 kg
Av. Yield 11.0% of live wt.

## Slide 3: Source
Hide
Slaughtered animals
20-25 %
Fallen Animals
75-80%
* Fallen animals: Death due to natural
Skin
Slaughtered animals
80 %
Fallen Animals
20%
cause

## Slide 4: Destination of Hide/ Skin
Hide/Skin
Drying/ Curing
Conditioning
Tanning
Post-Tanning Operations
Leather
(End Product)

## Slide 5: Leather
Excellent tensile strength and flexibility
High resistance to puncture and tear
Insulation from weather
Good molding tendency hence versatile usage.

## Slide 6: Cross-section of Hide/Skin
Epidermis- Outer pigmented zone
Dermis- a.k.a Corium, (elastin fibres+ reticular fibres+ collagen fibres)
Subcutis- Loose membrane network of fatty deposits.
*Inner portion of corium is interwoven with
bundles of collagen which makes up into leather.

## Slide 7: Flaying
Process of skin removal from dead animal
Performed by skilled workers
Sharp flaying knives used.
Practiced on Pritch Plates :- Steel plates 120cms long, 60cms wide and 20 cms thick.
Animal secured on pritch plates by Pritch Bars: A metal rod.
Sometimes practiced on skining cradles, made from round steel/timber tublings.
https://www.youtube.com/watch?v=9y03R9WVnGY

## Slide 8: Flaying of Large Animals
Hide opened from neck (ventral side)
Incision continued from middle of dewlap to belly up to the middle of tail
Cut created at knee joint and hock joint
Fore leg incision continued to breast bone
Hind leg incision continued to scrotum/udder
Hide separated from carcass from breast to neck and from breast to navel

## Slide 9: Contd…
Incisions are moved towards the medial end of the carcass
The carcass is hung by hooks on its hind legs
The hide is removed from the tail
Carcass is raised high, the hide is pulled back to the hump, then to the shoulders and finally to the neck, separating the thick subcutaneous tissues
Hide is severed from the carcass by giving a cut behind the horns

## Slide 10: Flaying of Fallen Animals
Difficult due to harder connective tissue.
Coagulated blood capillaries stain the hide
Leads to inferior quality stained leather
Practiced on Flaying Cradles: Two poles 150cms long and 15cms in diameter, separated by a gap of 30cms

## Slide 11: Flaying of Small Animals
Small incision in the hind leg on inner side of hock joints
Smooth and narrow wooden/steel rod (45cms) inserted from the incision to loosen connective tisue between skin and body
Rod removed, hand cut made around incision hole
Air pumped in the cut, carcass inflates like a balloon

## Slide 12: Contd…
Carcass lifted from ground and hung on hind legs
Circular cut made around knee and hock joint and around neck to severe the head
Cuts made from the hock joint to scrotum, fingers inserted into the incision and the skin is pulled downwards, continued till worker reaches the chest
Worker grips the skin with both the hands and removes it with force, knife used where it is absolutely necessary
https://www.youtube.com/watch?v=lqqBU5T3Gas

## Slide 13: Classification of Hides and Skin
Acc. to weight
Name | Origin | Weight (lbs)
Slunk Skin | Unborn Calf | ---
Calf Skin | Immature Calf | 9-15
Kip Skin | Calf | 15-25
Heifer Skin | Heifer | 25-30
Cow Hide | Cow | >30
Light Cow Hide | Cow | <53
Heavy cow Hide | Cow | >53
Extreme Light Hide | Steer | 32-48
Light Steer Hide | Steer | 48-58
Heavy Steer Hide | Steer | > 58
Bull Hide | Bull | 60-100
Other factors
Name | Description
Texas/Colorado hide | Hides branded on butt.
Native hides | Unbranded Hides
Slaughtered Hides | Flaying of slaughtered animals
Fallen/ Rendered/ Murrian Hides | Flaying of Fallen animals
Big Packers Hide | Flaying by highly skilled workers
Small Packers Hide | Flaying by less skilled workers

## Slide 14: Goat Skin Classification
On the basis of weight and length
(Baba and Bhote, 1966)
Class | Wt. (kg) | Length (cms) | Region
Big Goat Skin | 1.3 | > 96.5 | Punjab, Kashmir, Odhisa , U.P.
Medium Goat skin | 0.91 | 76.2-96.4 | Rajasthan, Maharashtra, Andhra Pradesh, Kerela, Karnataka
Small Goat Skin | 0.86 | <76.2 | Eastern Part of India
FAO
(Aten, 1955)
Grades | Specification
First Grade | Shape/Pattern Regular and Symmetrical with minor scores/gouges
Second Grade | Good Shape and Pattern, 1/16 of area show concentrated scores/gouges
Third Grade | Irregular shape and Pattern; ½ of the area damaged by knife
Reject Grade | Irregular shape and Pattern; Extensive damage on back or butt

## Slide 15: Defects in Hide/Skin
Ante-mortem Defects
Poor substance- Genetic Factor/ Species variation
Defects due to Disease -Pox, Mange, Dermatitis etc.
Grain Damage -Thorns or wire fence scratches, branding, abscess abrasion, tick damage, bacterial action
Post -mortem Defects
Bad Shape/ Pattern -Ground drying, Fallen hides etc.
Bad Flaying -Knife Cut
Curing Defect -Salt burns, improper application of salt
Smoke damage -Excessive exposure to smoke.