## Slide 1: ANALYSIS OF CONTINUOUS CABINET DRYERS Food Engineering (DTE - 321)
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Mass balance and Energy Balance in Counter-current Continuous cabinet Dryers
  Air In ma 2 1 Air Out, ma
  Product Out, mp Product In, mp
Moisture Balance: Moisture In = Moisture out
ma H2 + mp w1 = ma H1 + mp w2
Where,
ma = Air flow rate (kg dry air / h), mp = Product flow rate (kg dry solids / h) , H = Absolute humidity (kg water / kg dry air) and w = Product moisture content (kg water / kg solid) Ta= Temperature of air ( ⁰ C) Tp = Temperature of product ( ⁰ C ) and 1 is inlet condition; and 2 is the outlet condition.
Energy balance : Energy In = Energy Out
ma Ha2 + mp Hp1 = ma Ha1 + mp Hp2 + Q
Where, Q = Heat losses from dehydration system, Ha = Heat content of air (kJ / kg dry air) and Hp = Heat content of product (kJ / kg dry solids).

## Slide 3: Enthalpy of Product determination
Considering 0 ⁰ C as the reference temperature the expressions for heat content of air and product are :
Ha = Cs (TA – T0)+ H (L0), where
Cs = 1.005 +1.88 H and L0 = 2500.5 at T0 = 0°C
Hp = Cps (Tp - T0 ) + w Cpw (Tp - T0 )
Where,
Cps – Specific heat of product solids (kJ /kg K)
Cpw – Specific heat of water (kJ /kg K),
Tp – Product temperature. T0 =0°C
Using these equations, the quality of air required for drying an established amount of product over known moisture content range can be determined. In addition, for known inlet conditions of air, the moisture characteristics of air at the system outlet can be established.

## Slide 4: Numerical on Continuous Dryer
A continuous dryer is being operated counter-currently to dry a product 0.2 kg water per kg dry solid to final moisture content of 0.05 kg water/kg kg dry solid. The feed rate is 500 kg dry solid/hr. The solid product enters the dryer at 20°C and products at 70°C. The heat capacity of drying solid is 2.0 KJ/kg °C. The drying air enters at 95° C with 0.005 kg water / kg dry air and moist air exits at 45° C. If the specific heat of the product is assumed as constant and there is no heat loss from dryer, calculate the air flow rate and the exit humidity ratio of air.
Solve It.

## Slide 5
THANK YOU