## Slide 1: Dressing of Food Animals

## Slide 2: Dressing of Food Animals
Methods of dressing of various food animals
Booth or Bed System
Line or On-the rail dressing

## Slide 3
In this system one or two persons do all the work in one place.
No individual is allotted with a specific work.
All the slaughter procedure is carried on floor.
Prevalent in most municipal and corporation abattoir in India.
Major disadvantages
- hygiene is poor,
- operation is congested.
1. Booth or Bed System

## Slide 4
Consists of conveying the carcass by gravity or power through overhead rail to various places after stunning and sticking.
Also known as one man-one job system.
Men will be at different places carcass
will reach them and they will attend to
their allotted work.
Manual labor saving devices such as brisket cutter, hock cutter, hide puller, etc., are used.
2. Line or On-the rail dressing

## Slide 5
In modern meat plant line method of slaughter is highly essential.
In this system there are four types.
Gravity rail system
In this method the carcass will be suspended from a spreader and single wheel trolley or runner, gravitated to each station and stopped by manually operated stop on the overhead rail.
The system is used for lower slaughter rates 10-40 cattle/hr.
Most compact and economical.
Less chance of breakdowns with consequent loss of production.
Adequate ceiling height is necessary because of the pitch of the rail to gravitate the carcass.

## Slide 6
2. Intermittent Powered System
In this system the carcass is suspended over a spreader(gambrel) and trolley, and moved mechanically on a level rails at an intervals by means of variable timing device.
Here Slaughter rate of 10-75 cattle/hr can be achieved.

## Slide 7
3. Continuous Power System
Here dressing line will be in continuous motion.
More sophisticated instruments are used in the slaughter line (mechanical hide puller, moving top inspection table etc.)
Carcass can be revolved to a full 3600.
The platform may be fixed or movable,
elevated or lowered.
Rate of slaughter – 40-120 cattle/hr.

## Slide 8
This is a continuous conveyorised method in which heavy Beef trolleys or runners suspend the carcass from overhead rail.
Here everything is done systematically (mechanized).
Rate of slaughter – 50-150 animals/hr.
Commonly used in modern meat plants.
Here from arrival of animals till completely dressed the work is divided into 32 divisions (each work is carried out by one man).
Developed and patented by the Canada Packers Ltd., Canada; hence called Canpak system.
4. Canpak System

## Slide 9: Canpak System

## Slide 10
Advantages of line system over booth system
Time is saved.
Safer for operatives.
Hygienic than booth system.
A comfortable operative position is provided to the operator.
Saving of space.
Increased output and enhanced value of carcass.
Possible Disadvantages
High standard of engineering maintenance is needed.
When break down occurs production ceases completely.
Trained personnel needed.
Meat inspection is sometimes more difficult and possibly less efficient.

## Slide 11
Whole procedure

## Slide 18
THANKS