## Slide 1: Drum Drying & Analysis
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Drum Drying
Thin film on the outside surface of rotating steam heated drum causes drying and rotation enhances the agitation and high heat transfer coefficients during drying. It is known as film drying or Roller Drying.
The residence time of heating and evaporation is from feed point to the point of doctor blade, which scraped the dried film from the drum. It took about three quarter of a complete rotation on the drum surface
Above the surface of film either atmospheric pressure or vacuum is maintained.
The ratio of steam consumption to water evaporation is from 1.2 to 1.6 : 1 in drum drying under atmospheric pressure
Scorched Flavour in Powder and lower solubility of about 85 % are the disadvantages due to high protein denaturation in drum drying under atmospheric pressure.

## Slide 3: Types of Drum Dryers
    Number of Drums: (a)Single drum, (b) double drum, or twin drum
    Pressure surrounding the film of feed: (a) Atmospheric (b) Vacuum
    Feeding Arrangements: (a) Nip Feed , (b) Splash Feed ( c ) Dip Feed, and (d) Roller Feed
    MOC : (a) Alloy Steel (b) Stainless steel and ( c) Chrome or Nickel plate steel

## Slide 4: Evaporation Rate and Drying Time
Rate of evaporation
dw/dt = U A ∆T/ ∆Hv
  ∆T = (ts – tb) Mean temperature difference between the roller surface (ts) and the product boiling temperature (tb) in °C
  ∆Hv = Latent heat of vaporization at tb i.e. boiling point of milk
  1/U = 1/hs + x/k +1/hp + 1/(hc + hr +he), where
  hs = Eqivalent film coefficient of steam, Kcal/h-m2 °C=4000
  X = Film Thickness, m
  K Thermal conductivity of metal, Kcal/h-m- °C
  hp = Equivalent film coefficient of product, Kcal/h-m2 °C
  hc =Convection Coefficient, Kcal/h-m2 °C = 5.0
  hr = Radiation coefficient, Kcal/ h-m2 -°C=7.5
  he = Evaporation film coefficient, Kcal/h-m2 °C= 250

## Slide 5: Factors Affecting the Capacity and Operation of Drum Dryer
The drying capacity varie from 5 to 50 kg of dry product per m2 and is affected by following factors:
Milk Feed temperature, concentration (desirable 18-25 % TS) and level of milk
Avoid uneven and broken sheet of drying materials on the drum
Drum gap in double drum dryer
Drum speed, Roller alignment
Steam pressure and temperature not too high and drum speed not too low
Condensate removal
High moisture of the product may be due to low temperature, thick film, high solid and high rpm of the drum.

## Slide 6: Factors Affecting the Capacity and Operation of Drum Dryer
Drums must be properly aligned and have identical characteristics of speed, heat transfer and wear etc. The spacing between drums is about 0.5 to 1.0 mm.
Knives must be reground regularly after every 100 hour for uniform sharpness
Drums must be kept smooth
Drums must be vented of air for better heat utilization
Condensate must be continuously duscharged from the drum
Accurate control of the feed device
Preheating of the milk is advantageous but the temperature must not exceed 71° C
Slightly acidic milk yields a powder of dark colour and poor flavour
The dried product must be scraped off after ¾ to 7/8 revolution of the drum so that solid contact to meta is less than 3 seconds to avoid the scorched flavour, burning and brown colour with poor quality

## Slide 7: Total Drying Time including diffusion controlled falling rate period
Total drying time in three stage of spray dying rates:
  Constant Rate Period
  First Falling rate period without diffusion controlled but capillary movement controlled
  Second Falling Rate Period with diffusion controlled period
Total Drying time t = tc + tf1 + tf2
  tc = HL (wo - wc )/ h A ( TA – Ts )
  tc = HL (wo - wc )/ (K/R) 4 πR2 ( TA – Ts )
  tf1 = wc / Nc ln (wc / w1)
  tf2 = R2 /π2 D ln [6/π2(w1 –we)/( w –we)]

## Slide 8: Drum Dryer

## Slide 9: Drum Dryer with Vapour Hood

## Slide 10: Vacuum Drum Dryers- Single and double Roller types

## Slide 11
THANK YOU