## Slide 1: Meat Science (JRF) Part 3
By Dr. Gargi Mahapatra
Asst. Prof. cum Jnr. Scientist
Bihar Veterinary College
B.A.S.U., Patna.

## Slide 2: Utilization of Glands
Glands should be excised from slaughtered animals with in
15-20 min.
Glands are chilled in metal containers in direct contact with ice but avoid contact with water as principal agent may wash away.
Clean glands quickly frozen to -20 to -18 °C.
Glands are packed individually and processed to acetone dried powder (A.D.P.), longer method of preservation
Organ Remove Con. Tissue/ Immerse in 4 vol. of chilled
Blood Vessel/Fat etc. Acetone for 3 hr.
Ground Mince Tissue
to fine treat with 3 vol. Cut into small pieces, 3 vol.
powder chilled acetone of chilled acetone, 2-3 hr.

## Slide 3: Glands & their Bio-chemicals
Pancreas
Mainly Insulin (ß cells) in addition Glucagon ( cells), trypsin, chymotripsin & amylase.
1 kg fresh bovine/pig pancreas yields 150 mg of crystalline insulin with activity 25 IU/mg of insulin.
Thyroid Gland
Acetone dried powder of this organ is used to extract Thyroxine using Barium Hydroxide.
Yeild of thyroxine 0.08%
Parathyroid Gland
Extraction of Parathormone.
Used in the prevention of tetany and increase the rate of calcium excreation.
Adrenal Glands
Outer cortex & Inner Medulla
Corticosteroids Adrenaline and
Nor-adrenaline hormone
Edision’s Dis.
(Hypo-coticosteroid Syn.) 0.2% Adrenaline
Fresh Wt. or
1.0% Dry wt.

## Slide 4: Stomach Rennet/Rennin Pepsin Unwashed Mucosal Abomasum of lining of hog milk fed calf stomach preserved in 1% H2SO4 or as A.D.P
Pituitary Gland
Anterior Lobe Posterior Lobe
Growth hormone Oxytocin
L.H. (Extracted in 2%
F.S.H. Acetic acid; Milk
A.C.T.H. ejection factor;
M.S.H. Uterine contraction)
Vasopressin
(Vasoconstrictor;
Anti-diuretic
Hormone)
Gall Bladder
1kg Bile- 6 Buffalo or 5 S/G gall bladder
Golden greenish colour,
pH 7.1 ; Sp. Grav- 1.025
Bile Powder - 6% Moist.

## Slide 5: Contd….
Ovaries: Mature ovaries with corpus luteum but no cysts.
Extraction of estrogen and progesterone.
Testes: Testosterone extracted.
Hyaluronidase enzyme (Bull/Ram Testes)
Lungs: Heparin extracted from lungs of cattle (commonly)
Liver: Liver extracts; Yield 15% of raw wt.
Indicative in case of anaemia.
*Crude insulin purified by crystallization using zinc salts or picric acid.
*Insulin recovered by insulin picrate by gel filtration.

## Slide 6: Hides/Skin Utilization
Hides Skin
Large Animal Small Animals / Young Calves
Yield- 7% of live wt. Yield- 11% of live wt.
Wt. > 30 lbs/ 13.62 kg Wt. < 20lbs/9.1 kg
Slaughtered Ani. 20-25 % Slaughtered Ani. 80%
Fallen Animals 75-80% Fallen Animals 20%
Skin of pig is known as rind.
Fresh hides/skin a.k.a. green hides/skin.
Flaying- Process of removal of skin.
Destination of hide- Leather or Gelatin

## Slide 7: Classification of Hides and Skin
Hides branded on butt - Texas/Colorado Hide
Unbranded Hides - Native Hides
Flaying of Slaughtered Animals - Slaughtered Hides
Flaying of Fallen Animals - Fallen/ Rendered/ Murrian Hides
Flaying by highly skilled workers - Big Packers Hide
Flaying by less skilled workers - Small Packers Hide
Unborn Calf- Slunk Skin
Immature Calf - Calf Skin - 9-15 lbs. wt.
Calf – Kip Skin - 15-25 lbs. wt.
Heifer- Heifer Skin - 25-30 lbs. wt.

## Slide 8: Contd…
Light Cow Hide (30-53 lbs.)
Cow Cow Hide (>30lbs.)
Heavy Cow Hide (>53 lbs.)
Extreme Light Hide (32-48 lbs.)
Steer Light Steer Hide (48-58 lbs.)
Heavy Steer Hide (> 58 lbs.)
Bull Bull Hide (60-100 lbs.)

## Slide 9: Defects in Hide/Skin
Ante-mortem Defects
Post -mortem Defects
Poor substance- Genetic Factor/ Species variation
Defects due to Disease -Pox, Mange, Dermatitis etc.
Grain Damage -Thorns or wire fence scratches, branding, abscess abrasion, tick damage, bacterial action
Bad Shape/ Pattern -Ground drying, Fallen hides etc.
Bad Flaying -Knife Cut
Curing Defect -Salt burns, improper application of salt
Smoke damage -Excessive exposure to smoke.

## Slide 10: Processing of Hides
Hide/Skin
Drying/ Curing
Conditioning
Tanning
Post-Tanning Operations
Leather
(End/Final Product)

## Slide 11: Drying Techniques (7 days min.) Ground Drying Suspension Drying (Frame Drying, Line Drying & Tent Drying)
Conditioning of Hides
Washing and Soaking
Fleshing
Liming and De-hairing
Washing and De-liming
Batting ( vegetable tanning)
Pickling( chrome tanning)
Hide Curing
Done immediately after flaying
Techniques Dry Salting
Wet Salting

## Slide 12: Important Points
During dry salting hides kept flesh side up. 2-3 mm thick layer of fine salt applied. The weight of salt equal to weight of hide. These salted hides are then stacked on one another, to a max. height of stack 1m. Dry salting is practiced in rooms maintained at 15°C and 85-90% relative humidity.
During wet salting a curing solution prepared (23 kg salt+ 62 kg water for 100 kg of hides). The hides are soaked in pits, 1.25m deep. Soaking times varies from 2 days for fleshed hides to 2 weeks for un-fleshed hides. The Brining liquid maintained at room temperature. Such hides retain 35% moisture.

## Slide 13: Important Points
Hides are soaked in zinc chloride+ soda ash+ borax solution. All proteins of blood and lymph removed and it rehydrates and restores its shape.
During the liming process Hides soaked in saturated lime solution with 0.1% sodium sulphide. This is applied to loosen hair and epidermal cells.
Hides washed with mild acid to neutralize the lime.
During batting hides are treated with proteolytic enzymes at pH 8.5. Results in soft and pliable pelt. Such pelts tanned by vegetable tanning
During pickling pelts are pickled in bath of 1% Sulphuric acid and 10% salt in water, maintained at a pH of 2-2.5 for 2-3 hrs. Such pelts are tanned by chrome tanning process.

## Slide 14: Tanning (5-6 hrs)
Vegetable Tanning
Delimed pelts are immersed in natural tanning liquor of progressively stronger concentration. The tannin diffuses and imparts uniform colour
Used for heavy leather articles like belts, saddle, harness etc.
Tanning producing plants are
Avaran ( Cassia auriculata),
Babul (Acacia arabia),
Myrabalan (Terminalia chebula)
Konnan (Cassia fistula).
Chrome Tanning
A more modern, quicker and popular technique. Yields softer, stronger and supple leather.
Types
Single Bath Process- Chrome salts prepared in a solution and then applied on skin. The strength of the solution is then gradually increased
Double Bath Process- Chemical interaction forming the chrome solution is practiced on skin itself.

## Slide 15: **During double bath process sodium-bichromate is reacted with maltose and sulphuric acid to get chromic sulphates. Chromic sulphates are applied @ 1.5-2.0% at a pH of 2.5 , then increased to pH of 3.5.
Post tanning Operations
Setting out and Wiring- Hide passed between 2 large rollers. Removes excess tanning liquor and moisture
Splitting and Shaving- Practiced to adjust leather thickness
Dyeing- To produce desired color
Fat Liquoring- Lubrication with oil to adjust firmness.
Staking- Makes the leather more pliable.
Buffing- Smooth the grain surface of leather for better appearance. (Buffed Leather)
Glazing- Done in case of chrome tanning. Glass cylinders are rolled on the surface of the buffed leather. This process produces high luster on the grain surface

## Slide 16: Wool (Medulla is absent)
Outer layer- Cuticle/ Cuticular cells
Wool fibre
Inner layer- Cortex/ Corticullar cells
Basically it is protein called keratin, which is rich in sulphur.
Wool sweat- Yolk/ Suint- Water Soluble
Wool wax- Lanolin – Washed by detergents
Wool- Medulla absent
Hair – Medulla present
Kemp- Medulla irregularly present
Indian Breeds- Coarse wool- Carpet Quality- Annual yield 1-1.5 kg of greasy wool.
Indian wool- Canary colored- Bacterial action at high pH and low grease ( Ideal color- white/ creamy white).

## Slide 17: Contd…
Shearing- Twice a year (Spring & Autumn), 1st shearing at 8 months age.
Dagging- Shearing of soiled wool.
Lox- Wool contaminated with feaces and urine.
Animal washed 10-15 days before shearing.
Animal off-feed 10 hours before shearing.
Sampling size of fleece- 200 fibres are chosen randomly.
Fine wool <6cm in length; Coarse wool >10cm in length.
Impurities in wool: Max 20%
Vegetable content in wool known as Burr: Low burr (3%) Medium burr (5%) and High Burr content (>5%)
Burr is removed by acid treatment known as Carbonization.

## Slide 18: Contd…
Neck area- Coarse and broader wool
Shoulder area- Choice wool.
Flank area- Very good wool.
Leg area- Hair
Pole- Kempy
Belly area- Soiled poor quality kempy fibre- Skirting practiced to remove it.
Thigh area- Kempy
Back bone line- Poor quality fibre
1 inch below back bone line till flank- Good quality wool.

## Slide 19: Pulled Wool
Wool obtained from slaughtered animal
METHODS
Sweating- Controlled putrefaction of skin in damp chambers (20 °C x 48 hrs.); follicles loosen up and wool is pulled out.
Painting- Hair loosening agent (sodium sulphite) painted on pelt. Best technique.
Liming- Immersion of pelt into lime water.

## Slide 20: Important Points
Crimps- Number of waves in a fiber. Approx. 2-12/cm; the more the better.
Staple length- Length of fiber with crimps.
Fiber Length- Length of stretched fiber without crimps. It is measured in hanks which is 1/12 of an inch.
Fiber diameter measured in microns.
Medullation percentage is measured by Projection microscope, Lanometre or Dichlorobenzene.
Carpet wool has about 15% by count and 35% by wt. of medullated fibres.
Wool is hygroscopic in nature: can absorb water which is 18-50% of its own wt.
Wool can extend upto 70% of its original length before breaking.

## Slide 21: Important Points
Basal layer of epidermis crucial for wool development.
Wool follicles appear in the second month of gestation.
Primary follicles produce coarse wool whereas secondary follicles produce fine quality wool. The S:P ration dictates the fleece quality. Fine wool producing breeds S:P= 20:1 whereas coarse wool producing breeds S:P= 3:1 to 1:1.
Mohair- Obtained from Angoora Goat, No medulla.
Fur- A synonym of hair- Has medulla.
Wool: Specific gravity 1.304
Wool: refractive index 1.553- 5.00.
Detergent washing of greasy wool is known as scouring. This process removes wax.

## Slide 22: Bristles
Stiff hair of pigs, hog and boar. Area- Back, Neck & Tail.
Production- China > India > Russia
Live animals, bristles plucked. Superior lusture & resilience. Plucked twice a year.
Dead/ Slaughtered animal- Pulled or Shaved after scalding.
Colour- White bristles (only UP & Punjab); Black/ Darjeeling bristles (Darjeeling/ W.B.) and Grey bristles. White bristles more expensive than dark bristles.
Wild boars- bristles of better length.
Length of bristles: 44-159 mm (India 57-159 mm). Bristles over 121 mm length fetch good price.
Short bristles < 44mm known as rifflings.

## Slide 23: Bristles contd..
Thickness of bristles increases with length. Based on thickness bristles categorized to extra stiff bristles, stiff bristles and soft bristles.
Dragging- Process of sorting bristles into grades of specific length.
Bristles stacked butt side up. Each size tied up into 100 gm bundle of 2 inch diameter
Kanpur is the biggest dressing center for bristles.
Bristles sterilized by autoclave at 25-40 lbs X 1.5 hrs. The wet bristles are then dried in hot air oven at 60 °C.
Bristles quality, 19 grades and 11 Schedules based on
Bristle Grading and Marketing Rules -1969 &
Bristle Grading and Marketing Rules (Amendment) -1973

## Slide 24: Organic Wastes
Biogas- Anaerobic fermentation of feaces, urine and slaughter house waste products. Contains 60% CH4, 30% CO2 and traces of H, CO etc. (Impure CH4- 93% air and 7% CH4)
Compost- Aerobic fermentation of feaces, urine and slaughter house waste products. Made in 90 days. Used as manure for soil.
Paunch- Liquid and solid fractions separated by pressing. Liquid fraction concentrated to be used in pig feed whereas fibrous fraction used as fuel.
Paunch Production- 27 kg Cattle; 2.7 kg Sheep and 1.7 kg lamb.

## Slide 25: Thank you