## Slide 1: NUMERICALS ON EVAPORATOR AND DRYING Dairy Process Engineering (DTE - 212)
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Numericals on Single Effect Evaporators
100 kg of liquid food at 45° C is to be concentrated from 10 % TS to 20% TS in a single effect evaporator by boiling at 50°C. The latent heat of vapourization at 50°C is 2260 Kj/kg and specific heat of liquid food is 4.2 KJ/Kg °C. calculate the amount of heat energy required.
Solution: Total Mass balance : F = V + P
100 = V + P
Total Solid balance : F xf = P xp
100 x 0.1 = P x 0.2
P = 50 Kg and V = 100 – 50 = 50 kg
Amount of heat energy required: Q = F Cp (T2 –T1) + V L
= 100x4.2x (50 -45) +50x2260
= 115100 KJ
              :

## Slide 3: Numericals on Triple Effect Evaporator
In a triple effect evaporator, the steam temperature in first effect is 108°C and boiling point of liquid in the last effect is 52°C. The overall heat transfer coefficients are 2500, 2000, and 1000 kcal/ h m2 °C in first, second and third effects respectively. Determine the boiling point of liquid in first and second effect.
Solution: Total temperature drop ∆T = 108 -52 = 56 °C, and let Tb1 , Tb2 and Tb3 (i.e. 52°C) are boiling temperatures in three effects.
Assume q1 = q2 = q3 and A1 = A2 = A3
U1A1 ∆T 1 = U2A2 ∆T 2 = U3A3 ∆T 3
∆T 2 = ∆T 1 U1 / U2 = ∆T 1 x 2500/ 2000 = 1.25 ∆T 1
∆T 3 = ∆T 1 U1 / U3 = ∆T 1 x 2500/ 1000 = 2.5 ∆T 1
∆T = ∆T 1 + ∆T 2 + ∆T 3
56 = ∆T 1 + 1.25 ∆T 1 + 2.5 ∆T 1 = 4.75 ∆T 1
∆T 1 = 11.8 °C Therefore, Ts – Tb1 = 11.8 i.e. 108- Tb1=11.8 and
Tb1 = 96.2°C and ∆T 2 = Tb1 - Tb2 i.e. 1.25 x 11.8 =96.2 - Tb2
Tb2 = 81.5°C.

## Slide 4: Numerical on Drying
Calculate the time required to dry a food material from 80% m.c. (w.b.) to 20% m.c. (w.b.) in a tray dryer with a loading rate of 10 kg/m2. The food is dried from one side only. The critical m.c. of food is 45% (w.b.). The convective heat transfer coefficient is 6.31 W/m2. °C. The dry bulb temperature and wet bulb temperature of air are 60°C and 30 °C respectively. The velocity of air is 10 m/s and density of air is 1 kg/m3. The latent heat of vapourization at 30°C is 2430 KJ/Kg.
Solve it: Formula mw/A = h (TA – Tw)/ HL
Nc = mw/A / Solid load per m2
And Drying Time = wo –wc/Nc + wc/Nc ln wc/w

## Slide 5: Numericals to be solved
The constant drying rate for a material is 0.15 kg water/ kg dry matter. Min and has water activity of one at moisture content greater than 1.10 kg water/kg dry matter. Calculate the total drying time for the product to dry from an initial m.c. of 75^ (wb) to a final m.c. of 8 % (wb).
A 40 kg syrup contains 20 wt% sucrose. Citric acid is added into the syrup such that its concentration in the resultant syrup is 3 wt%. Calculate the amount of citric acid added to the syrup. (Answer: 1.24 kg)
A single effect long tube evaporator has ten tubes each of 2.5 cm diameter and 6 m length. It concentrates pineapple juice from 18° Brix to 23° Brix. The feed rate into the evaporator is 557 kg/hour at the boiling point of 70°C (L = 2333.82 KJ/kg). Neglecting boiling point rise, calculate the overall heat transfer coefficient in Watt/m2 K for 12 °C temperature gradient across the tube walls. (Area = nπdl). (Answer = 1387.16 )

## Slide 6
THANK YOU