## Slide 1: Product and Process Control Dairy Plant Management (DTT – 421)
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Different between Process Control & Product Control
S.No. | Process Control | Product Control
1. | Process control is applied during Production process. | Product control is applied after production process.
2. | Process control is of two types: Online quality control and offline quality control | Product control is no types.
3. | Process control is an integral part of manufacturing | Product control focus on sorting and isolating defective products
4. | Process control is to reduce waste, minimize costs and reduce the environmental impact | In product control efforts are made to segregate and sort defective products and give signals for improving quality in process of manufacturing.
5. | In process control the end products may be or may not be fulfilling the desired quality and costs | In product control, the end product of product control should fulfill the desired quality, count and property.
6. | Process control used to reduce the breakages and leakages. | Product control used to fulfill the desired quality after production
7. | Controlling of process sequence or steps is known as process control to produce products of desired quality, costs and desired environmental impact | Controlling the segregation of defective items in the produced lots of products using control methods is product control

## Slide 3: Process and Product Controls
Process Control
The main objective in any production process is to control and maintain a satisfactory quality level of the manufactured product. This is done by ‘Process Control’. In Process Control the proportion of defective items in the production process is to be minimized and it is achieved through the technique of control charts.
Product Control
Product Control means that controlling the quality of the product by critical examination through sampling inspection plans. Product Control aims at a certain quality level to be guaranteed to the customers. It attempts to ensure that the product sold does not contain a large number of defective items. Thus it is concerned with classification of raw materials, semi-finished goods or finished goods into acceptable or rejectable products.

## Slide 4: Control Charts for Variables
These charts may be applied to any quality characteristic that can be measured quantitatively. A quality characteristic which can be expressed in terms of a numerical value is called as a variable. Many quality characteristics such as dimensions like length, width, temperature, tensile strength etc… of a product are measurable and are expressed in a specific unit of measurements.
The variables are of continuous type and are regarded to follow normal probability law. For quality control of such data, there are two types of control charts used. They are as follows :
(i) Charts for Mean ( x bar )
(ii) Charts for Range (R)

## Slide 5: Statistical Quality Control (SQC)
Control Charts
In an industry, there are two kinds of problems to be faced, namely
To check whether the process is conforming to its standard level.
To improve the standard level and reduce the variability.
Shewhart’s control charts provide an answer to both. It is a simple technique used for detecting patterns of variations in the data. Control charts are simple to construct and easy to interpret. A typical control charts consists of the following three lines.
Centre Line (CL) indicates the desired standard level of the process.
Upper Control Limit (UCL) indicates the upper limit of tolerance.
Lower Control Limit (LCL) indicates the lower limit of tolerance.
If the data points fall within the control limits, then we can say that the process is in control, instead if one or more data points fall outside the control limits, then we can say that the process is out of control.

## Slide 6: Control Chart
The following lines with the data points plotted and diagram shows all the three controls. As all the points falls within the control limits, we can say that the process is in control.

## Slide 7
THANK YOU