## Slide 1: Tray Drying Analysis
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Theoretical Analysis of Packed bed surface Tray Drying
For evaporation from a tray with packed bed of moist material, assuming no change in the bulk volume
  Consider thickness of the bed in Tray Dryer = y meter
  Bulk Density of the dry material = ℓs kg/m3
  Latent heat of vapourization = L KJ/kg
  h = Total heat transfer coefficient in Watt / m2 °C
  dw/dt = Rate of evaporation
  Ta = Hot air temperature, °C
  Tw = Wet product surface temperature, °C
  Rate of Evaporation
    dw/dt = h (Ta - Tw ) / y ℓs L x103

## Slide 3: Through Circulation Type Tray Dryer
  For a through – circulation Type of Tray Drying, the air passed through pores from though circulation type bed.
    Cosider ‘a’ as heat transfer area in m2 / m3 of porous bed
    Consider ‘e’ as void ratio of the bed and ‘d’ as the diameter of spherical particles of wet food to be dried.
    The a = 6 (1 – e) /d for a packed bed of spherical shape of diameter ‘d’
    dw/dt = h a (Ta - Tw ) / ℓs L x103
  If the porous bed is of cylindrical shaped particles of diameter ‘d’c and length ‘l’, the area ac can be determined as:
    ac = 4 (1 – e) (l + 0.5 dc)/dc
    Where ‘e’ = void ratio = volume of voids divided by volume of solids
    ii. dw/dt = h ac (Ta - Tw ) / ℓs L x103
    Where L = Latent heat of vapourization in KJ/Kg, ℓs =Bulk density, kg/m3

## Slide 4: Constant rate drying time in terms of Latent heat of vapourization at wet bulb temperature of surface
Let HL = Latent heat of vapourization at wet bulb temperature of surface, in J /kg moisture
Equating Rate of mass transfer rate (Nc = dw/dt) with rate of convection heat transfer (Q) we have :
Q = Nc HL = h (Ta - Tw ) / y ℓs Joule/second
Nc = h ( Ta – Ts ) /HL . y ℓs
As tc = (wo - wc )/ Nc
Therefore, tc = y ℓs HL (wo - wc )/ h ( Ta – Ts )
Therefore, Constant rate Drying Time tc given by two equations:
    tc = 0.622 R TA (wo – wc)/ km A Mw P (ws - wa ), and
tc = y ℓs HL (wo - wc )/ h ( TA – Ts )
h = K/ R and A = 4 π R2 , where K = thermal conductivity of droplet surface

## Slide 5: Drying Time in single Falling Rate Period of drying from CMC to EMC
Consider the falling rate drying curve follow the straight line equation as follows:
  NF = a w + b
  d NF = a. dw + 0 = a . dw
  dw = d NF /a
  If NF = - dw /dt
  ∫ dt = - ∫ dw/ NF = - 1/a ∫ d NF / NF
  Keeping limit of drying time from 0 to tF when Drying rate varies from Nc to NF
  Therefore, tF = - 1/a ln (NF / Nc ) = + 1/a ln ( Nc / NF), where
  a = d NF / dw = (Nc - NF ) / (wc – w) = Nc / wc , when NF =0 at w = 0
As NF = a w and Nc = a wc, because intercept b =0 at x axis and we can write Nc / NF = wc /w
Therefore, tF = wc / Nc ln (wc / w)
Therefore Total drying time t = tc + tF in two stage of drying
t = (wo – wc)/ Nc + wc / Nc ln (wc / w)

## Slide 6: Drying Time during Diffusion controlled falling rate Period
Moisture diffusion inside a solid expressed by Fick’s law
∂w/ ∂t = D [∂2w/ ∂r2 + j/r ∂w/ ∂r]
  D = Diffusion coefficient
  j = 0 for an infinite slab geometry
  j = 1 for an infinite cylinder
  j = 2 for a sphere
Considering the droplet as spherical geometry, the solution under following boundary condition is
  At centre, ∂w/ ∂r = 0, r =o and t ≥ 0
  At EMC of drying, W = we , r = R and t > 0
  At initial stage from CMC, W = wc , 0 ≤ r ≤ R and t = 0
(wc- w)/(wc-we) = 1- 6/π2 exp [-Dn2π2t/R2]
tF = R2 /π2 D ln [6/π2(wc –we) /w –we)], if n= 1(neglecting other terms of series)

## Slide 7: Total Drying Time including diffusion controlled falling rate period
Total drying time in three stage of spray dying rates:
  Constant Rate Period
  First Falling rate period without diffusion controlled but capillary movement controlled
  Second Falling Rate Period with diffusion controlled period
Total Drying time t = tc + tf1 + tf2
  tc = HL (wo - wc )/ h A ( TA – Ts )
  tc = HL (wo - wc )/ (K/R) 4 πR2 ( TA – Ts )
  tf1 = wc / Nc ln (wc / w1)
  tf2 = R2 /π2 D ln [6/π2(w1 –we)/( w –we)]

## Slide 8: Tray Dryer

## Slide 9: Tray Dryer with heater, exhaust and Panel

## Slide 10
THANK YOU