## Slide 1: Thermal Efficiency and Controls in Spray Dryers
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Drying Efficiency
The thermal efficiency of operation of dryer is the ratio of theoretical heat required to the actual heat used in heating the air in spray dryer.
If R = Radiation loss, % of total temperature drop in dryer,
T0 = Atmospheric air temperature, °C
T1 = Temperatur to which air is heated, °C
T2 = Temperature of air leaving the spray dryer, °C
Thermal Efficiency = [(1 – R/100) (T1 - T2 )]/(T1 - T0 )
The overall thermal efficiency of a spray dryer is 50 – 60 per cent.
The heat requirement to evaporate 1 kg water in spray dryer are 1200, 980 and 850 Kcal/kg in sinle, double and three stage dryers respectively.

## Slide 3: Factors Affecting the thermal efficiency of spray dryer
    Increasing the feed temperature reduces the viscosity and also reduces the heat required to produce a unit weight of dried product.
    Higher Inlet air temperature can be used to reduce fuel consumption i.e. Kcal per kg of powder produced.
    Higher the temperature difference means lower the heat requirement to produce a unit weight of product of constant residual moisture content from a constant solids feed. It can be achieved with either increasing inlet air temperature or decreasing outlet air temperature.
    Low Outlet Air temperature leads to higher moisture in the product as it leaves the dryer and hence two stage drying is required, which improves the quality and efficiency but with additional fixed cost.

## Slide 4: Factors Affecting the thermal efficiency of spray dryer
    High efficiency of heat exchanger for air heating also improves thermal efficiency.
    The drying capacity of the dryer is increased by 5 %, when the concentrate is fed to the atomiser at 70°C instead of 50°C. The average size of atomized particle is reduced and lowers the outlet air temperature and improves the solubility of powder.
    Use of Outgoing Exhaust air or effect of recycling of exhaust air (10-50%) to preheat supply air to dryer recovers some of the waste heat of exhaust air but it should be partial to avoid the increase of humidity of inlet air. Reducing heat losses and air leakage from dryer body also improves efficiency.

## Slide 5: Factors Affecting the thermal efficiency of spray dryer
    Heat input is proportional to the evaporation rate. Higher the solids content means low evaporation rate and thereby lower heat input.
    Increase in solids content from 10 to 25 % for a given production rate results in reduction of 66.6 % heat input. Skim milk and whole milk are concentrated to 48-50 % solids and whey to 55-60 % solids to increase efficiency. Beyond this would have adverse effect on quality of powder.
    The two stage drying has higher thermal efficiency with the principle of reducing the outlet air temperature with the moisture content of powder as 6-7 % leaving the main dryer and from 3-4 % when leaving the secondary dryer. The secondary dryer uses the heated fresh room air with higher drying capacity and less air requirement comparatively. Thus unit is operated with less air than if all the drying is done in the main drying chamber.

## Slide 6: Controls in spray Dryers
Objective is to produce a powder of high uniform quality i.e. desired moisture content, high solubility, optimum bulk density and minimum free fat in whole milk powder without discolouration or undue loss of nutrients. Selection of proper atomizer controls the b.d. and free fat in powder along with feed conditions. Nozzle powder has less occluded air and higher b.d. than powder from rotating atomizer.
Whole milk powder produced from nozzle atomizer contains less free fat than from rotary atomizer due to higher homogenizing effect in high pressure pump and nozzle.

## Slide 7: Controls in spray Dryers
Automatic controls in spray dryers
Constant product input with control of Inlet air temperature
Constant product input during which outlet air temperature is automatically maintained by inlet air temperature variation
Control of moisture and quality with multistage drying with respect to maintaining constant outlet air temperature by feed control automatically
Variable Feed input in which outlet air temperature is constant for a constant air inlet temperature

## Slide 8: Factors Affecting the Capacity and Operation of Drum Dryer
The drying capacity varie from 5 to 50 kg of dry product per m2 and is affected by following factors:
Milk Feed temperature, concentration (desirable 18-25 % TS) and level of milk
Avoid uneven and broken sheet of drying materials on the drum
Drum gap in double drum dryer
Drum speed, Roller alignment
Steam pressure and temperature not too high and drum speed not too low
Condensate removal
High moisture of the product may be due to low temperature, thick film, high solid and high rpm of the drum.

## Slide 9
THANK YOU