## Slide 1: Application of Membrane Filtration in Utilization of Whey and skim milk in dairy Products
Dairy Process Engineering (DTE- 221)
Dr. J. Badshah
Head, Dairy Engineering, SGIDT, Patna
(Bihar Animal Sciences University, Patna)
ejazbadshah@gmail.com

## Slide 2: Utilization of Whey through UF
Applying membrane technology to whey processing allowed the production of refined proteins of commercial usage and thus transformed a waste byproduct from cheese production into a valuable product.
Fractionation of whey into protein rich and lactose containing streams is one of the most successful industrial applications of UF.
Protein content of raw whey can be increased from an initial value of 0.6 per cent to over 20 per cent in the UF step. When whey is concentrated about 20 times by UF, a dry matter content of 18-20 per cent is attainable.

## Slide 3: Utilization of Whey through UF
It is suggested when UF of whey be carried out for deproteinization for lactose manufacture, whey protein concentrates (WPC) powders should be made by drying of retentate from ultrafiltration of whey.
They are described in terms of protein content i.e. percent protein in dry matter ranging from 35 to 85 per cent. To make 35% protein product the liquid whey is concentrated to about 6-fold to an approximate total dry solids content of 9%.

## Slide 4: Milk protein standardization and fractionation
UF milk fractionated components can be used to stand the nutritional value of consumer milk or to prepare standardized milk powders, overcoming natural variations in milk composition.
The protein content by ultrafiltration makes the milk whiter, and more viscous, the sensory quality more similar to that of higher fat milks.
An MF/UF process can be used to fractionate non-fat milk into value-added protein ingredients. Resulting ingredients include native casein concentrates (from the retentate), pure milk serum proteins (from the permeate) and individual milk protein isolates that have application as emulsifiers, fortifying proteins and gelling agents.

## Slide 5: Fermented dairy products
UF can be used to standardize protein and total solids in milk for use in fermented dairy foods such as cream cheese, yogurt and cottage cheese.
Fermented products made with UF milk have superior quality and sensory characteristics compared to products made from milk concentrated by conventional methods.
Membrane filtration helps control quality attributes such as consistency, post-processing acidification and extent of syneresis.
However, using membrane-processed milk often requires an adjustment in starter culture selection and fermentation conditions.

## Slide 6: Membrane filtration in Cheese making
The cheese industry uses membrane concentrated milk to elevate the solids level of cheesemilk. Future applications for membrane processing may include the manufacture of fresh, soft, hard and semi-hard cheese varieties.
UF concentrated milk, with its fat and protein content concentrated to 3.5 fold and a portion of the lactose, ash and water removed, possesses the ideal composition for the potential manufacture of fresh cheeses like ricotta or brine cheeses like Feta.
Replacing 10-15% of the cheese milk volume with UF milk creates the opportunity to boost total solids, therefore increasing cheese throughput in factory by as much as 18 per cent and subsequently reducing production costs.
Using concentrated milk could also reduce rennet and starter culture requirements, depending on the application.
In addition, using UF milk could reduce a cheese plant’s wastewater processing costs.

## Slide 7: Cream &Skim milk Retentate powder
Scurlock in 1986 used UF as the 1st stage in the preparation of protein enriched whipping creams. Whole milk concentrated 2 to 5 fold by UF was separated conventionally to produce protein enriched creams with fat 25 – 45 % (w/w).
Ultra filtered skim milk retentate is spray dried to obtain S.M. retentate powder with 50 – 65 % protein. It shows lower bacterial counts and acidity and an excellent flavour.
A standardization of the protein levels with WMP with 32 - 35 % protein and skim milk powders with 38 - 41 % protein can be done by using UF skim milk and whey retentate and permeate.

## Slide 8: Low lactose milk powder
● It is developed by using low lactose milk powder, lactose content of which can be reduced by 86 %.
● Lactose was replaced by malto-dextrin.
● Na and K salts are added to compensate the loss of milk salts.

## Slide 9: Skim milk based concentrates &Sweetened condensed milk
In-container sterilized milk concentrates are prepared from UF skim milk.
Such concentrates with edible carbohydrates have TS of 40 % and shelf life oveer 1 year.
UF concentrates are used in making of SCM.
Such SCM has reduced sandiness in the texture.

## Slide 10: Ice – cream, Non Fat Dairy Cofee whitener and Whey Protein Quarg
Ice -Cream
UF can be used to prepare ice cream by using UF skim milk or UF reconstituted skim milk. Ice cream doesn’t shows any change in viscosity, specific gravity and overrun but gives improved creamy body and texture.
Non – fat dairy coffee whiteners
Retentates obtained by UF of skim milk are freeze – dried. The product is comparable to commercial non – dairy coffee creamer and has acceptable dispersibility.
Whey protein quarg
Concentrate obtained by UF of mixture of 80 % whey and 20 % skim milk is heated to obtain firm coagulum. It is also suitable for sweet desserts and puddings.

## Slide 11
THANK YOU