## Slide 1: Energy Analysis in Size Reduction Equipments
Dr. J. Badshah
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Technology

## Slide 2: Objectives of Size Reduction Units
Size reduction causing Increase in surface Area
Enhanced Rate of extraction &expresion of juices
High rate of drying, freezing, crystallization etc.
Reduction in Process Time in Cooking, Blanching
Development of new products such as flour, maida, spices, etc.

## Slide 3: Sieve Analysis
Particle size distribution in granular materials : Sieving or screening
Classification in course, medium and fine grains
Uniformity Index= Course : Medium : Fine grains
If it is 1: 3 : 6, then Course grain = 1/10, edium = 3/10 and Fine grains = 6/10
Fineness Modulus: Defined as the sum of the percent weight fraction retained above each sieve divided by 100.
Average size of particles in inches = Dp = 0.0041 (2) F.M.
Average Size of Particles in mm, Dp = 0.135 (1.366)F.M.

## Slide 4: Sieve Stack arranged in increasing order of mesh size
7 3/8 Mesh weight fraction% w1
6 4 Mesh w2
5 8 w3 F.M. = (w1x7+ w2x6+ w3 x5
4 14 w4 + w4x4+ w5x3+ w6 x2
3 28 w5 w7x1+ w8 x0 )/100
2 48 w6
1 100 w7
0 Pan w8

## Slide 5: Mesh Number System
The mesh number system is a measure of how many openings there are as per linear inch in a screen.
Sieving is a method of separating a mixture or grains into two or more size fractions. The oversize materials are trapped above the screen, while undersize materials can pass though the screen. In stacks, sieve divides samples into various size fractions.
There are two mesh sizes 9I) US Sieve size and Tyler equivalent size or Tyler Mesh Size. Table is available for ex. 10 Us sieve = 9 Tyler mesh = 2 mm,
40 US Sieve = 35 Tyler mesh = 0.420 mm and 100 US sieve = 100 Tyler Mesh = 0.149 mm particle size opening eyc.

## Slide 6: Energy Analysis of Size Reduction Unit
Mathematical Models for energy dE required to produce small change dx in the size of a unit mass of material
  General Model : dE/dx = - K /xn
  Rittinger’s Law:
    Energy required is proportional to the new surface area produced, i.e. n=2
    dE/dx= - K /x2
    On Integration E = KR [1/x2 – 1/x1]
    x1 and x2 are the average size of feed and product particles
    E is the energy per unit mass required to produce this increase in surface area and KR is Rittinger’s constant
    It is found to hold better for fine grinding where greater change in surface area is required.

## Slide 7: Energy Analysis of Size Reduction Unit
  Kick’s Law:
    Energy required is proportional to size reduction ratio i.e. n=1
    dE/dx= - K /x1 ∫dE = - ∫ K /x for limit x1 to x2
    On Integration E = Kk ln (x1 / x2 )
    x1 and x2 are the average size of feed and product particles
    E is the energy per unit mass required to produce this increase in size and Kk is Kicks’ constant
    Kick’s law has been found to apply best to coarse crushing
    Bond’s Law:
    Energy required is proportional to the square root of the surface to volume ratio of the product and n = 3/2
    dE/dx= - K /x3/2 ∫dE = - ∫ K /x3/2 for limit x1 to x2
    On Integration E = 2 KB [ 1/√x2 - 1/√x1 ]
    x1 and x2 are the average size of feed and product particles
    E is the energy per unit mass required to produce this increase in size and KB is Bonds’ constant
    Bond’s law has been found to apply best to variety of materials undergoing coarse, intermediate and fine grinding

## Slide 8: Bonds’law in terms of Bond Work Index
Energy Required in KW hr per unit mass in ton Ranges from 10 -20 KWhr/ton
Dp and Df are size such that 80 % of the sample passed through mesh of diameter Dp and Df in mm respectively.
Wi Bond work index in (2000 lb) is the work required to reduce from a very size to that size in which 80% passing through the 100 micron screen
P= kilowatt and m = ton/ hr Kb = √(100x10-3 ) wi = 0.3162 wi
P/m= 0.3162 wi [1/ √Dp - 1/√Df ]

## Slide 9: Numericals on Bonds’ law
What is the power required to crush 100 tons /hr of limestone if 80 per cent of the feed passes a 2 – in screen and 80% of the product a 1/8 –in screen? Given index for limestone is 12.74
Solution: M = 100 tons /hr
Dpa = 2 inch = 2x 25.4 = 50.8 mm
Dpb = 1/8 inch = 1/8x 25.4 = 3.175 mm
The Power Required P/m = 0.3162 wi [1/ √Dp - 1/√Df ]
Therefore, P = 100 x 0.3162 x12.74 (1/ √3.175 – 1/ √ 50.8)
Therefore P = 169.6 KW = 227 hp

## Slide 10: Numericals on Bonds’ Law
Sugar is ground from crystal of which 80% pass 30 mesh screen down to a size in which 80% pass a 200 mesh sieve and 5 h.p. metor is sufficient for required throughput. If the requirement is changed such that the grounding is only down to 80% through a 150 mesh sieve but the throughput is to be increased by 80%. Would the existing motor has the sufficient power to operate the grinder. Assume Bond Equation.

## Slide 11: Numericals on Bonds’ Law
Df = 30 mesh = 0.595 mm
Dp1 = 200 mesh = 0.074 mm
Dp2 = 150 mesh = 0.110 mm
M1 = m
M2 = 1.8 m
P1 = 5 h.p. = 5 x 0.746 = 3.730 Kw
Using Bonds’ Law
The Power Required P/m = 0.3162 wi [1/ √Dp - 1/√Df ]
3.73/m = 0.3162 wi [1/ √0.074 - 1/√0.595 ] ---------(1)
Similarly P2/ 1.8 m = 0.3162 Wi [ 1/ √0.110 - 1/√0.595 ]----(2)
On solution P2 = 6.55 h.p. ( Not Sufficient)