## Slide 1: Equipments for Pulping Fruits and Vegetables
Food Engineering (DTE – 321)
Dr. Jahangir Badshah
University Professor-cum-Chief Scientist
Dairy Engineering Department, SGIDT, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Purpose and Objectives of Pulping
Pulping: Process that crush the fruits and vegetables products with the aim of separating the pulp from seed and skin by pulping equipments or extraction equipments.
Type and design of pulper depends on size, shape and texture of fruits and vegetables.
Sometimes, g– a major unit operation for making processed products as per requirement of end products for some processed foods.
Capacity as well as Hygienic production and maintenance of equipments.
Driving mechanism: Mechanically or Electrically operated

## Slide 3: Types of Pulper
Fruit Crusher
Fruit Presses
Fruit and Vegetable Pulper
Twin Pulper
Fruit Mill
Motorized Hydraulic Fruit Press
Fruit Juicer
Stainless Steel Pulper

## Slide 4: Fruit Crusher
It consists of a rotating screw inside a casing, which has screen in the base.
The cone screw expresser or paddle pulper fitted with appropriate screeens serves the purpose of sparating the juice from particulate matter.
Juice and pulp drains from an outlet in the base of casing and skin is ejected from the end of the casing down a chute.
It is used for hard fruits such as Pine apples, which are cut into larger pieces and fed into hopper.
Monthly greasing of bearings, routine checks of belt tensions and electrical connections are important

## Slide 5: Fruit Press
1. Manual Fruit Press: It has a SS cage in which a press plate is raised or lowered by a screw.
The screw made of harder grade of steel than the bearing to prevent the more expensive from wearing down.
Layer plates made from SS, nylon or painted mild steel
In operation a muslin or cotton bag is placed in the cage and pulp is poured in. The bag is closed and the press plate is lowered. After collecting Juice via a pipe, the screw is then raised and the bag is removed.
2.Hydraulic basket: A press system where pistons move down into a press sack containing the crush.
Better extraction is obtained by mixing the crush between multiple pressing to expose fresh surface near the cloth.

## Slide 6: Fruit Press
Thermal Screw
A thermal screw is a continuous system for both transporting and heating or cooling crushed fruit or whole small fruit.
In continuous pressing, the screw can even be slowed down enough to accomplish the holding time and then feed directly to press with another screw.
Belt Press
A more expensive system is a belt press where the pulp is pressed between porous belts by rollers.
Multiple pressing or rotations further yields more but require more time.
Juice clarification, filtration and deaeration to improve quality and shelf life of packed juice.
It is used for apple, grape, pear, pineapple, carrot etc.

## Slide 7: Fruit and Vegetable Pulper & Twin pulper
It consists of scraper rotors, spiral scraper and brushes which rotates at a very high speeds and thus separating the stone, skin and the pulp.
The second stage in twin pulper is used for receiving the refined pulp from the primary stage and are available in the wide range of capacity.
The fruit and vegetable pulper is used for the extraction of pulp from vegetables and fruits like mango, litchi, guava, pear, tomato, passion fruit, grape and so on. Capacity varies from 80 kg/hr to 3 tonnes per hour depending upon size, type and quality of the products to be pulped.

## Slide 8: Fruit mill and motorized hydraulic press
It uses SS rotor against the SS blades driven with a powerful motor to crush hard seedless fruits for extaction.
All parts are made up of food grade SS.
Manufacturer of fruit mill crusher enabled with sturdy fixture mounted on MS steel band.
Hydraulic Juice Press: Manufactured with high quality materials with durability and high tensile strength. It has SS tray with proper depth.
It is used for the extraction of juice from crushed fruits like pineapple, grapes, orange, apple and so on.

## Slide 9: Thank You ejazbadshah@gmail.com