## Slide 1: TVR and MVR Operations and Analysis
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: TVR
In thermo compressor, the kinetic energy of a jet of steam is used to compress the vapour. It consists of a steam nozzle, suction chamber with inlet for sucking in the vapour, mixing chamber and recompression chamber.
The live steam at pressure P1(state-1) is almost isentropically expanded in the nozzle to suction pressure P2 (state-2). Steam pressure usually employed in the condensing plant is about 8-12 bar and suction pressure about 0.2-0.3 bar depending on the effect from which the vapour is drawn. The expanded steam emerges from the nozzle as a jet of steam. The velocity of the steam is about 1000 m/sec.
Fig. 7.3 Enthalpy - entropy diagram of thermal vapour recompression (TVR)
The amount of vapour, MV and amount of live steam, Ms are related as follows (Kessler, 1981).
MV/Ms= [0.8 (h1-h2) / (h4-h3)] – 1
Where h1, h2, h3, h4 is enthalpies of steam at various state points.
It can be seen from the above equation, that if the vapour to live steam ratio is higher, the factor h4-h3 decreases. This means that rise in temperature of compressed vapour is smaller. A thermo compressor with a vapour to live steam ratio of 50 : 50, gives a temperature rise in the compressed vapour of about 15oC. But, if the proportion is 60 : 40, the temperature rise is only 11oC.
Generally, the vapour drawn from the first effect is recompressed and used for the same effect again. However, more recently, the trend is to draw vapour from the second or third effect and use the recompressed vapour in the first effect. This is due to the fact that the evaporating capacity of earlier effects is increased.
With thermo compressor drawing vapour from the second effect, one must choose the right thermo compressor to achieve a temperature which lies at least 5oC above the boiling temperature of the first effect. The performance of thermo compressor is influenced by the heat transfer rate in calandria, suction pressure, discharge pressure and the motive steam pressure.

## Slide 3: TVR
In the mixing chamber the sucked-in vapour is entrained and carried away by the expanded steam. The vapour is accelerated as the steam transfers its kinetic energy to it. The mixing occurs at constant pressure, the enthalpy is increased and state point-3 is reached.
From this point onwards, the cross-section of the thermo compressor increases, and so the kinetic energy of mixture is converted into potential energy. The pressure of the mixture is increased almost isentropically from state-3 to state-4.
In this way the low pressure steam taken from a lower effect is compressed to a higher pressure corresponding to the inlet pressure of previous stage operating at higher pressure and temperature.

## Slide 4: Advantages and disadvantages of TVR
Advantages of TVR
  Implementation of flavour recovery is possible
  Simple and effective design
  No movable parts required in steam jet ejector design of TVR
  Low investment costs
  High operation Reliability
Disadvantages of TVR
  High long term cost
  Overall high energy requirements
  Intensive in space requirements
  Negative CO2 footprint

## Slide 5: Mechanical vapour recompression (MVR)
The low pressure vapour is compressed mechanically i.e. employing single or multiple stage radial flow compressors or by axial flow compressors. These compressors may be driven by electric motors, I.C. engines or steam turbines.
The quantity of vapour MV drawn from the evaporator is at saturation condition with pressure P1, temperature t1 and enthalpy h1. The mechanical compressor compresses the vapour almost isentropically to a pressure P2, temperature t2 and enthalpy h2.
This is superheated steam, which is not suitable for heating the milk as such, because of its bad heat transfer properties. It is cooled down to saturated state-3 i.e. temperature t3 and enthalpy h3 at constant pressure P2.

## Slide 6: Mechanical vapour recompression (MVR)
This is done by diverting a portion of condensate at temperature t4 and injecting it in the superheated steam. The condensate evaporates by consuming superheat from the compressed vapour. The mixture thus achieves final state-3 with temperature t3 enthalpy h3 and pressure P2 . The amount of steam available is thus increased by the amount of condensate mixed.
At this stage is should be remembered that the energy required to drive the MVR may be costlier than steam. Thus actual saving will be somewhat less depending on the prices of steam and other forms of energy employed to run MVR.

## Slide 7: Advantages of MVR
Apart from being extremely economic MVR has other advantages.
  1. The maximum evaporating temperature of first effect can be reduced to such as extent that burning on of product is minimized.
  2. The lowest effect of evaporating temperature i.e. of last effect can be high enough which results in lower viscosity of the concentrate facilitating easy handling of concentrate. The pre-heating of concentrate before drying may be avoided or may be reduced to a less drastic treatment.
  3. The higher temperature in the final effect results in reduced choking of calandria. Thus the plant can be run for a longer period before cleaning.
  4. The need for cooling water is considerably reduced or totally eliminated.
  5. Energy efficient, reduced CO2 footprint and low long term cost.

## Slide 8: Disadvantages of MVR
A major disadvantage of MVR is the greater expenditure on equipment, maintenance cost and noise problem, but most of the studies indicate that the payback period for MVR is about 2-2.5 years.
Efficiency depends on production volumetric flow rate along with high investment costs
High wear and Tear
Not simple and cumbersome design
Less operation reliability and needs one standby at high investment.

## Slide 9: Factors to decide MVR over TVR
As a conclusion, we can tell that the decision whether to utilize evaporator with MVR or a plant with TVR depends on several factors like the consideration of steam production cost, size of the company or production volume.
  Capacity and operating data like annual operating hours
  Wear and Tear and Electricity requirements
  Legal framework of the production location
  Personnel and labour cost for operating and servicing the plant
  Space availability for steam production in boilers
  Product properties like viscosities as for higher viscosities MVR is preferred.
  Capital Costs involved
  Size of evaporating plant

## Slide 10: Single effect evaporator with accessories

## Slide 11: Single effect with MVR evaporator

## Slide 12: TVR in Single effect evaporator

## Slide 13
THANK YOU