## Slide 1: Numericals on Size Reductions units
Dr. J. Badshah
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Technology

## Slide 2: Numerical on Ball Mill
Q.1.What is critical rotational speed in revolution per second, for a ball mill of 1.2 m diameter charged with 70 mm diameter balls.
Soltion: Critical speed for a ball mill Nc = 1/2π (√2g/(D-d))
Nc = 1/2x3.14 (√2x 9.81/(D1.2-d70x10-3)) = 0.663 rps
Q.2. A ball mill of 1.8 m diameter is loaded with steel balls each having a diameter of 6 cm. The rotational speed of the ball is kept at 75 % of the critical speed. Calculate The operational speed of the ball mill in rpm.
Solution: Critical Speed of ball mill = Nc = 1/2π (√g/(R-r))
Nc = 1/2x 3.14 ( 9.81/(0.9-0.03)) = 0.534 rps = 32.04 rpm
However, Operational speed of ball mill = 0.75 x 32.04 = 24.03 rpm

## Slide 3: Numericals
A pulse mill grinds Bengal gram of 2 mm volume- surface mean diameter to powder of 100 micron volume-surface mean diameter. Calculate the ratio of Rittinger’s to Kick’s constant in the grinding opearation.

## Slide 4: Numerical
The fineness modulus of the ground maize feed is 3.7. Calculate the average size of the particle.
It is found that the energy required to reduce particles from a mean diameter of 10 mm to 3 mm is 11 KJ/Kg. Using Rittinger’s law calculate the energy requirement to reduce the same material from a diameter of 1 mm to 0.3 mm.

## Slide 5
Thank you