## Slide 1: OPERATION AND MAINTENANCE OF SPRAY DRYERS FOR MILK POWDER
Dairy Process Engineering (DTE – 221)
Dr. Jahangir Badshah
University Professor-cum-Chief Scientist
Dairy Engineering Department, SGIDT, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: PREPARATIONS REQUIRED
UTILITIES AND SERVICES REQUIRED
  ELECTRICITY
  WATER
  COMPRESSED AIR
  STEAM AT REQUIRED PRESSURE FOR AIR INLET TEMPERATURES OF 180-200° C ( 12 – 15 KGF/CM2)
  CLEANING & SANITIZATION OF DRYING PLANT
  PROPER SETTING OF ATOMIZER, AIR HEATER, FEED PUMP AND AIR DISPERSING VANES IN DRYING CHAMBER
  PROPER LUBRICATION OF ATOMIZER (DISK TYPE) OR NOZZLES SETTING AND REPLACEMENT OF WORN OUT NOZZLE HEADS
  PROPER FUNCTIONING OF INSTRUMENTS AND QUALITY CONTROL LAB FOR TESTING MOISTURE CONTENT OF POWDER

## Slide 3: START UP PROCEDURE FOR SPRAY DRYING PLANTS
CHECK FOR PROPER CONNECTIONS AND CLOSING OF ALL JOINTS IN CHAMBER AND CYCLONE SEPARATORS
OPEN THE CHAMBER DOOR AND START THE EXHAUST FAN AND COOLING AIR FAN
START THE SUPPLY FAN AND CLOSE THE CHAMBER DOOR AND AIR SWEEP DOORS.
ADJUST THE DAMPER IN EXHAUSR FAN TO KEEP SLIGHT VACUUM OF 7-10 MM HG IN DRYING CHAMBER ON EQUILIBRIUM WITH AIR VELOCITY OF APPROX. 5 TO 10 m/s.
START THE ROTARY VALVES, VIBRATING DEVICE, AIR CONVEYING FANS
START THE ATOMIZER, IF CENTRIFUGAL DISK TYPE BEFORE STARTING POSITIVE DISPLACEMENT LOBED IMPELLER PUMP.
ADMIT STEAM FOR HEATING THE FILTERED AIR AND WHEN THE OUTLET AIR TEMPERATURE IS RAISED TO 85 TO 100°C, THE FEED PUMP IS STARTED AND WATER IS FED TO THE ATOMIZER.
CONTROL THE WATER INLET FLOW RATE SO THAT THE AIR INLET TEMPERATURE IS ADJUSTED TO AROUND 95-100° C.

## Slide 4: START UP PROCEDURE FOR SPRAY DRYING PLANTS
When the outlet air temperature is raised to 190 – 200°c, switch over to concentrate (45- 50% TS).
Control the mass flow rate of concentrate to adjust outlet air temperature to 90 -95°c. Higher air outlet air temperature means low moisture in powder. This is due to low mass flow rate of concentrate. Increasing flow rate of concentrate means decrease in outlet air temperature and increase in moisture content of powder.
The outlet air temperature should be continuously monitored to control uniform quality of powder either manually or automatically using servomotor to change the feed rate automatically.

## Slide 5: SHUT DOWN PROCEDURE FOR SPRAY DRYING PLANTS
Change over to water from product. Continuously reduce the feed water to maintain the air inlet temperature not lower than 120-150° C to avoid soiling in the chamber.
Close the steam valve of air heater. When the air inlet temperature comes down to about 120-150°C stop feed pump.
Open the drain cock provided on feed line to the atomizer.
Stop the atomizer.
Open the door and hook it to prevent complete closures of the door.
Stop the air supply fan and cooling fan.
Stop chilled water to the powder cooling chamber.
Allow air sweeping of the chamber.
When all the powder is carried out of the plant, the exhaust fan, conveyor fan and rotary valves are stopped.
Close the chamber door and dampers on the air ducts.
It is important that when the exhaust fan is started without running supply fan, the chamber door should be kept opened otherwise it will damage the chamber lining.

## Slide 6: Operational Problems and Remedial measures in spray dryer
Improper spray pattern
Erosion of Pressure Nozzles
Plugged atomizer should be cleaned.
Reducing the high concentration of concentrate which may clog or chock the nozzles.
Very high pressure or low pressure in Nozzle atomizer and very high or low speed in disk atomizer.
Feed containing high foreign particles or high concentration
Cavitations due to high feed temperature and air leakage
Too high atomizer pressure

## Slide 7: Operational Problems and Remedial Measures
Incomplete drying and high moisture content
Low moisture in powder
High Feed rate and low air outlet temperature. Reduce feed rate and increase outlet air temperature.
High air inlet humidity and incorrect spray pattern
Low pressure or low speed
Increase flow rate to reduce outlet air temperature.
Fine atomization due to diluted feed
High pressure or speed.

## Slide 8: Operational Problems and Remedial Measures
Burnt powder particles.
Lumpiness in Powder
Dusty air exhaust and higher stack losses
Deposition on atomizer or dryer wall
Air temperature too high, adjust it.
Improper and delayed cooling of powder
Excessive moisture in powder.
Insufficient and slow cooling of powder.
Too fine atomization.
Increased load on separation.
Insufficient powder separation
High air outlet temperature
Coarse droplets
Incorrect spray pattern
Incomplete drying
Air dispersion vanes wrongly set.

## Slide 9: Thank You ejazbadshah@gmail.com