## Slide 1: Treated Dairy Effluents and Disposal
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Global warming from dairy farms and processing
Man made activities have added significant quantities of green house gases (GHGs) to the atmosphere. The most important GHGs generated by the dairying ate methane (CH4), Nitrous oxide (N2O), carbon dioxide (CO2) and some refrigerant emission (CFCs and HFCs).
The largest emissions of GHGs are due to dairy animals which accounts around 80 % of the GHG emissions of the total life cycle of milk.

## Slide 3: Global warming from dairy farms and processing
Main sources of GHGs emissions from dairying:
Animals – primarily CH4 emissions. Young animals below 3 months do not produce methane
The manure storage –CH4 and N2O emissions
Crop, pasture, direct emissions on the pasture and indirect emissions through leaching – N2O emissions
Feed productions- mainly N2O emissions
Process energy consumption and fuel consumption for transport- CO2
Industry refrigeration for process, freezing and storage- CFCs and HFCs

## Slide 4: Dairy Plants discharge Problems
Need of permit to discharge waste waters directly to streams, bays, rivers, creeks and /or estuaries and land disposal from the state government control agency.
Effluents from waste treatment systems must be sufficiently reduced in BOD and biological nutrients (e.g., P, NH3) as per the limits of Environmental regulatory agencies
To reduce the volume of dairy wastewater to be treated and reduce treatment costs, careful attention must be given to minimizing losses of milk and milk products in the dairy plant.
With good product conservation and selection of an effective waste treatment process, dairy plant operators should be able to operate profitably and meet environmental requirements.

## Slide 5: Dairy Plants discharge Problems
The combined effluent varies in its characteristics by way of its organic contact, BOD varying from 500 mg/l to 3500 mg/l.
The dairy industry is not a major contributor to carbon foot- prints i.e. not contributing much GHGs. World summit held in Berlin in September, 2009 forced over the need to control the carbon foot print or GHGs emission.
The dairy sector has to control the production of methane pollution resulting mainly from milk production systems.
Secondly, the usage of energy intensive technologies have to be optimized by adopting various energy conservation programs and giving special policy thrust to decide the appropriate use of non-thermal technologies.

## Slide 6: Dairy Plants discharge Problems and Solutions
Similarly use of renewable energy resources such as biogas, solar energy, bio fuels energy etc. would place Indian dairy sector to a level field of international sanitary and hygiene standards. It will also derive the best benefits of the global carbon trading for India.
As the energy is becoming costlier, the aerobic processes are becoming very costly to operate, and hence are becoming an economic burden to the dairy industry.

## Slide 7: Alternative to Aerobic Treatments
The first intermediate alternative is to go for anaerobic treatment. The dairy waste being highly bio-degradable, the anaerobic process should also be equally amendable to reduce the organic content for the wastes. Kadam and Saxena, 1996 mentioned the details of High rate activated sludge processes, Plastic media Bitowers and Upflow anaerobic Sludge blanket (USAB) process apart from anaerobic lagoons, oxidation ponds, aerated lagoons and activated sludge process for effluent treatment systems in a dairy plant.

## Slide 8: Alternative to Aerobic Treatments
The cheese whey has BOD in the range of 35000 to 60000 mg/l. Therefore, it is highly suited for anaerobic treatment because such streams with high BOD can yield biogas without requiring any energy.
On the other hand, the biogas produced contains methane in the range of 65-80 % which can be used as the gaseous fuel replacing LPG or it may even be used simultaneously with diesel for running the diesel engine.

## Slide 9: Guidelines for Carbon Credits and carbon Trading
While finding solution to the Effluent disposal and Global warming problems, the concepts of carbon credit and trading come into picture as part of an international agreement, popularly known as Kyoto Protocol.
Carbon credit is a generic term meaning that a value has been assigned to a reduction or offset of GHGs emissions. One carbon credit is equal to one ton of CO2, or in some markets, CO2 equivalent gases.
The goal is to allow market mechanisms to drive industrial and commercial processes in the direction of low emissions of GHGs.

## Slide 10: Guidelines for Carbon Credits and carbon Trading
Since GHGs mitigation projects generate credits, this approach can be used to finance carbon reduction schemes between trading partners and around the world.
Carbon credits are certificates issued to countries that reduce their emissions of GHGs that leads to global warming.
Animal waste methane recovery and utilization
Installing an anaerobic digester & utilizing methane to produce energy
Capture of biogas, Fuel switching from more carbon intensive fuels to less carbon intensive fuels, Renovation of older power plants, Upgrading instrumentation, controls and/or equipments, Changes in vehicles/Milk tankers and/or fuel type, for example, switch to electric cases or fuel cell vehicles (CNG/ Bio fuels)

## Slide 11
THANK YOU