## Slide 1: Basic Concepts of Heat Transfer
Dr. J. Badshah
Professor and Head, Dairy Engineering
SANJAY GANDHI INSTITUTE OF DAIRY TECHNOLOGY
(Bihar Animal Sciences University, Patna)
Email: ejazbadshah@gmail.com

## Slide 2: Basic Concepts of Thermodynamics and Heat Transfer
System & Boundary:
  Isolated,
  Open,
  closed,
  Adiabatic,
  Homogeneous system e.g. Water plus Niitric acid
  Heterogeneous system e.g. Water plus Steam or Ice plus Water
Thermodynamic Equilibrium :
  Thermal Equilibrium,
  Mechanical Equilibrium
  Chemical Equilibrium
Properties of the system
  Intensive Properties
  Extensive Properties

## Slide 3: Thermodynamic Terms
State : a condition of the system at any instant of the time and it says each property has a single value at each equilibrium state.
Process: It occurs when system undergoes a change instate
  Non-Flow Process : Closed systems undergo non-flow process
  Flow Process: Mass is entering and leaving through the boundary of an open system as well as heat or work crossing the boundary of the system
  Cycle , Point Function Properties and Path Function Properties
Heat and work are path function properties, However temperature, Volume, Pressure are point function properties.

## Slide 4: Temperature, Pressure and Energy
Temperature
Absolute Temperature :
  When no kinetic energy left in any molecule of substance/gas and gas will not occupy any volume
  Absolute temperatur = Thermameter reading in °C + 273
  Absolute temperature = 0° A or – 273 °C
  Methods to measure temperatureand calibration of Thermometer
  Line above sulphur boiling uses Platinum Rhodium thermocouples
  Line below sulphur boiling uses Platinum Resistance Thermometer

## Slide 5: Calibration Table for thermameter
Gold Melting : 1316.16 °A = 1063°C
Silver Melting : 1233.96 °A = 960.80 °C
Sulphur Boiling : 717.76 °A = 444.60°C
Water Boiling : 373.16 °A = 100°C
Melting point of Ice: 273.16°A = 0°C
Oxygen Boiling Point :90.19°A = - 182.97 °C
No K.E. left in molecule : 0°A= - 273.16 °C

## Slide 6: Units of Heat and Temperature
Heat: A transient quantity which only appear at a boundary while a change is taking place
Units of Heat:
Mean gm calorie (quantity of heat required to raise the temperature of 1 gm of water from 0 to 100°C divided by 100)
Kg calorie : 1000 gm calorie
B.T.U. (quantity of heat required to change the temperature of 1 lb water from 59.9 to 61.7°F.
CHU (quantity of heat required to change the temperature of 1 lb of water by 1°C at 1 atm. Pressure)
°C + 273.16 = Kelvin
C/5 = (F-32)/9 = (K -273)/5 = (Reumer -492)/9

## Slide 7: Energy, Work and Heat
Energy
  Stored Energy: Internal Energy (chemical energy, Electrical Energy) & Mechanical Energy ( Potential energy , Kinetic energy)
  Energy in Transition : ( Heat and work)
  Work
    + ive Work : Output work i.e. work done by the system
    _ ve Work : Work Input to the system i.e. work done on the system
    Heat
    +ive Heat: Heat received by the system
    -ve Heat : Heat rejected by the system