## Slide 1: Modes of Heat Transfer & Analysis
Dr. J. Badshah
Professor and Head, Dairy Engineering
SANJAY GANDHI INSTITUTE OF DAIRY TECHNOLOGY
(Bihar Animal Sciences University, Patna)
Email: ejazbadshah@gmail.com

## Slide 2: Modes of Heat Transfer
Conduction
  Transfer of heat without appreciable displacement of molecules forming the substance
  In solids conduction by lattice vibration or by transport of free electrons
  In gases, the kinetic energy of the molecules is a function of temperature and energy is transferred in low temperature region by collisions
  In liquid the molecules are more closely spaced than that of gases but the mechanism of heat transfer is same as that of gas
  Fourier’s law of heat conduction: Q= - KA dt/dx
  The decreasing value of temperature gradient (dt/dx) will take care of –ive sign in above equation.
  Area A is perpendicular to the direction of heat flow, m2 , Q is in Watt if thermal conductivity K is in W/m. K and dx is the thickness in m in the direction of heat flow

## Slide 3: Thermal Conductivity: Essential Features
Definition: K = Q/A . dx/dt where Q is heat per unit time
Conduction of heat proportional to K
Heat conduction : In decreasing order of pure metals, alloys and non metals due to decreasing K values.
K in pure metals varies from 10 to 400 W/m °C, K in Alloys varies from 12 to 120 W/m °C
K in insulating materials: 0.023 to 2.9 W/m. °C
K in liquid : 0.2 to 0.7 W/m. °C
K in gases and vapours: 0.006 to 0.05 W/m. °C
Dependence of thermal conductivity on Temperature:
K = K0 (1 + β t), where β is -1/°C for metals and liquids (Aluminium, Uranium and water being the exception)

## Slide 4: Thermal Conductivity: Essential Features
In gases the values of K increases with increase in temperature because K is proportional to mean molecular path of the molecules. But higher molecular weights gases having high density and low mean molecular path results in lower K values at the same temperature.
In solids and liquids K depends weakly on pressure but in gases K is independent of pressure (near atmospheric pressures).
K of damp materials of non metallic solids is considerably higher and depends on type of gas in the voids.
Wiedmann and Franz Law: The ratio of the thermal (K) and electrical conductivities (σ ) is the same for all metals at the same temperature. The ratio K/ σ is proportional to absolute temperature T °A for all metals. K/ σ T = C = 2.45 x 10 – 8 W Ω/ K2
The materials which are good conductors of electricity are also good conductors of heat.

## Slide 5: Thermal Resistance and Electrical Analogy
Electric Circuit Theory has Ohm’s Law: I = V/R
Fourier’s Equation have Q = dt /(dx/KA)
Thermal Resistance (dx/KA) is analogous to electrical resistance R, Q is analogous to electrical current ‘I’ and Temperature difference ‘dt’ is analogous to electrical voltage difference.
Therefore rules for combining electrical resistances in series and parallel will apply equally to the combination of thermal resistances.
Calculate the rate of heat transfer per unit area through a copper plate 45 mm thick, whose one face at 350°C and the other face at 50°C. Take thermal conductivity of copper as 370 W/m °C.
Q/A = -K dt/dx = -370 (50 -350)/0.045 = 2.466 x 106 W/ sq. m.

## Slide 6: Heat Transfer by Convection
Newton’ law of cooling: Q = h .A. (ts- tf)
Factors for film heat transfer coefficient h are:
Thermodynamic and Transport proprties
Nature of flow
Geometry of surface
Prevailing Thermal conditions
Convection Thermal Resistance = 1/ h A
A hot plate 1 m x 1.5 m is maintained at 300°C. Air at 20°C blows over the plate. If the convective heat transfer coefficient is 20 W/m2 °C. Calculate the rate of heat transfer. Solution: Q = 20 x 1.5 x (300-20) = 8400 W

## Slide 7: Heat Transfer by Radiation
Laws of Radiation:
Wein’s Law: wavelength corresponding to the maximum energy (λm) is inversely proportional to absolute temperature of hot body
Kirchhoff’s Law: Emissivity of the body is numerically equal to its absorptivity for radiant energy from body at the same temperature.
The Stefan- Boltzmann Law: The law states that the emissive power of a black body is directly proportional to fourth power of its absolute temperature i.e. Q α T4
Q = F σ A ( T14 - T2 4)
Where, F = A factor depending on geometry and surface properties, Stefan- Boltzmann constant σ = 5.67 x 10 -8 W/m2 K4 , T1 and T2 : Temperature in degrees kelvin

## Slide 8: Numericals on modes of heat transfer
Solve 5 Numericals on each modes at least.
A carbon steel plate (K = 45 W/m°C) dimension : 600 mm x 900 mm x 25 mm is maintained at 310°C. Air at 15°C blows over the hot plate. If convection heat transfer coeficient is 22 W/m2 °C and 250 W is lost from the plate surface by radiation, calculate the inside plate temperature. In this case Qcond. = Q conv. + Q radiation
- K A. dt/dx = h. A ( ts –tf) + F σ A ( T14 - T2 4)
-45x0.54xx (310 – ti) /0.025 = 22 x 0.54 (310-15) + 250
Therefore ti = 313.86 °C

## Slide 9: THANKS TO ALL