## Slide 1: Heat Conduction through Hollow Spheres Heat and Mass Transfer (DTE - 122)
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Conduction Through Hollow Spheres
  Let us consider a Hollow sphere of inner radius r1 and outer radius r2 and made up of materials having constant thermal conductivity. The inner hot fluid temperature as t1 and outer surface temperature as t2 with the condition that t1>t2 .
  Therefore temperature varies only radially and we can assume that this radial direction is x-direction. Thus temperature field is one dimensional and the isothermal surfaces are spherical surfaces possessing a common axis with the sphere.
  Consider a small element of thickness dr at any radius r. Area of element through which heat is transmitted, A = 4 πr2

## Slide 3: Conduction Through Hollow Shere
During steady state, the rate of heat transfer is given by
Q = -K. 4πr2 . dt/dr
Rearranging and integrating the above equation, we obtain for limit from r1 to r2 with respect to time from t1 to t2:
Q ∫dr/r2 = - 4πK ∫dt
- Q [1/r2 – 1/ r1] = -4πk (t2 - t1)
Q = (t1 – t2) /[(r2 – r1)/4πKr1r2 ]
  Case II: Variable thermal conductivity, we have:
  Q = [4πK0r1r2 / (r2 – r1)][1 β/2 (t1 + t2 )](t1 – t2)
  Observe Figure of steady state conduction through Hollow sphere on group whatsapp.

## Slide 4: Logarithmic Mean Area For Hollow Sphere
It is considered that the heat flow from the hollow sphere is of the sme form as that of the plane wall. Expression for heat flow through the hollow sphere and plane wall are :
Q sphere = (t1 – t2) /[(r2 – r1)/4πKr1r2 ]
Q plane wall = (t1 – t2) /[(r2 – r1)/K Am]
Log mean Area , Am is so chosen that the heat flow through the sphere and plane wall will be equal for the same thermal potential.
Q sphere = Q plane wall
(t1 – t2) /[(r2 – r1)/4πKr1r2 ] = (t1 – t2) /[(r2 – r1)/K Am]
Therefore, Am = 4πr1r2
(Am)2 = (4πr1r2)2 = (4πr1)2 x (4πr2 )2
(Am)2 = Ai x Ao
Am = √ Ai x Ao = 4π(rm )2 = 4πr1r2
Therefore Logmean radius rm= √(r1r2)

## Slide 5: Numericals on conduction through sphere
A spherical shaped vessel of 1.4 m diameter is 90 mm thick. Find the rate of heat leakage, if the temperature difference between the inner and outer surfaces is 220°C. Thermal conductivity of the material of the sphere is 0.083 W/m°C.
Solution : Use The formula:
Q sphere = (t1 – t2) /[(r2 – r1)/4πKr1r2 ]
R2 = 0.7 m
R1 = 0.7 – 0.09 = 0.61 m
Q = 1088.67 W

## Slide 6
THANK YOU