## Slide 1: CONDUCTION THROUGH A COMPOSITE SPHERES and Numericals Heat and Mass Transfer (DTE - 122)
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Conduction Through Cylindrical Wall
  Let us consider a Composite sphere of inner radius r1 , outer first layer radius r2 and outer second layer radius r3 . Let us assume K of the materials are constant. The inner hot fluid temperature as thf , and outer face temperature of sphere as t1, Temperature at outer temperature of first layer as t2 and second layer as t3 and tcf as temperature of cold fluid atmospheric air at extreme outer are held at constant values. In which, the condition prevails as thf > t1> t2 > t3 > tcf .
  Therefore temperature varies only radially and we can assume that this radial direction is x-direction. Thus temperature field is one dimensional and the isothermal surfaces are spherical surfaces possessing a common axis with the sphere.

## Slide 3: Conduction Through Composite Cylindrical Wall
During steady state, the rate of heat transfer is given by
Q = hhf 4π(r1)2 (thf - t1 ) = KA. 4π. r1 r2(t1 - t2 )/(r2 - r1)
= KB. 4π.r2r3 (t2 - t3 )/ (r3 - r2) = hcf 4π (r3)2 (t3 - tcf )
(thf - t1 ) = Q/ hhf 4π (r1)2
(t1 - t2 ) = Q (r2 - r1)/ KA 4π. r1 r2
(t2 - t3 ) = Q (r3 - r2) / KB 4π. r2r3
(t3 - tcf ) = Q/ hcf 4π (r3)2
On Addition, we have general equations for two layer case:
Q = 4π (thf – tcf)/ [ 1/ hhf .(r1 )2 + (r2 - r1)/ r1 r2 .KA + (r3 - r2)/r2r3 . KB + 1/ hcf .(r3 )2]
For nth layer case, the general equations is :
Q= 4π (thf – tcf)/ [ 1/ hhf .(r1 )2 + ∑ (n=1 to n=n){(r(n+1) - rn)/ rn . r(n+1) .Kn }+ + 1/ hcf .(r(n+1))2]

## Slide 4: Numerical on Composite sphere with convection coefficients
A spherical shaped vessel of 1.4 m diameter is 90 mm thick. Find the rate of heat leakage, if the temperature difference between the inner and outer surfaces is 220°C. Thermal conductivity of the material of the sphere is 0.083 W/m . °C.
Solution: Rate of heat loss: r2 = 0.7 m and r1 = 0.7 – 90/100 = 0.61 m
Q = (t1– t2)/ [(r2 - r1) / KA 4π. r1 r2 ]
Q = 220/ [(0.7 - 0.61) / 0.083 x 4π. 0.61 x 0.7 ]
Q = 1088.67 Watt

## Slide 5: CRITICAL THICKNESS OF INSULATION
Insulation : To retard the to and fro heat Flow in boilers, Air Conditioning system, Refrigerators, Cold Stores etc.
Critical Thickness: The thickness upto which heat flow increases and after which heat flow decreases is termed as Critical Thickness of insulation.
Critical thickness of insulation for cylinder:
Q = ( t1 - t2) (2πL)/ { ln (r2/ r1 )/K + 1/ ho . r2 } kcal/hr
Q becomes maximum when denominator will be minimum. When differential of denominator with respect to r2 is equated to zero, the condition for minimum denominator or total resistance and maximum heat loss will be achieved:

## Slide 6: CRITICAL THICKNESS OF INSULATION
Q = (t1 – tair)/ [ 1/ ho .(4πr2 )2 + (r2 - r1)/ r1 r2 .4πK ]
On differentiation to get minimum denominator and maximum heat flow:
d/dr2 [ 1/ ho .(4πr2 )2 + (r2 - r1)/ r1 r2 .4πK ]= 0
d/dr2 [ 1/ ho .(r2 )2 + (1/K. r1 - 1/K. r2) ]= 0
1/ K. .(r2 )2 - 2/ ho (r2)3 = 0
(r2)3 .ho = 2 K . (r2 )2
Critical Radius, r2 = 2K/ ho

## Slide 7: CRITICAL THICKNESS OF INSULATION
Considering r2 as variable: d/dr2 [{ ln (r2/ r1 )/K + 1/ ho . r2 } = 0
1/k . 1/ r2 + 1/ ho(- 1/( r2)2 = 0
1/k - 1/ ho. R2 = 0
r2 (= rc ) = K/ ho

## Slide 8: Numericals on steam pipe without and with insulation
An aluminium pipe carries steam at 110°C. The pipe (K = 185 W/m. °C) has an inner diameter of 100 mm and outer diameter of 120 mm. The pipe is located in a room where the ambient air temperature is 30°C and the convective heat transfer coefficient between the pipe and air is 15 W/m2 °C. Determine the heat transfer rate per unit length of pipe without insulation.
To reduce the heat loss from the pipe, it is covered with a 50 mm thick layer of insulation (K = 0.20 W/m. °C). Determine the heat transfer rate per unit length from the insulated pipe. Assume that the convective resistance of the steam is negligible.

## Slide 9: Numericals on steam Pipes
Use the formula with convective coefficient on cold air side only: Case I- L = 1 meter, r1 = 0.05 m, r2 = 0.06 m
Q = 2π L (thf – tcf)/ [ln (r2/r1)/ KA + + 1/ hcf .r2] = 451.99 W/m
Case II- L = 1 meter, r1 = 0.05 m, r2 = 0.06 m and r3 = 0.11 m
Q = 2π L (thf – tcf)/ [ ln (r2/r1)/ KA + ln (r3/r2)/ KB + 1/ hcf .r3]
Q = 138.18 W/ m

## Slide 10
THANK YOU