## Slide 1: TYPE And standard OF MARKET MILK
Dr Sanjeev Kumar
Dairy Technology

## Slide 2: INTRODUCTION
Market milk refers to ‘fluid milk’ that is sold for direct consumption and thus excludes milk consumed on the farm and that used for the manufacture of dairy products.
The market milk industry in India was started in 1950-51 with the establishment of Central Dairy of Aarey Milk Colony.

## Slide 3: Types and standards of market milk
Class of milk | Designation | Locality | Minimum Percent | 
Mixed Milk | Raw, pasteurized, boiled, flavour and sterilized | All India | 4.5 | 8.5
Standardized Milk | Pasteurized, flavoured and sterilized | All India | 4.5 | 8.5
Recombined Milk | Pasteurized, flavoured and sterilized | All India | 3.0 | 8.5
Full Cream Milk | Pasteurized, and sterilized | All India | 6.0 | 9.0
Tonned Milk | Pasteurized, flavoured and sterilized | All India | 3.0 | 8.5
Double Tonned Milk | Pasteurized, flavoured and sterilized | All India | 1.5 | 9.0
Skimmed Milk | Raw, pasteurized, boiled, flavour and sterilized | All India | NMT 0.5 | 8.7
FSSAI, 2006

## Slide 4: Types and standards of market milk
Note: (i) When milk is offered for sale without indication of the class, the standards prescribed for buffalo milk shall apply.
(ii) The heat treatment for the various designated milk shall be as follows:
Designation | Heat Treatment
Raw | Nil
Pasteurized | Pasteurization
Boiled | Boiling
Flavoured | Pasteurization or sterilization
Sterilized | Sterilization

## Slide 5: Microbiological Standards of Market Milk
Requirements | Sampling Plan | Pasteurized Milk
Total Plate Count | m | 30,000/g
 | M | 50,000/g
Coliform Count | m | -
 | M | Less than 10/g
E. Coli | M | Absent/g
Salmonella | M | Absent/25g
Staph. aureus (coagulase positive) | m | -
 | M | Less than 10/g
Listeria monocytogenes | M | Absent/g
Where, m = represents an acceptable level and values above it are marginally acceptable in terms of the sampling plan.
M = separates marginally acceptable quality from unsatisfactory/potentially hazardous quality. Values above M are unacceptable in terms of sampling plan.

## Slide 6: Factors affecting Microbiological quality of Market milk
Raw milk quality
  Depends on number & types of microorganisms in raw milk.
  Inferior quality leads to inferior product and vice versa.
  Psychrotrophs (including heat stable
  lipases and proteases)
  Thermodurics & thermophilic
  Coliforms
  Toxigenic microflora
  So before proceeding, assess quality of raw milk by various platform and microbiological tests.
Subsequent spoilage and
public health problems in market milk

## Slide 7
2. Processing Steps
  Miscellaneous operations before and during processing significantly affects microbiological quality of product.
Steps before processing
  Pumping
    Increases bacterial count without increasing the actual number of bacteria due to mechanical breakage of bacterial clumps
    Improper cleaning and sanitization of pump adds to microflora.
  Filteration
    Microorganisms adhered to dirt particles on filter carried over to milk .
    Type of microflora depends on nature of particulate material.

## Slide 8
  Centrifugal separation
    Sludge material contains high amount of bacterial cells, somatic cells and coagulated proteins.
    Bacterial count is not reduced due to simultaneously breaking up of bacterial clumps.
    Increased removal of bacteria achieved by
      Slow milk flow
      Prior homogenization of milk( no sweeping effect)
  Standardization
    In line standardization- uses centrifugal force
    Offline standarization- by addition of skim milk, cream etc.
    Quality depends on quality of added products.
  Homogenization
    Break down of bacterial clumps
    Improperly cleaned & sanitized
Increases microbial load

## Slide 9
Steps after processing
  Pasteurization of milk
    Selection of time-temp. combination on basis of
      Destructiion of heat resistant pathogen
      Phosphatase test should be negative
      Cream line should be minimally reduced
    Different pasteurization process:
      LTLT process- 63°C/30 min
      HTST process- 72°C/15 sec
      Flash process- 75-80°C/ few sec
      In- bottle pasteurization
Pros of pasteurization | Cons of pasteurization
Destruction of pathogens and spoilage causing bacteria | Unable to inactivate heat stable enzymes and Staphycoccal toxins
Increases keeping quality | Reduction of cream line
Inactivation of phosphatase and lipase | Destruction of some vitamins and antimicrobial substances
Masking off-flavours | Rennet coagulation time increases

## Slide 10
  Sterilization of milk
    Complete in-bottle system:
      Heated in bottle at 110°-120°C for few minutes.
      Slow heat penetration --> growth of thermophiles, off-flavour and browning effect
    A two-stage process:
      1st stage --> sterilization at 130°-150°C/1-20 sec followed by bottling.
      2nd stage --> in-bottle treatment( 100°-110°C/10-15 min)
    Ultra high temperature(UHT) processing
      Rapidly heating milk to 130°-150°C for few seconds followed by aseptic packaging.
      Mode of heating may be direct or indirect.
      UHT treated milk must be kept without deterioration, free from microbes and toxins and microorganisms do not proliferate during storage.

## Slide 11
    Effects of UHT sterilization:
      Destruction of microorganisms/spores - Sterilizing efficiency of a UHT process is determined by “Sterilizing Effect”
      Survival of microbial enzymes – particularly heat stable lipases and proteases.
      Increases Keeping quality
      Influence on colour, taste and nutritive value of milk
Post-Heating Operations
  Cooling
    Rapidly cooled to below 10°C (preferably to 4-5 °C) after pasteurization.
    Part of cooling is done by regenerative principle and part by using refrigerant non-milk coolant.

## Slide 12
  Packaging
    Equipment for packaging
      Thoroughly cleaned and sanitized
      Condensate contamination can be prevented using drip deflectors
    Packaging materials
      Single service type paper or plastic containers are gaining popularity
      Should be non-toxic and microbiologically safe
      Glass container should contribute < 1 microorganism/ml & no coliform
    Closure equipment, materials and procedure
      Closure properly designed and handled
      Overfilling should be avoided
    Handling
      Properly handled to prevent small breaks in sterilized products
    Aseptic packaging of sterilized milk like UHT is of utmost importance
  Distribution/marketing
    In tropical countries like India, product should be kept under refrigeration temperature(7.2°C or below) to prevent multiplication of spoilage microorganisms while transporting market milk to retails shops and finally to consumers.

## Slide 13: Microflora of Market Milk
Microflora of Pasteurized milk
  Those surviving pasteurization temperature
  Those entering as post-pasteurization contaminants
  Thermoduric Microflora:-
Micrococci
M. luteus, M. candidus, M. caseolyticus
Associated with insanitation of equipments
Microbacterium
M. lacticum, M liquifaciens
Former one is most heat resistant non-sporeformer
Bacillus
B. subtilis, B. cereus, B. circulans, B. polymyxa etc.
These are aerobic sporeformers invariably present in past. Milk.
Streptococcus
S. thermophilus, S. faecalis, S .faecium
Increasing pH and substituting peptone for tryptone increses recovery of these bacteria
Lactobacillus
Others
Lb. bulgaricus, Lb. lactis
Fastidious, not encountered frequently in past. milk
Arthrobacter spp., Clostridium spp.,Streptomyces spp.

## Slide 14
  Sources of thermoduric organisms:
    Insanitary conditions of milking equipment
    Insanitary conditions of pasteurization plant( milk stone formation and improper cleaning of rubber parts)
    Repasteurization of returned pasteurized milk.
      Thermodurics start multiplying at warm stages during second pasteurization
  Significance:
    Due to temperature fluctuations, these organisms produce defects such as sweet curdling, gassiness, proteolysis, bitterness etc.
    Under refrigerated storage ,psychrotropic thermodurics like Bacillus and Clostridium spp.

## Slide 15
  Thermophilic microflora
    They grow well during holder method of pasteurization. Their upper limit for growth is 70°C.
    Types:- aerobic or facultative anaerobic sporeforming rods constitute majority of thermophilic microflora
      Lactobacillus thermophilus
      Bacillus spp. like
    Sources:
      Their count is less in raw milk which significantly increases during holding at high temperature
      This group represents dairy plant rather than farm contamination
B. stearothermophilus
B. thermoacidurans
B. calidolactis
B. coagulans
Repeated use of improperly cleaned hodling vats
Residual milk foam and warm milk in dead ends/vats
Repasteurization of returned milk
Increases thermophilic count

## Slide 16
  Significance:
    Under ambient condtions, sporeforming bacilli cause spoilage problems like sweet curdling or bitty cream defects in pasteurized milk.
  Psychrotrophic microflora:
    Grow at refrigerated temperature(2°-7°C) irrespective of their optimum growth temperature.
    Most of them are mesophiles, some are psychrophilic
    Types: divided into two categories
Psychrotrophic thermoduric bacteria
Gram-positive rods and cocci
e.g. Bacillus, Clostridium and Streptococcus.
Psychrotrophic bacteria
Gram-negative rods
e.g. Pseudomonas, Flavobacterium, Alkaligenes, Achromobacter, Acinetobacter

## Slide 17
    Sources:
      first category --> survival during pasteurization
      Second category --> post pasteurization contamination
      Water supplies may serve as a possible source.
    Significance:
      At referigerated storage(7.2°C or lower) --> gram-negative psychrotrophs outgrow
      At 10°C or above --> thermoduric psychrotrophs tend to outgrow
      Importance of gram-negative psychrotrophs --> cause number of defects like fruity, rancid, bitter , putrid, roppiness and discoloration etc.
      Minimum population required to produce defects are 107/ml

## Slide 18
  Coliform bacteria
    This group of organisms refer to aerobic and facultatively anaerobic, Gram-negative, non-sporeforming rods which ferment lactose into acid and gas at32°C within 48hrs in presence of bile salts and dye.
    Types: Escherichia, Enterobacter, Klebsiella and Citrobacter
    Source:
      Destroyed during pasteurization.
      Post-pasteurization contamination.
      Improper cleaning/sanitization
      Unhygienic handling practises
      Water supplies
Major sources of contamination

## Slide 19
    Significance:
      Unlike water supplies, where their detection is taken as index of faecal contamination, coliform detection in pasterurized milk is taken as index of post-pasteurizartion contamination.
      This group is usually traced to dairy plant.
      Above 7.2°C, they cause defects like roppiness, gassiness, unclean and medicinal off-flavours and bitterness.
  Pathogenic microorganisms
    That survive pasteurization --> B. cereus, Cl. Perfringens, haemolytic streptococci and some viruses
    Through post-pasteurization contamination --> dirty habits of handlers( E.coli, Salomella) or those carried by an unhealthy handler.
    L. monoctogenes and Y. enterocolitica can multiply even below 7.2°C but these species are heat labile.
    Improper storage of loose milk after such contamination is equally hazardous.

## Slide 20: Microflora of UHT milk
Ultra-high temperature is carried out at 135°-150°C coupled with aseptic packaging.
The only microflora survive UHT treatment are bacterial spore of thermophlic bacilli( B. stearothermophilus) and sometimes to mesophilic bacilli and clostridia.
Major spoilage organisms in heat processed milk are, B. megaterium( main cause), B. firmus, B. polymyxa, B. coagulans and Clostridium spp.
Microorganisms entering through faulty packaging practices are usually associated with stagnant water on dairy floors ( Pseudomonas, Coryneform, Micrococci etc).
Major defects --> coagulation, bitterness and gassiness.

## Slide 21: Microflora of Boiled Milk
In India, milk is boiled to 100°C for brief period before consumption.
Boiling kills vegetative forms of all microbes except heat stable enterotoxins esp. of Staphylococci.
Post pasteurization contamination can also occur due to improperly cleaned utensils and due to improperly heated portions of milk.
Major defects--> off-flavour (proteolytic), coagulation and gassiness.
Boiled milk should be utilized within 16 hrs, particularly in absence of refrigeration.