## Slide 1
Dr. Sanjeev Kumar
Associate Professor-cum-Senior Scientist
& Head Dept. of Dairy Technology
SGIDT, Patna
Chemical and biological methods of preservations
of milk

## Slide 2
INTRODUCTION
Milk is an easily perishable raw material.
Contaminating bacteria may multiply rapidly and render it unsuitable for processing and/or unfit for human consumption.
Bacterial growth can be retarded by refrigeration and/or heat treatment thereby slowing down the rate of deterioration.
Under certain conditions refrigeration may not be feasible due to economical and/or technical reasons.
In India milk is produced in small quantities (2-4) liters by approx. 70 million farmers spread around 5 lakh villages
Difficulties in applying refrigeration are specially a problem for certain areas in the country for setting up or expanding milk production.
In these situations, it would be beneficial to have access to a method, other than refrigeration, for retarding bacterial growth in raw milk during collection and transportation to the dairy processing plant.

## Slide 3
PRESERVATION OF MILK WITH H2O2
Initially some chemicals e.g., Mercuric chloride, Formalin, Potassium dichromate were tried
In 1967 the FAO/WHO Expert Panel on Milk Quality concluded that the use of hydrogen peroxide might be an acceptable alternative in the early stages of development of an organized dairy industry
H2O2 is a strong oxidizing, bleaching and germicidal agent
Concentration of H2O2 ranging between 0.02-0.50% resulted in preservation of milk for a very short period
Addition of H2O2 @ 1% (w/v) preserved freshness of raw milk upto 12-24 hours at room temperature
Storage of milk at 5°C extended upto 100days

## Slide 4
Preservative action of H2O2
Antimicrobial action of H2O2 is not due to it’s oxidative properties as a molecule
Production of other powerful oxidants e.g., singlet oxygen, superoxide radicals, and hydroxyl (OH) radical
The reactive oxygen species cause irreversible damage to a host of cell components such as enzymes, membrane constituents & DNA
OH– plays the largest role in the toxicity of H2O2
When produced adjacent to the DNA, OH radicals are unique in that they can both add to the DNA bases & abstract H-atoms from the DNA helix
OH radicals also damage cell membranes – by increasing lipid peroxidation as well and ion permeability
Effective against: S. aureus, E. Coli, Bacillus subtilis, A. Niger, C. parapsilosis

## Slide 5
Requirements of chemical preservative
No effect on organoleptic quality
No reaction with the milk constituents
Eliminated before consumption
No toxic effect

## Slide 6
Removal of residual H2O2
Could be removed by heat treatment or by addition of a catalase enzyme
Influence of H2O2 on milk flavour
High concentration impart ‘metallic’and/or ‘utensil’ flavour to milk
Milk containing high amount of undecomposed
H2O2 developed oxidized flavour

## Slide 7
Influence of H2O2 on proteins
In higher concentration H2O2 oxidizes proteins especially β- lactoglobulin, casein, and some enzymes e.g., pepsin, trypsin and chymotrypsin
Addition of H2O2 ≥ 0.02% reduce rennet coagulation properties and thus produce soft curd
H2O2 causes complete breakdown of β -lactoglobulin
Some essential and non-essential amino acids e.g., tyrosine, tryptophan, cysteine, cystine, lysine and methionine are very sensitive to H2O2
Influence of H2O2 on fat
It increases the oxidative rancidity of fat rich dairy products

## Slide 8
Other Issues of using H2O2
Difficulty of controlling its use
It may be misused to disguise milk of basic hygienic quality produced under poor hygienic conditions.
The toxicological aspects of the use of relatively high concentrations of hydrogen peroxide in milk have also been questioned.

## Slide 9
THANKs