## Slide 1
Homogenization
Dr. Sanjeev Kumar
Associate Professor-cum-Senior Scientist
Dept. of Dairy Technology
SGIDT, Patna

## Slide 2
Why Homogenization?
Vg = velocity
g = force of gravity
p = particle diameter
ρhp = density of the liquid
ρlp = density of the particle
t = viscosity

## Slide 3
Homogenization
Homogenization was invented by a French named :
Gaulin, in 1899 described it in French as “fixer la composition des liquides”.
Homogenization primarily causes disruption of fat globules into much smaller ones
The homogenisation reduces fat globule size from an average of 3.5 μm in diameter to below 1 μm, this is accompanied by a four- to six- fold increase in the fat/plasma interfacial surface area.

## Slide 4
Homogenization
The newly created fat globules are no longer completely covered with the original membrane material. Instead, they are surfaced with a mixture of proteins adsorbed from the plasma phase.
Casein is the protein half of the complex and it is associated with the fat fraction through polar bonding forces.
The casein micelle is activated at the moment it passed through the valve of the homogeniser, predisposing it to interaction with the lipid phase.

## Slide 5
Process requirements
The physical state and concentration of the fat phase contribute most
Homogenisation below 40 °C results in incomplete dispersion of the fat phase.
Products of high fat content are more difficult to homogenise & also more likely to show evidence of fat clumping.
Increasing the homogenisation temperature decreases the visocity of milk & improves the transport of membrane material to the fat globules.
Homogenisation : Temp 55 – 80 °C & pressure is between 10 and 25 MPa (100 – 250 bar)

## Slide 6
Flow characteristics
When the liquid passes the narrow gap, the flow velocity increases The speed will increase until the static pressure is so low that the liquid starts to boil
The maximum speed depends mainly on the inlet (homogenization) pressure
When the liquid leaves the gap,
the speed decreases and the pressure increases again. The liquid stops boiling and the steam bubbles implode
The Homogenization Valve

## Slide 7
Homogenisation theories
The theory of globule disruption by turbulent eddies (“micro whirls”):
  A lot of small eddies are created in a liquid travelling at a high velocity.
  If an eddy hits an oil droplet of its own size, the droplet will break up.
  Higher velocity gives smaller eddies.
  This theory predicts how the homogenising effect varies with the homogenising pressure. This relation has been shown in many investigations.

## Slide 8
Homogenisation theories
The cavitation theory
  Shock waves are created when the steam bubbles implode disrupt the fat droplets.
  Homogenisation takes place when the liquid is leaving the gap, so the back pressure which is important to control the cavitation is important to homogenisation. This has also been shown in practice.
  However, it is possible to homogenise without cavitation, but it is less efficient.

## Slide 9
The homogeniser
A high pressure homogeniser is basically a pump with homogenization device (valve)

## Slide 10
Single-stage and two-stage homogenisation
Homogenisers may be equipped with one homogenising device or two connected in series
In two-stage homogenisation the back pressure (P2) is created by the second stage.
Using modern devices, the best results are obtained when the relation P2/P1 is about 0.2
The second stage also reduces noise and vibrations in the outlet pipe.

## Slide 11
Two-stage homogenisation is used primarily to reach optimal homogenisation results and to break up fat clusters in products with a high fat content.
Disruption of fat globules In first & second stages of Homogenization
Single-stage and two-stage homogenisation
Single-stage homogenisation may be used for homogenisation of products with high fat content demanding a high viscosity (certain cluster formation)

## Slide 12
Effect of homogenisation
Smaller fat globules leading to less cream-line formation
Whiter and more appetizing colour
Reduced sensitivity to fat oxidation
More full-bodied flavour, and better mouthfeel
Better stability of cultured milk products Disadvantages
Somewhat increased sensitivity to light – sunlight and fluorescent tubes – can result in “sunlight flavour”
The milk might be less suitable for production of semi-hard or hard cheeses because the coagulum will be too soft and difficult to dewater

## Slide 13
The homogenization valve
The distance between the seat and the forcer is approximately
0.1 mm or 100 times the size of the fat globules in homogenised milk.
The velocity of the liquid is normally 100 – 400 m/s in the narrow annular gap.
The higher the homogenisation pressure, the higher the speed.
Homogenisation takes 10 – 15 microseconds.

## Slide 14
The homogenization valve
The piston pump boosts the pressure of the milk from about 300 kPa (3 bar) at the inlet to a homogenization pressure of 10 – 25 MPa (100 – 250 bar)
The oil pressure on the hydraulic piston and the homogenisation pressure on the forcer balance each other.
The hydraulic unit can supply both first and second stage with an individually set pressure. The homogenization pressure is set by adjusting the oil pressure
Homogenization always takes place in the first stage. Second stage basically serves two purposes:
  Supplying a constant and controlled back-pressure to the first stage, giving best possible conditions for homogenization
  Breaking up clusters formed directly after homogenization as shown in

## Slide 15
Transmission electron micrograph of milk fat globules
16000X
Bar = 500nm
66000X
Bar = 200nm
Non-homogenized
26000X
Bar = 5000nm
Homogenized

## Slide 16
Merits of Homogenization
No formation of cream layer/plug
Fat will not churn
Thick body and rich appearance
Produces soft curd, easily digestible
Less susceptibility to oxidation
Demerits Increased cost of production
Fat from returned homogenized milk is difficult to salvage.
Sediment is greater
May produce rancidity if temperature is not kept adequately high.

## Slide 17
Product specific purposes of Homogenization
Market milk - creaming of fat is avoided & taste improvement is achieved
Coffee cream, evaporated milk - avoids creaming & improved the whitening power in coffee
Cheese milk - enhances the biochemical fat degradation especially in mould ripened cheeses
Acidified dairy products - improvement in consistency & taste, more stable acid gel and reduced whey syneresis
Milk mix beverages – improving body, good distribution of stabilizer & additives
Ice cream mix – reduced buttering of fat during freezing process

## Slide 18
Factors Affecting Homogenization
Homogenization pressure
two-stage homogenization is needed
to prevent fat clustering pressure of
140 bar (2000 psi) and 35 bar (500
psi) in the first and second stage
respectively are applied in two-stage
homogenization.
Stage of homogenization
milk with more than 6% fat,
twostage homogenization is better.
Temperature of homogenization
enzyme lipase should be inactivated prior to homogenization by pre-heating milk to a temperature of 60°C or above.
Efficiency of Homogenization
Degree of homogenization defined as - ratio of the volume of fat with fat globules diameter of < 0.7 µ to the total fat content of milk or cream.
The value of 0.7 µ was based on the fact that fat globules with smaller diameter- do not form clumps because they break up again due to Brownian movements.
Farrall index It is a widely accepted microscopic method - determining the homogenization efficiency.
This index may be defined as the number of fat globules having < 2 µ in diameter.
The efficiency of homogenization is apparently based on the number of fat globules larger than 2 µ (if any), as measured under specified conditions.

## Slide 19
Homogenizer in the processing line
In general, the homogenizer is placed upstream, i.e. before the final heating section in a heat exchanger. In most pasteurization plants for market milk production, the homogenizer is usually placed after the second regenerative section
In production of UHT milk, the homogenizer is generally placed upstream in indirect systems but always downstream in direct systems, i.e. on the aseptic side after UHT treatment. In the latter case, the homogenizer is of aseptic design

## Slide 20
Factors affecting the fat globule size
Homogenization pressure
Stages of homogenization
Fat content & ratio of amount of surfactant (usually protein) to amount of fat
Temperature
Proper operation of the homogenizer

## Slide 21
Homogenisation efficiency
1. Size distribution analysis
Size distribution curve

## Slide 22
Homogenisation efficiency
2. Studies of the creaming rate
1 000 ml is stored for 48 hours, after which the fat content of the top 100 ml is determined, as well as the fat content of the rest. Homogenization is reckoned to be sufficient if 0.9 times the top fat content is less than the bottom fat content
Creaming index by centrifugal method: 50 ml of milk is centrifuged at 1000 rpm/5 min in 3 sets. Top 5 ml milk is separated and fat content determined for both the fractions :
Creaming index = (A-B)/B x 100, A = fat% of top, B = fat% of bottom
Quality of homogenization: Excellent up to 10, Good 11- 20, Fair 21-30 & Bad over 30

## Slide 23
Homogenisation efficiency
3. Farrall index: efficiency in excellent when upon microscopic examination 90% of the fat globules has average diameter ≤ 2μ

## Slide 24
Overall effect of Homogenization
Reduction of size of the fat globules accompanied by four- to six-fold increase in the fat/plasma interfacial surface area
Creation of new MFGMs and adsorption of disrupted casein micelles on the new MFGMs
Slight increase in viscosity
Increased foaming properties
Increased digestibility
Whiter and more appetizing colour
More full-bodied flavour, and better mouthfeel
Reduction in heat stability
Increased in foaming properties
Somewhat increased sensitivity to light – sunlight and fluorescent tubes – can result in “sunlight flavour”