## Slide 1: Dairy Waste Management
BY
Dr. J. Badshah
University Professor-cum-Chief Scientist, Dairy Engineering Department

## Slide 2: Waste Management in Dairy Industry
Introduction
Types of Waste water in Dairy and Food Processing Plants
Depending on the Forms of wastes
  Solid Waste
  Liquid Waste
  Oily Waste
  Gaseous Wastes/Water Vapours

## Slide 3: Waste Depending on the sources
Depending on the Sources
  Manual Cleaning of storage tanks and equipments
  Floor/drainage cleaning
  CIP Cleaning of Equipments
  Wastes from utilities like water tanks, Boilers & Refrigeration systems
  Wastes from workshops, offices and gardens etc.
  Wastes from laboratories and packaging sections
  Unavoidable wastes from Heat exchnagers, drum dryers, spray dryers, condensers, compressors etc.

## Slide 4: Waste Management in Dairy Industry: Avoidable Losses
Depending on Avoidable or Unavoidable Losses
Avoidable Losses : Deliberate discharge of unwanted materials such as milk, whey, waste water, solid powders etc.
  Leaking valves, pipes and joints etc.
  Overflows and spills
  Leakages and spills during processing, handling and storage
  Losses due to not using hot water (<65°C) for viscous and sticky products such as cream, butter, ghee etc. for cleaning and recovery.

## Slide 5: Waste Management in Dairy Industry : Unavoidable Losses
Unavoidable Losses
  Entrainment Losses in evaporators
  Stack losses in spray dryers
  Surface deposits in Heat exchangers and drum dryers
Ways to prevent unavoidable losses and enhancing efficiencies
  Control of levels of milk in vapour separators
  Control of atomization and spray drying process to reduce stack losses and to use powder recovery efficient systems such as wet scrubbers, bag filters and collecting chamber etc.
  Use of proper CIP cycle in processing equipments to avoid surface deposits & milk stones
  Use of proper flow rates and temperature of steam condensation

## Slide 6: Wastes depending upon reuse potentials
  Losses due to making predominant by-products into low value animal feed/fertilizer or dumping as waste. Rather it should be benefited by converting into value added products.
  Whey to value added products such as whey poder, whey protein concentrate and whey drinks etc.
  Butter milk to butter milk powder or butter milk salted drinks
  Skim milk to skim milk powder or UF protein concentrate and lactose recovery.

## Slide 7: Waste Minimization and recycle systems
Solid waste reduction in all processes
  Stack losses of minute powder particles
  Solid ghee residues
  Film (LDPE) losses in packaging section
  Ash from boiler if solid fuel is used
  Waste generated by adverse events such as explosions, fire in uncontrolled processes and damaged and nonfunctional equipments/machineries.
  Liquid waste reductions in CIP, Manual cleaning and use of water
  Recycling water and chemicals
  Recovery and reuse of cleaning solution from first use
  Recovery and reuse of spilled raw materials, off-spec materials and products.

## Slide 8: Instrumentations, Process Controls & Automations
Losses depending upon the design, configuration and range of manufacturing technologies in use and their thermal and handling efficiencies.
Losses due to low efficiencies of process monitoring, recording and control system
Losses due to non availability of plant operation and procedures interlock /alarms to enhance efficiencies
The non availability/non functionality of automated operation in CIP systems, Dryers, Pasteurizers plants
Improper training and awareness of operator or poor commitment and efficiency of operator and laborers
Improper routine and preventive maintenance
Improper inventory maintenance
Lack of managerial and leadership qualities to control automations and instrumentations as per the tune of running cycles of equipments