## Slide 1: BUTTERMILK
Department- Dairy Technology
Semester-5th
Course-By Product Technology
Teacher- Bipin Kumar Singh

## Slide 2: Introduction
Buttermilk is an important by-product obtained during manufacture of butter. In addition, a substantial amount of lassi (sour buttermilk) is also produced during the manufacture of makkhan directly from fermented milk (curd).

## Slide 3: Types of Buttermilk
Sweet cream buttermilk
b) Sour buttermilk
c) Desi buttermilk (lassi)

## Slide 4: Average gross composition and physico-chemical properties of sweet cream buttermilk (obtained from buffalo milk)
Characteristics | Butter Milk
TS(%) | 9.88
Fat(%) | 0.59
Total Protein(%) | 3.73
Lactose(%) | 4.81
Ash(%) | 0.75
Total Paspholipids(mg%) | 78.56
Titratable acidity(%LA) | 0.12
pH | 6.86
Curd Tension(g) | 18.84
Relative viscosity(cP at 30°C) | 1.84

## Slide 5: Difference between sweet cream buttermilk and skim milk
Particular | Butter milk | Skim milk
Fat | more | less
Protein mixture | more | less
Phospholipids | Do not have short chain fatty acid | Both are present
Physica –chemico properties are also varying(Above Table) |  | 

## Slide 6: How To Make Buttermilk
Standardization of Milk- Heat Treatment –
Cooling - Inoculation - Incubation - Cooling,
Agitation and Dilution - Packaging & Storage

## Slide 7: Utilization of Sweet Cream Buttermilk
Sweet cream buttermilk, because of its resemblance in gross chemical composition with skim milk, is usually admixed with bulk of skim milk for further spray drying or even products manufacture in dairy plants.
Sweet cream buttermilk can be used in beverage form and in the fluid milk industry as a milk extender with specific benefits over skim milk.

## Slide 8: Utilization of Desi Buttermilk
Desi buttermilk also known as chhanch makes an excellent drink, especially in warm weather. Chhanch is an important domestic beverage in India. It can be flavored in various ways with salt, mint, cumin, and even spicy additions such as ground chilies, fresh ginger or garlic. It is considered to be an excellent thirst quenching and nourishing beverage.

## Slide 9: Utilization of Sour Buttermilk
Sour buttermilk obtained from first category is not preferred for human consumption. This may, however, be converted into casein by adopting modified processing conditions for other uses. A process has been standardized for the manufacture of paneer from the mixture of buffalo milk and sour buttermilk.

## Slide 10: Utilization of Buttermilk Powder
Buttermilk powder can replace partly skim milk powder for incorporation into baked goods, ice cream, Pudding, sauces, beverages and chocolates.