## Slide 1
Sources and characteristics of water

## Slide 2
Water
Water supply and sanitation scheme:
  Improved health
  One of the most effective and permanent way to improve human health
Without safe community water supply there can not be a status of positive health
With the supply of safe water, there is drastic decline in disease burden of community
Provision of safe community water supply is one of the MOST effective & permanent health technologies to improve and maintain public health

## Slide 3
Use:
  Domestic: Drinking, cooking
  Public: Garden, swimming pool, Fire fighting
  Industrial: Iron, paper, food
  Agricultural: Irrigation
  Power generation
  Waste management
Therefore, essential for
  Economic
  Social
  Cultural development
Water is required for a number of daily activities

## Slide 4
Water Requirement:
  2 liter/person/day: mere survival
  Adequate H2O must be supplied
  150-200 liters (35-40 gallons) /person/day
Consumption depends on:
  Climate
  Standard of living
  Personal habits

## Slide 5: Sources of water
Rain H2O
Surface H2O
  Impounding reservoir
  Rivers, Streams
  Tanks, Ponds, Lakes
Ground H2O
  Shallow well
  Deep well
  Springs

## Slide 6
Criteria
Quality : Acceptable
Quantity : Must meet 95% of annual need
        Present
        Future

## Slide 7
1.1 billion lack access to "improved" drinking water supply
4 billion cases of diarrhoea annually, 88% attributable to unsafe water
1.8 million die each year from diarrhoeal diseases, vast majority being children under5
Lack of safe water perpetuates poverty
WHO says 94% of diarrhoeal cases preventable through environmental modifications
Unsafe Water, Inadequate Sanitation and Hygiene

## Slide 10
Water cycle:
  Ground water
  Evaporation
  Run off Streams, rivers Sea
  Uptake by vegetation
“Prime” source but not important in our country
Rain

## Slide 11
Purest H2O in nature
Physically: clear, bright, sparkling
Chemically: Very soft with traces of
  dissolved solid (0.0005%)
  Bacteriologically: Free from pathogens
Characteristics of Rain Water
Impurities:
  Suspended particles: Dust, shoot, microbes
  Gases: CO2, N, O2 NH3

## Slide 12
  Mostly rain water
  Majority of Indian cities use it
  High probability of contamination
    Inorganic
    Organic
    Bacterial
    Viral
Surface water
  Impounding reservoir
  Rivers, Streams
  Tanks, Ponds, Lakes

## Slide 13
  Artificial lakes generally Earth work or massonary work for storage of large quantity of surface water
  Dams across
    Rivers
    Mountain streams
Impounding reservoir
Disadvantages:
Longer storage
Growth of algae and other microscopic organisms
Bad taste odour

## Slide 14
Characteristics:
  Usually fairly good quality H2O
  H2O clear and palatable
  Next to rain H2O in purity
  Usually soft H2O
  Usually free of pathogens
Impurities:
From Catchment areas
      Human habitation
      Animal husbandry grazing
      Wild animals
The belief that H2O from mountain streams are pure,
is not always true

## Slide 15
Dependable H2O supply of source
  Grossly polluted
  Unfit for drinking without treatment
Rivers
Characteristics:
  Turbid during rainy season
  Contains dissolved and suspended impurities
  Bacterial counts may be very high

## Slide 16
Direct connection between
Customs/Habits:
    Bathing
    Washing  Cloths
     Animals
    Disposal of dead
Impurities
Alimentary canal and mouth
of people
living up and downstream

## Slide 17
Dilution
Sedimentation
Aeration
Oxidation
Plant life
Animal life
Sunlight
Natural purification

## Slide 18
Important source of water in many villages
Large excavations to store ground H2O
Receives contaminants of all types
Increase amount of silt and colloidal matter
Older tanks may have vegetation (aquatic plants)
Tanks
Liable to unlimited possibility of contamination
Highly Dangerous

## Slide 19
Natural purification not adequate
Elevated edges
Fencing: to check animal access
Platform: to take out H2O
Restricted entry
Weed removal
Cleaning: Specially at the end of dry season
Improvements
Even then, pollution prevention remains a practical problem

## Slide 20
Plentiful source
Limitations: 3.5% salts in solution
Off shore water of Ocean & sea have salt conc.
  30000 to 36000mg/lit of dissolved solid
    19000 mg/lit of chloride
    10600mg/lit of Na
    1270 mg/lit of Mg
Sea Water
Desalting and Demineralization--- Heavy expenditure

## Slide 21
Superior to surface H2O
Ground water
Cheapest and most practical
Likely to be free of pathogenic agents
Usually requires no treatment
Assured supply
Less amenable to contamination
Advantages
High in mineral content:
Hardness Mg/Ca
Requires pumping
Disadvantages
  Shallow well
  Deep well
  Springs

## Slide 22
source of H2O in
Indian villages
Primary
Wells
Shallow well
Deep well
Chem:
Quality
Above first impervious layer
Taps H2O From
Definition:
Moderately hard
Bact: Grossly polluted
Yield: Dries during summer
Purer
Below first impervious layer
Much hard
Continuous supply
Definition:
Taps H2O From
Quality

## Slide 23
Latrines
Urinals
Drains
Cesspools
Soakage pits
Manure collection
Potential health hazards since liable to pollution
Indian wells are Mostly shallow

## Slide 24
Porous Strata
Porous Strata
Deep
Well
Non-Porous Strata
Non-Porous Strata
Shallow
Well
…………………………………………………………………………………………………………
…………………………
…………………………………………………………………………………………………………
…………………………
…………………………………………………………………………………………………………
…………………………………………………………………………………………………………
…………………………………………………………………………………………………………
………………………………………………………………………………………………
………………………………………………………………………………
……………………………………………………………………………………………………………………………………………………………………………….
………………………………………………………………………………………
Porous Strata

## Slide 25
held under pressure
Water comes to surface on to its own
Not common in India
Artesian wells
Saline Intrusion

## Slide 26
Step wells: Now obsolete
Dug wells
Most common
Pacca
Katcha
Katcha wells
  Deepening of bottom
  Hand pump
  Fill with sand upto water
  level and clay above that
  Platform for drainage
Pucca wells
  Upper 10 feet or > pucca
  Hand pump
  Raise lining above ground
  at least one feet
  Concrete slab as cover
Improvements
/ Masonary

## Slide 27
Properly located
Well constructed
Protected against pollution
Provides again safe water
Sanitary wells

## Slide 28
i. Location:
  15 mts (50ft) sources of pollution
  Elevation
  100 mts from house
ii. Lining:
  6 mts (20ft) 
  2’-3’ above ground

## Slide 29
vi. Covering:
  To cover top of well ‘’ Bacteriological quality
  Open well is not a sanitary well
iii. Parapet:
  At least 70-75 cms above ground
  Concrete
iv. Platform:
  Atleast ‘1 mt’ around well with outward slope
v. Drain
  Outside cone of filtration (Drainage area)

## Slide 30
vii. Hand pump:
  Robust to withstand rough handling
   H2O Quality : Bacteriological
viii. Consumer responsibility
ix. Quality: Improved
  Physical
  Chemical and
  Bacteriological

## Slide 31
SUCCESSFUL
  Bacteriological safe
  Cheap
Deep
Costly but good
with  yield
No dependence
on rain fall
Successive layers of rocks
Shallow
Largest source of H2O in rural areas
Area within 15 mts must be pollution free
Water bearing stratum
Tube wells

## Slide 32
Shallow, Deep, Mineral, Thermal
Liable to gross pollution
Yield is too low for use as a source of
community H2O supply
Springs
Topography
Not important source

## Slide 33: Reference book
1. Park’s Textbook of Preventive and Social Medicine, 24th Edition
By: K. Park, Banarsidas Bhanot Publishers.