## Slide 1: SETTING UP OF TESTING FACILITIES AND ANALYTICAL LABORATORIES, CONCEPT OF MOBILE TESTING LABORATORIES

## Slide 2
Types of dairy laboratories (According to BIS  5 types) :
Category A - 1 lakh liters or more of milk per day.
2) Category B - 25,000 litres or more of milk per day, but less than 1 lakh litres.
3) Category C - 10,000 liters of milk or more per day, but less than 25,000 liters.
4) Category D - 5,000 liters of milk or more per day, but less than 10,000 liters.
5) Category E - less than 5,000 liters per day.

## Slide 3
Location of QC lab in a dairy:
should not be at a remote place from the dairy operations.
should not be very close to the dairy operations where there can be lot of noise, vibrations, steam etc.
should preferably be away from boiler houses.
should be easily accessible for all the major activities of the dairy.

## Slide 4
Layout / design of the laboratory:
adequate number of rooms/chambers and benches etc of suitable dimensions.
possible expansion of the dairy should be kept in view.
minimum of 2 exits.
BIS has given two alternate layout plans.

## Slide 5
General requirements for a QC lab :
Walls - smoothly finished - glazed tiles - wash up room and platform - Gerber test is conducted.
2) Windows - sufficient number - glass panes - to receive adequate
natural light.
3) Lighting –
i) Natural day light.
ii) Northern or east - northern - exposure is preferred - color matching.
iii) Lights - minimum average intensity of 400 to 450 lumen/m2 at
working level.
iv) Direct sun light should be avoided - sensitive instruments (e.g.
Chemical balance)
v) Roof light - helpful.

## Slide 6
4) Flooring - non- slippery and cleaned easily.
5) Store room - two :
1. acids, alkalies , ammonia
2. fine chemicals, glassware, apparatus and equipment.
6) Benches - several designs/sizes - examples :
150 x 75 x 90 cm
220 x 75 x 90 cm
360 x 67.5 x 90 cm
150 x 75 x 75 cm
210 x 75 x 75 cm
Any convenient size can be used.

## Slide 7
Bench top - resistant to acid and alkali
A. Above bench fittings - Shelves  keep various solutions, chemicals, reagent bottles, glassware etc.
B. Under Bench fittings - Drawers and cupboard with shelf accommodation  could be of fixed or removable type and inter changeable.
7) Cupboards - adequate number.
wall cupboards preferred  provide space for storing without occupying the floor space.

## Slide 8
8) Sinks
suitable dimensions in wash-up rooms  glazed earthenware or vitreous ware or stainless steel. Preferable dimensions  75 x 45 x 25 cm.
B. Service bench or laboratory bench or working bench should be fitted beneath the bench top  porcelain or other suitable material  Dimensions are 45 x 30 x 20 cm.
9) Fume cupboard/ fume hood/fume chamber - efficient means of removing objectionable fumes, gases, vapors etc for carrying out operations which cause fumes etc.  Fume chambers should have the provision for gas, water, waste outlet and electricity.

## Slide 9
10) Water supply - There should be adequate water supply.
11) Distilled water plant - of adequate capacity should be available in each lab .
Fume hood

## Slide 10
(c) Quartz Distillation Assembly
(a) Metal Distillation Assembly
(b) Glass Distillation Assembly

## Slide 11
12) Gas - provision of gas supply  in the form of own gas supply, in the form of own gas plant or portable gas supply.
13) Electric supply - electric supply, electric points for water bath, heaters, oven etc.
14) Service lines (of water, gas & electric power) - tap water, electric power and gas, should run along the walls, concealed 80 cm above floor level and connection taken to the laboratory benches.
While installing service lines, two main points should be kept in mind:
Benches should be easily removable.
Service lines should be easily accessible.

## Slide 12
15) Drainage
16) Fire-extinguishers
17) Ventilation
18) Air-Conditioners
19) Chemicals, glassware & Consumable Stores
20) Equipments

## Slide 13
List of equipments ordinarily required in QC lab
Mojonnier apparatus, water baths
Hot air oven, Hot plates
Analytical balances, Desiccators
Colorimeter / Spectrophotometer
Nitrogen digestion / distillation apparatus

## Slide 14
Glass distillation apparatus
Refrigerator, BOD incubator
Microscope, Autoclaves
Milko tester / Milko scan
Gerber fat testing centrifuge
Automatic measure for Gerber acid and iso - amyl alcohol

## Slide 15
Butyro - refractometer with circulating water bath
Polarimeter
pH meter, Viscometer
Pro-milk, Infra-red Moisture tester
General purpose centrifuge
Solubility index apparatus

## Slide 16
Special Requirements for specific purposes
1. Fat Test
white tiled platform of suitable dimension
2. Wash-up Room
3 sink units with draining board & draining rack.
3. Balance Room
least affected by vibrations.
4. Doors
self closing.

## Slide 17
5. Bacteriological Room
dust-free and air- conditioned.
6. Drains
made of an acid-proof material.
the volume of discharge should be taken into account.
should be provided with suitable traps at suitable places to prevent blockage of drains.
7. rooms meant for analytical work in the laboratory should be fly-proof and rodent proof.

## Slide 18
Various chemical tests ordinarily conducted in a dairy laboratory
Organoleptic test
Sediment test
Alcohol test
COB test
Acidity
Fat
SNF
Freezing point determination
Adulterants
Preservatives

## Slide 19
11. Neutralizers
12. Phosphatase test
13. Hardness of water
14. Available chlorine (Cl2)
15. pH
16. Turbidity test
17. Salt (NaCl) purity
18. BR at 40°C
19. Reichert–Meissl value (RM) and Polenske value (PV)
20. Acid value
21. Sugar / lactose
22. Over-run (weight per liter)
23. Strength of alkali / acid etc.

## Slide 20
Mobile Testing Laboratories
integrated analytical platform equipped with state-of–the–art measurement systems - to detect, analyze and confirm the chemical and biological adulterants/contaminants in food, water, milk etc.
Lab for the detection of food adulteration - rapid chemical and microbiological tests in particular - should have proper safety features - fabricated on a specially modified mobile platform like heavy duty trucks.
FSSAI  setup the mobile testing laboratories - expected to be positioned at various locations in the country.

## Slide 21
Mobile Testing

## Slide 22
Objectives of Mobile Testing Laboratory
To take  food testing - door steps of the consumers and others.
i) Visit the local markets, households, restaurants, godowns, schools and other public places, conduct tests on the spot and declare the result  thereby creating awareness among people and also furnish feedback to the food safety authorities.
ii) Collection of information by means of testing and preparation of a data base, useful in  maintaining surveillance and could also be utilized by the Food Safety Officers, Laboratories and others involved in Food Safety regulation.

## Slide 23
Design of the Laboratory
laminated panels with excellent insulation properties.
External dimensions - type and kind of testing to be carried out in a particular laboratory.
Container is designed in such a manner that it can be lifted by both crane, truck with container hoist and can be transported by truck, ship, train and aeroplane.
Laboratory  two portions internally by a sliding door.

## Slide 24
One half of the laboratory - the preparation of samples and the other functions  measurement laboratory where instrumentation can be located.
platform includes both rear and side entry doors with dual pan windows.
adequate number of generators most likely two numbers one on each side of the platform.
filtered fresh air intakes and exhaust vents with HEPA (High Efficiency Particulate Air) filters to avoid contamination of environment.

## Slide 25
A basic mobile laboratory should have the following features:
1. Mobile laboratory
At least 20 ft. container  laminated aluminium panels. Ext. dimensions: 606 x 244 x 244 cm.
connection to external power supply (230 - 400 V).
connection to  external water supplies, air conditioning and internal climate control for operation in adverse weather conditions.
Separate air conditioning and ventilation systems.
Built in diesel generator for power supply in the event of power cuts.
Fume hood, refrigerator/freezer/microwave.
Lines for telephony, data, internet, e-mail.

## Slide 26
equipment
Equipments

## Slide 27
2. Equipment
Type of equipment depends upon  kind of testing to be performed.
The possible equipments :
Sampling equipment and containers.
Milko tester/Milk analyzer
Ovens, Incubators.
Gerber Centrifuge and clinical centrifuge.
Rapid chemical testing kit.
Rapid microbiological testing kits
Biosensor based tests for antibiotics etc.
Lactometers,
Computers (PC’s), Printer
Protective equipment

## Slide 28
THANKS