## Slide 1: CASEIN
Department- Dairy Technology
Semester-5th
Course-By Product Technology
Teacher- Bipin Kumar Singh

## Slide 2: Introduction
Casein (/ˈkeɪsiːn/ KAY-see-n, from Latin caseus "cheese") is a family of related phosphoproteins (αS1, αS2, β, κ). These proteins are commonly found in mammalian milk, comprising c. 80% of the proteins in cow's milk and between 20% to 45% of the proteins in human milk.

## Slide 3: Classification
Classification based on coagulant:
Acid casein, Rennet casein,
Classification based on use
Edible casein or industrial casein.

## Slide 4: FSSAI (2011) compositional standards for Edible Casein

## Slide 5: Properties
Acid Casein:
Cow- yellowish white
Buffalo-Chalky white
Taste-Slightly acid
Rennet Casein:
Cow-Yellowish
Buffalo-Whitish
Tasteless

## Slide 6: EDIBLE ACID CASEIN MANUFACTURE
SM--Preheating(40-45°C)--Separation--Pasteurisation--Cooling-- Precipitation with Acid(35-38°C)--Drainage of whey--Thrice Washing with water(32-40°C,Ph-4.6)--Pressing(12-15hrs,34kg/cm²)-- Milling(Overnight)-- Drying(Inlet-71-77C,Outlet-52-57C)--Tempering--Grinding(30,60,90 Mess size)--Bagging-- Storage

## Slide 7: Uses
Acid Casein: Plastic, Button, Costume, Jewellery, Umbrella handle
Rennet casein: Adhesive, Paper coating, Paint, Films, leather finish and Textiles