## Slide 1: Plant/abattoir sanitation

## Slide 2: Reasons for cleaning and disinfection
To meet national and international standards
To reduce the risk of litigation
To engender & maintain a general quality ethos
To meet consumers quality expectations
To satisfy the increasing number of customer hygiene audits
To allow maximum plant productivity
To ensure the safety of operatives & maintenance staff
To help secure the shelf life of the product
To avoid food poisoning & foreign body contamination
To avoid pest infestation

## Slide 3: Scotoma/ factory blindness
Any person working routinely in an environment such as meat plant can gradually become mentally blind to hygiene standards and potential problems in their plant
Scotoma can be overcome by: vigilance, training & systemic monitoring & inspection procedures

## Slide 4: The soils or deposits
Fats, oils and greases: Triglyceroids of fatty acids
  Vary from waxy solids to liquid
  Insoluble in water
  Vary in their structure & properties:
    A. different part of same animal species
    B. different species
Proteins
Carbohydrates and starches

## Slide 5: The soils or deposits
Proteins: Complex, large molecule
  Large to dissolve in water
  Bile protein & gut based protein deposits on the evisceration equipment's
  Green & yellow tenacious deposits
  Pig dehairing equipment’s: heavy hard proteins deposits
  Blood protein: green/brown resistant staining

## Slide 6: The soils or deposits
Carbohydrates and starches: large molecule
  May be insoluble
  Carbohydrates and starches: large molecule
  Deposits may vary from soft & powdery to quite hard
Other deposits:
  Water surface corrosion
  Vehicles
  Outside materials

## Slide 7: The substrate: materials of construction
Many different material may be found
None is perfect
Vary very considerably in their ease of cleaning & resistance to corrosion
Smooth, non-porous, abrasion resistant, inert surfaces are ideal
  Stainless steel
  Zinc
  Terrazzo & concrete
  Plastic & rubbers

## Slide 8: Energies of cleaning
Thermal energy:
  Hot water & steam, doubles the rate of chemical reaction
Mechanical energy
  Brushes, water jets, turbulent flow in pipes
Chemical energy
  Nature & concentration of detergent used
Time
  Seconds to hours

## Slide 9: Detergent: design & choice
Design of detergent may be complex as the complexity of soil
Different component need to be employed:
  Alkali: caustic soda, caustic potash, carbonate, silicate, phosphate
  Acids: phosphoric, nitric, citric, glycolic, sulphamic, hydrochloric:
  Chelating agents: EDTA, NTA, gluconate, glucoheptonate, citrate, polymeric
  Solvents: isopropanol, propylene glycol, butyle diglycol, eathers
  Surfactants: anionic, cationic, nonionic, amphoteric
  Inhibitors: organic, inorganic
  Enzymes: proteases, amylase, lipase
  Oxidising agents: hypochlorite, isocyanurates
  Stabilizers
  Viscosity modifiers

## Slide 10: Ideal detergent
Prevent scale formation in hard water
Ensure optimum rinsing
Non-toxic
Non-corrosive
Biodegradable
  Hallogens:
  available as gas/ hypochlorite solution, non-expensive
  Required: 130-250ppm
  Corrosive to metal
  Gets inactivated with organic matter
  Quaternary Ammonium compound:
  Cationic & bacteriostatic effect against gram positive organism
  Non effective in the presence of hard water & organic matter

## Slide 11: Ideal detergent
Prevent scale formation in hard water
Ensure optimum rinsing
Non-toxic
Non-corrosive
Biodegradable
  Amphoteric compounds:
  These are long chain substitutes amino acids or betains
  Surface active
  Un-effected by hard water
  Inorganic acids & alkali: rarely used in abattoir
  Tago compounds:
  Surface active & bacteriostatic compounds

## Slide 12: Chemical and physical reactions of cleaning
Physical rection:
  Wetting
  Penetration
  Emulsification
  Dispersion
  Solubilization
Chemical reaction:
  Hydrolysis of protein & carbohydrate
  Saponification of fat, oils & greases
  Chelation of insoluble metol ions
  Oxidation of color materials, starches etc.
  Corrosion inhibition
  Enzymolysis

## Slide 13: Application methods
Manual cleaning
Foam cleaning: for large equipment's
Gels: use special chemicals & spray equipment's to give a thick, viscous layer of detergent that clings strongly even on vertical surfaces
Spray:
Fogging:

## Slide 14: Cleaning-in-Place (CIP)
Extensively used for the internal cleaning of pipes, vessels, tankers, heat exchangers, filters etc.
Mainly use in Breweries & diaries
It includes:
Timed pre-rinse
Cleaning
Rinsing stages

## Slide 15: Cleaning in Place (CIP)
Flow velocity: 1.5- 2m/s
The spray pattern & pressure: 1-3 bar for low pressure system, 6 bar for high pressure system
The temperature: 82oC
Detergent control
Chemical energy & foam control
Recycling of detergent solution