## Slide 1
DTC-311 (Chemical Quality Assurance)
Binod Kumar Bharti
Assistant Professor cum Jr. Scientist
Department of Dairy Chemistry
S.G.I.D.T. (BASU) Patna
SOFT AND HARD WATER, TEMPORARY AND PERMANENT HARDNESS, Treatments of water

## Slide 2: Contents
Introduction
Types of Water
Treatments of water
a. Cold lime method
b. Base exchange softening method
c. Demineralizing (Deionizing) water supplies
c. Filtration
d. Reverse osmosis systems
4. Chlorination
5. Conclusion

## Slide 3: Introduction
Water as an essential nutrient is second only to oxygen in importance to sustain life and optimize growth, lactation, and reproduction of dairy cattle.
Water is a basic renewable natural resource upon which the survival and well being of living organisms depend.
Water is also essential to the food supply and habitat of all other living organisms.
The food industry uses large quantities of water.
It is the most necessary item of the dairy and food industry.

## Slide 4
Uses of water-
Water is used for generating steam, cleaning, grading, and conveying products, as a heat exchange medium in heating and cooling operations,
for cleaning plant and equipment,
for condensing vapors,
for the fire protection,
sanitizing,
drinking,
as an ingredient in the finished products and
as a waste disposal.

## Slide 5
Water plays a versatile role in food industry, so water must be in adequate supply, safer and of high quality.
The supply of adequate quantity and safe quality of water is of vital importance to the food industry particularly to dairy industry.
Management of water in food industry consists of three main components such as
quality at entry level,
water conservation and
waste management.

## Slide 6: Types of Water
Normally water is classified into two groups-
Hard water and
Soft water.
Water hardness is due to the presence of di- cations including Ca2+ and Mg2+.
Water hardness is further classified into two types:
Temporary hardness and
Permanent hardness.

## Slide 7
Temporary hardness
Temporary hardness is mainly caused by the carbonates and bicarbonates of calcium and magnesium.
It can be easily removed by boiling of water.
Permanent hardness
Permanent hardness is due to presence of sulfates and chlorides of calcium and magnesium in water.
Permanent hardness is not removed by simple boiling of water but it requires some complex operations.

## Slide 8
The combined effect of temporary and permanent hardness is called as total hardness of the water.
Temporary hardness is also known as carbonate hardness and permanent hardness is also known as non- carbonate hardness. Conventionally hardness of water is expressed in terms of ppm of calcium carbonate.

## Slide 9
In Dairy and food industry, the major problem caused by hard water is the deposition of scales in and on the pipes which can clog plumbing and interfere with heat exchangers.
These scale problem, are caused mainly of calcium carbonate (CaCO3), magnesium hydroxide [Mg(OH)2], and calcium sulfate (CaSO4).
Calcium and magnesium carbonates tend to precipitate out as hard deposits to the surfaces of pipes and heat exchanger surfaces.
In boilers, the deposits act as an insulation that damages the flow of heat into water, reducing the heating efficiency and allowing the metal boiler components to overheat.

## Slide 10
The following equilibrium reaction refer to the formation of calcium carbonate scales
CaCO3 + CO2 + H2O ⇋ Ca2+ + 2HCO3-
Hard water, form white precipitate with soap solutions, instead of producing lather.
This effect arises because the di- cations destroy the surfactant properties of the soap by forming a solid precipitate.

## Slide 11: Physical and Chemical tolerances (BIS, 1981)
Sl. No. | Characteristics | Tolerance
1 | Turbidity (units) max. | 10
2 | Odour | None
3 | pH | 6.5-9.2
4 | Total Solid (mg/L), max. | 1000
5 | Total hardness (as CaCO3), mg/L max. | 600
6 | Sulphate (as So3), mg/L, max. | 200
7 | Fluoride (as F), mg/, max. | 1.5
8 | Chloride (as Cl), mg/L, max. | 250
9 | Iron (as Fe), mg/L, max. | 0.3
10 | Arsenic (as As), mg/l, max | 0.2
11 | Mercury (Hg), mg/L, max. | 0.001

## Slide 12: Additional tolerances for specific operations
Characteristics | Tolerance for |  | 
Total Hardness (as CaCO3), mg/L, max | Cooling | Washing, flushing and general purpose | Processing
 | 30 | 30 | -
Iron (as Fe), mg/L, max | - | 0.1 | 0.1
Manganese (as Mn), mg/L, max | - | - | 

## Slide 13: Treatments of water

## Slide 14
Water treatment is the process of making water suitable or acceptable for an end-use.
It removes existing water contaminants and so reduces their concentration that the water becomes fit for its desired application.
The amount & type of treatment process (Treatment Train ) depends upon quality of raw water and various standards required after treatment.

## Slide 15: SOFTENING OF HARD WATER
Dairy and Food processors always treat at least some of the water used in the plants. This is due to the special requirements for use in boilers, cooling towers, heat exchanger and similar equipment.
Treatment of water may be done to control corrosion and formation of scale on equipment, to remove the turbidity caused by solids, to eliminate staining, odor and flavor problems, and also to assure safety for consumption.
Satisfactory procedure for water supply may be inadequate for another. Designing a water treatment system for a food plant must be considered on an individual plant basis.

## Slide 16: Turbidity-Solids Removed
Turbidity process results from suspended particles in water. The particles may range in size from 100,000 millimicrons in diameter for fine sand to colloidal suspensions with particle sizes between 1 to 200 millimicrons.
To produce clear water, removal of particles in colloidal suspension is usually essential.
Since colloidal suspensions are relatively stable, a coagulant is used to cause aggregation of particles of sufficiently high density to promote settling out for clarification.
Some inorganic chemicals are used as coagulants are Ferric sulfate, Ferrous sulfate, Filter alum, Sodium aluminate.

## Slide 17: Softening
Softening of water is done to remove the hardness of water due to deposition of minerals.
Different methods are applied for water softening as:
1. Cold lime method
2. Base exchange softening method
3. Demineralizing (Deionizing) water supplies
4. Filtration
5. Reverse osmosis (RO) system

## Slide 18: Functions of Water Treatment Units
Unit Treatment | Function (Removal)
Aeration, chemical use | Colour, Odour, Taste
Screening | Floating matter
Chemical methods | Iron, manganese
Softening | Hardness
Sedimentation | Suspended matter
Coagulation | Suspended matter, a part of colloidal matter and bacteria
Filtration | Remaining colloidal dissolved matter and bacteria
Disinfection | Pathogenic bacteria, Organic matter and reducing substance

## Slide 19: 1. Cold lime method
Many municipal water treatment plants use the cold lime softening method.
In this method, calcium oxide (CaO) is added to the hard water to form calcium hydroxide, which reacts with magnesium and calcium bicarbonates and free CO2 to form insoluble calcium carbonate and magnesium hydroxide.
Magnesium hydroxide is used a good flocculating agent which aids in precipitating the calcium carbonate particles.
This treatment will usually result in water with about 70 to 85 ppm of calcium (4 to 5 grains per gallon) when discharged from the final filtration unit.
Sand and gravel filters are commonly used for removing the precipitated salts by the cold lime softening method.

## Slide 20: 2. Base exchange softening method
Most food plants uses the base-exchange process for softening the water for cleaning and other uses.
The main materials used in the ion exchange are natural or synthetic zeolites which often are hydrous silicate or styrene based resins.
Mostly Sodium zeolite softening is use of ion exchange.
In zeolite softening, water containing scale-forming ions, like calcium and magnesium, it passes through a resin bed containing strong Acid Cation resin in the sodium form.
Softening water with a sodium cycle ion-exchanger is most commonly found in processing plants.

## Slide 21: 3. Demineralizing (Deionizing) water supplies
The demineralized (deionized) water treatments are used for beverage industry.
Several variations are found in demineralization systems depending on the analysis of the untreated water and the desired purity of the treated water.
Systems for demineralizing water are basically of two types- multi-bed and mixed-bed.
Mixed-bed units offer the advantage of less space required, and they will also produce high quality water.
Multi-bed and mixed-bed ion ex-changers are sometimes sequenced into a system to produce very high quality demineralized water.

## Slide 22: 4. Filtration
Filtering is almost common methods in a water treatment system.
In many cases, water is filtered before softening or demineralizing process. It depending upon the system and quality of water desired, the final step may be filtration.
Large water treatment plants for municipalities will regularly use by gravity type filters.
Generally, food processing plants will usually find the enclosed pressure type filters with more satisfactory.

## Slide 23: 5.Reverse osmosis systems
The reverse osmosis (RO) technology is advancing rapidly.
Reverse osmosis separates one component of a solution from another by placing the solution under pressure against a semi permeable membrane.
Normally the pores of the semi permeable membranes used in RO are 5 to 20 Angstrom units (5 to 20 x 10-8 cm) in diameter.
A number of membranes have been developed, and generally cellulose acetate is used.
Reverse osmosis is a method of purifying water to a high degree, especially when used in conjunction with a prefilter and an ion-exchanger.
Advantages-
Chemicals are unnecessary, membrane life is normally 1-3 years, low maintenance requirements, pressure is the only energy requirement.

## Slide 24: Chlorination of Water Supplies
Addition of small amounts of chlorine to water supplies acts as a safeguard against water-borne diseases.
Food processing plants unit have increasingly been chlorinating water to improve sanitation.
Chlorine may be added to water systems in food plants as type of gas or as a solution of chlorine compounds which are mainly hypo chlorites of sodium or calcium.
Some plant operators have found chlorine dioxide to be very satisfactory where considerable organic matter is present, such as in recycled water systems.

## Slide 25: Chlorine Dose rates for specific purposes
Purpose of water | Dose rate (ppm)
Well | 1.5
Surface | 110
cooling | 3-5
chilling | 20
Washing | 50

## Slide 26: Conclusion
Water is an essential to the food supply and habitat of all other living organisms. The dairy and food industry uses large quantities of water. Water is used for generating steam, for cleaning plant and equipment, for condensing vapors, for sanitizing, for drinking, for waste disposal etc. Generally, Hard water and Soft water are found. Water hardness is due to the presence of di- cations including Ca2+ and Mg2+. Temporary hardness is mainly caused by the carbonates and bicarbonates of calcium and magnesium. It can be easily removed by boiling of water. Permanent hardness is due to presence of sulfates and chlorides of calcium and magnesium in water. It can not removed by simple boiling of water but it requires some complex operations. There are various methods are uses for treatments of hard water such as cold lime, Base exchange softening, Demineralizing (Deionizing) water supplies, Filtration, Reverse osmosis (RO) system and chlorination methods.

## Slide 27: Thank You