## Slide 1: Milk Reception, Cooling and Storage
By
J. Badshah
Univ. Professor, Dairy Engineering
SGIDT, Patna ( BASU, Patna)

## Slide 2: Milk Reception in Cans
Equipments for Reception of Milk in Cans at RMRD
  Chain Conveyor
  Tipping bar and Tilting Device
  Weighing Bowl with weighing Balance
  Dump Tank
  Can Washer with drip saver and chain conveyor
  Steaming Block
  Can scrubber
  Platform Balance
Quality Control Labs adjacent to RMRD

## Slide 3: Receiving Operations through Cans
Reception of milk and Cleaning & sanitizing of cans
  Off- loading of cans on chain conveyor
  Grading of milk to separate Sour Milk
  Weighing and sampling in duplex weighing Bowl of a batch and transferring to Dump tank
  Pumping milk from Dump Tank to milk Chiller
  Storage of Milk in RMST
  Inverting empty cans on Drip saver
  Conveying inverted cans to Can washer
  Sterilizing the washed cans
Quality tests of samples and Platform tests etc.

## Slide 4: Hygienic Rception and Platform Tests
Temperature, Time before chilling and bacterial growth
Sensory Evaluation or organoleptic Tests
Platform Tests
  COB test (Clot- on – Boiling Tests)
  Alcohol Tests
  Alizarin- Alcohol Tests
  10 minute Resazurine Tests
  Methylene Bluie Reduction Tests

## Slide 5: Can Washer Operation
Draining of milk or cream remains
Rinsing with normal tap water
Rinsing with warm water at 40 to 50°C
High velocity hot Dtergent cleaning at 71°C with alkalinity not more than 0.15%. Use of 0.5 % solution of sodium metasilicate and sodium carbonate with or without sequestering agent (if water is hard)

## Slide 6: Can Washer Operation..contd.
Rinsing with recirculated hot water at about 88°C
Rinsing with clean hot water
Steaming with dry saturated steam at 2.5 Kg/cm2 gauge.
Hot Air blasting at 110°C for drying of the cans to prevent corrosion and bacterial growth
Sanitizing with chlorine solution of 100-200 ppm or steaming in steam block

## Slide 7: Maintenance of Can Washer
Frequent Inspection of mechanical movement parts, lack of adjustment and worn out parts
Worn out bushing be replaced
Lubrication of moving parts
Washer and strainers cleaning
Cleaning of nozzles and tanks
Descaling of the can washer

## Slide 8: THANKS