## Slide 1: Homogenization of Milk Dairy Engineering(DTE – 212)
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Different between Process Control & Product Control
S.No. | Unhomogenized Milk | Homogenized Milk
1. | Milk Fat in the form of globules from 0.1 to 20 mm. | Fat globule size is reduced to 1 micron or less.
2. | Wide variation in density of fat globules and wide variation in size. | No variation in density and size of fat globules
3. | Formation of cream layer when the milk is left undisturbed causing non uniform distribution in the sense of quality of milk. | Prevents creaming in stored milk and packed milk causing uniform quality distribution to the consumer.
4. | Surface area of fat globules are about five times lesser in unhomogenized milk | Homogenization uses the principle of increasing the surface area providing richer flavour to milk but at the cost of expense of energy. .
5. | Curd tension is higher and digestibility of unhomogenized milk and products made from it is lower. | It brings physical changes in milk proteins resulting in lower curd tension that increases digestibility of homogenized milk.

## Slide 3: Effects of Homogenization on properties of milk
UV Light Susceptibility
Effect on viscosity due to shearing and cavitation action in first stage homogenization
Effect on viscosity in second stage homogenization
Effect of activation of inherent lipase system due to homogenization- hydrlytic rancidiy
Necessity of pasteurization of milk after homogenization to inactivate the lipase enzyme
Why homogenization of milk at a temperature of 57°C
  Higher efficiency
  Activity of lipase on newly formed fat globule surfaces
  Homogenization Index= (A- B) /B x 100
  Homogenization Index between 1 to 10: Good

## Slide 4: Theory of Homogenization
Shearing of milk layers
  High shear gradients/ velocity gradients
  Accelerating and retarding shearing action
  Thread like shapes to form small globules with small forces
  Disintegration of fat globules
Cavitation in flow of milk
  Kinetic energy increases and potential energy decreases
  Static pressure becomes as low as vapour pressure of liquid which forms the vapour bubbles
  Implosion of vapour bubbles with breaker ring causes deformation and disintegration of globules
Micro turbulence
  High velocity of 100 - 250 m/s through narrow slit
  Turbulence and collission with breaker ring
  Turbulence, implosion and disintegration of fat globules

## Slide 5: Process of Homogenization
Pumping of Milk at 60 -65 °C throough a small passage at high velocity at a pressure ranging 10 – 25 Mpa depending on the product
Net result is reduction of size of fat globules to 1 -3 microns size and Five fold increase in surface area
Single Stage Homogenizaton produces cluster by forming new membranes on newly formed small fat globules due to shearing and cavitation:Pressure -175 -210 Kgf/cm2
  Low fat content
  High viscosity desired
  Two Stage Homogenization produces low viscosity product by further turning apart any cluster formation with high fat content of milk or products: Pressure- 35 Kgf/cm2
  Clustering factors and increase in temperature Delta thita = P/40 if P is in Kgf/sq. cm.

## Slide 6: Component of Homogenizers
First stage Homogenizing Valve
Suction Manifold
Discharge Manifold
Feed Line
Pressure gauge in discharge manifold
Breaker Ring
Second Stage Homogenizing Valve
Triplex pump driving Crankshaft, Connecting rod, Piston and cylinder valve mechanism and lubricants etc.
Driving Electric motor

## Slide 7: Components of Homogenizers

## Slide 8
THANK YOU