## Slide 1: Power Consumption by Impeller Mixers
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Selection & Construction of agitators
Volume or amount of the products ti stirred
Viscosity and Rheological Characteristics of the products
Sensitivity of the structure of products
Density and shear gradients affecting sensitivity
Size and shape of the tank
Sufficiency of stirring with minimum power

## Slide 3: Power consumed by agitators
Power Consumption is proportional to the volume stirred per unit time (Q) and kinetic energy (ρ V2), where
V= Peripheral velocity = π d n
Volume stirred per unit time, Q α V .d2
Power consumption α Q ρ V2
Power consumption α V.d2 ρ V2
Power consumption = Power Number or Newton Number Po x V3.d2 ρ = Po x n3.d5 ρ
Power Number or Newton Number Po = Power consumption/ n3.d5 ρ = function of Reynolds Number (NRe)

## Slide 4: Power consumed by agitators
Reynolds Number NRe = ρ nd2 /μ
Dimension less Froud Number NFr = n2 d/g
For Unbaffled Tanks, the movement due to gravity or aeration is predoinant at NRe > 300 and the equation for Power Consumption is as follows:
Po / (NFr )m =f (Nre , S1, S2, S3, S4, S5)
Power consumption in unbaffled tanks =
Po x(NFr )m n3.d5 ρ
Power consumption in baffled tank = Po xn3.d5 ρ

## Slide 5: Shape Factors
S1 = d/dt
S2 = E/dt
S3 = L/d
S4 =W/d
S5 =J/dt
S6 =H/d

## Slide 6
THANK YOU