## Slide 1: Buoyancy AND FLOATATION
J. Badshah
SGIDT, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Principle of Buoyancy
During a floating body in equilibrium of weight W, the upthrust (U) on a body is equal to the weight of the volume of fluid displaced by the body and Since the body is in equilibrium, the W = U.
This is known as Archimedes’ Principle.
If W is greater than U, the body will sink in liquid.
If W is less than U, the body will float and rise until the buoyant force reduces and becomes equal to W. Only that much portion of the body will be submerged which will displace the fluid equal to the weight of the body. The body which is partially submerged are called Floating body.

## Slide 3: Floating Body
On a strip of area dA and height h, there are two pressures at the end. These are p1 dA and P2 dA
The difference between upword and down ward forces is the buoyant force
dU= p2 dA – p1 dA
=( p1 + Ꞅh )dA – p1dA = Ꞅh dA = ꞄdV
Where dV is the volume of vertical prism in the liquid. The buoyant force on the entire ABCD = ∫ dU = ∫ ꞄdV = ꞄV

## Slide 4: Stability of Floating BOdies
For the body to be in equilibrium, the downward force due to weight acting through centre of gravity and upward buoyant force acting through centre of buoyancy must be collinear, equal in magnitude and act in opposite direction.
A body is said to be stable, if tends to return to its original position after it had been tilted through a small angle.
The body is said to be unstable if it does not return to its original position.
The body is said to be in neutral position if it remains in the new position.

## Slide 5: Stability of Submerged Bodies
A fully submerged body is in stable equilibrium if its centre of gravity is below the centre of Buoyancy.
For a floating body to be in stable equilibrium, it is essential that the metacentre be above the centre of gravity. The metacentre is the point which is an intersection of line of action of U through new centre of buoyancy B1 with the axis through centre of gravity G.

## Slide 6: THANK YOU