## Slide 1: Derivation for Non- Newtonian Flow and Numericals
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Derivation for non-Newtonian Fluid flow in a pipe
Consider the mechanism of liquid flowing through a pipe/tube by overcoming shearing resistance with a pressure difference across the cross section beween the length of pipe.
Let the radius of pipe as R, diameter be D and length of shearing area of pipe is L. For an elemental ring at r from centre with a thickness dr, the ring area is 2πr dr. The shearing area of elemental ring is 2πrL and cross sectional area of element is πr2.

## Slide 3: Motion of Fluid Foods in a pipe
On equilibrium at point r =r , consider the force balance on the cross section between P1 and P2. The shear force for area 2π r L is equal to the force due pressure difference on the element i.e.
Ꞇ . 2π r L = (P1 – P2) πr2
Therefore, Ꞇ = (P1 – P2) .r/2L -------------------(1)
Consider the fluid as non-Newtonian
Therefore at radius r, Ꞇ = m(- dv /dr)n --------- (2)
From equation 1 and 2, we have
∫ - dv = (∆P/2mL)1/n . ∫ r1/n dr Integrating from r =r to r = R for velocity from vr to zero, we get
Vr = (∆P/2mL)1/n n/(n+1)(R(n+1)/n - r(n+1)/n) -----------(3)
and average velocity vavg
Vavg . πR2 = 2π (∆P/2mL)1/n n/(n+1)∫r(R(n+1)/n - r(n+1)/n)dr

## Slide 4: Derivation for Velocity profile in Newtonian flow through a pipe
Therefore, v avg = (∆P/2mL)1/n . n/(3n+1) R(n+1/n) ------(4)
This is a Rabinowitsch-Mooney equation Equation The velocity profile can be obtained from equation 3 and 4:
Vr/vavg = [(3n+1)/(n+1)] [1- (r/R)(n+1)/n] -----------------(5)
At r=0 , vr = Vmax and at r = R, vr = 0
Keeping the values in above equation (5) for flow behavior index n =1
Vr/vavg = 2 [1- (r/R)2] and Vmax = 2 vavg, This is the condition of laminar flow and velocity profile is completely parabolic.

## Slide 5: Flow Rate Equation for non- Newtonian Flow
Flow Rate Q = ∫(0 to R) Vr . 2πrdr
Q = ∫(0 to R) (∆P/2mL)1/n n/(n+1)(R(n+1)/n - r(n+1)/n) . 2πrdr
Q=2π(∆P/2mL)1/n n/(n+1) ∫(0 to R)[(R(n+1)/n - r(n+1)/n) . rdr]
Q = π (∆P/2mL)1/n [n/(3n+1)]R (3n+1)/n
The Rheological parameter m and n can be determined for developing model of fluids by taking log on both side. Finally draw a graph between log (∆P/2L) and log Q obtained by measurement during experiment of flow through a tube viscometer. The slope of the line will be n and the intercept at certain value of log Q can determine the value of m by substituting and calculating from the final equation of log (∆P/2L) versus log Q.

## Slide 6: Flow Rate Equation for non- Newtonian Flow
Log Q = logπ+1/n. log(∆P/2mL)+ log [n/(3n+1)]+ (3n+1)/n log R
n log Q = n logπ + log(∆P/2mL)+ n log [n/(3n+1)]+ (3n+1) log R
log(∆P/2mL) = - n logπ - n log [n/(3n+1)]- (3n+1) log R +n log Q
log(∆P/2L) =[log m- n logπ - n log [n/(3n+1)]- (3n+1) log R] +n log Q
It is a straight line equation if we draw a graph between log (∆P/2L) and log Q. The slope will give flow behavior index ‘n’ and intercept would result on calculation the consistency coefficient ‘m’. Solve numerical for Determining rheological parameter, if ∆P and Q are given.

## Slide 7: Maximum Shear Rates in non-Newtonian Flow through a Pipe
From Equation (5), the velocity Profile forNewtonian Flow through a pipe is given as:
Vr/vavg = [(3n+1)/(n+1)] [1- (r/R)(n+1)/n] -----------------(5)
On Differentiating, we have
dvr/dr = [(3n+1)/n] vavg [r1/n/R(n+1)/n]
For maximum shear rate at the wall of pipe, r = R and we have from above equation:
(dvr/dr )at r =R = [(3n+1)/n] [vavg. /R] = (4 vavg ) / R[3/4+1/4n]
ϓw maximum shear rate at wall for n =1 = 4 vavg / R and minimum shear rate at the centre of a pipe i.e. r =0, zero.

## Slide 8: Numerical on non-Newtonian Flow
A tube viscometer with0.267 cm diameter and 0.91meter length was used to obtain the following data for apple sauce product:
S.No. | ∆P (105x Pa) | Flow Rate Q (10-4xm3/s)
1. | 1.30 | 0.91
2. | 1.45 | 2.50
3. | 1.56 | 2.10
4. | 2.00 | 3.20
5. | 2.13 | 5.20
6. | 2.41 | 8.50
7. | 2.70 | 12.50

## Slide 9: Numerical
Solution: Draw Table for log (∆P/2L) and log Q
S.No. | ∆P/2Lx 105 | log (∆P/2L) | log Q
1. | 0.715 | 4.85 | -4.04
2. | 0.795 | 4.90 | -3.82
3. | 0.855 | 4.93 | -3.68
4. | 1.095 | 5.04 | -3.50
5. | 1.17 | 5.07 | -3.29
6. | 1.33 | 5.12 | -3.07
7. | 1.49 | 5.17 | -2.90

## Slide 10: ….Contd.
Draw a graph between log (∆P/2L) and log Q , we have flow behaviour index n as 0.28 ( Slope of the line).
The intercept is 5.15 for log Q as – 3.0. Substituting in equation we have m = 4.074 Pa –sn ., Ꞇ = 4.074(- dv /dr)0.28
Experimental results with a coaxial cylinder viscometer used for banana puree at 340 K were as follows and determine the rheological parameters required to describe the product.
S.No. | Shear rate (10-3x1/s) | Shear stress(10-4 x Pa)
1. | 1 | 1.06
2. | 1.5 | 1.22
3. | 2.0 | 1.37
4. | 3.0 | 1.62
5. | 4.0 | 1.80
6. | 5.0 | 2.01
7. | 6.0 | 2.10
8. | 7.0 | 2.21

## Slide 11
THANK YOU