## Slide 1: Dynamic Measurement of Viscoelastic Foods
Dr. J. Badshah
University Professor-cum- Chief Scientist
Sanjay Gandhi Institute of Dairy Technology
(Bihar Animal Sciences University, Patna)

## Slide 2: Cone and Plate Viscometer and Parallel Plate Viscometer
Oscillatory Mode Measurement: To measure time dependent viscoelastic properties of viscoelastic foods, Cone and Plate viscometer and Parallel plates viscometers are used in oscillatory mode.
The lower plate is made to oscillate at a frequency of ω radian /second giving a sinusoidal varying strain in food materials kept on lower plate with a maximum amplitude of Ꞅ0 and strain of Ꞅ, which is
Ꞅ = Ꞅ0 Sin ωt
d Ꞅ/dt = Ꞅ0 ω Cos ωt

## Slide 3: Shear stress under oscillating mode
The shear stress is deduced for torque measurement on the upper plate also vary sinusoidly at the same frequency as the oscillation given to strain but it will be shifted out by an angle del ($) depending upon the elastic component:
For Newtonian Fluid
Ꞇ = μ ( d Ꞅ/dt ) = μ Ꞅ0 ω Cos ωt = μ Ꞅ0 ω Sin (π/2 +ωt )
Therefore del ($) = π/2 for viscous fluid i.e. π/2 radian out of phase with strain. For an Ideally Elastic solid, shear stress is in phase with strain and Ꞇ = G( Ꞅ )

## Slide 4: Del for Viscoelastic Food
For Viscoelastic material, in which viscosity and elasticity both are present eg. Milk Gel. Del has a value between 0 and π/2.
G’ (ω) = Ꞇ0 / Ꞅ0 Cos (del)= Storage Modulus (This is elastic part of stress)
G” (ω) = Ꞇ0 / Ꞅ0 Sin (del)= Loss Modulus(This is viscous Part of stress)
Tan (del) = G” (w) / G’ (w)
G* Complex Modulus = √ [(G’ (ω)2 + G” (ω)2 ]

## Slide 5: Characteristics of Viscoelastic Foods
Wissenberg Effect: On Agitation the fluid may climb the impeller haft
Jet Swell: When viscoelastic fluid exit as a jet from a nozzle, it will swell or expand two or more times.
Tubeless Syphon: Fluid tends to climb in the tube and comes out of cylindrical vessel.

## Slide 6: Tests on Dynamic mechanical Analysis
Cure Test: In this test sample is hold at constant temperature and frequency
Temp. Sweep: In this test, temp. is increased at a fixed frequency
Strain Sweep: Increasing strain amplitude at a fixed frequency
Frequency Sweep:Increasing the frequency of oscillation a a fixed strain
Sress Relaxation: Relaxation of the stress at the constant strain.
It is used for Paneer, Cheese, Meat, Fruits pulp, Yoghurt, Dahi and Meat Paste/ Fish Paste, Vegetabl;es pulp etc.

## Slide 7: THANKS