## Slide 1: Hydrostatic Forces On Gate of Dam- Vertical and Inclined
J. Badshah
SGIDT, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Measurement of pressure
Total Pressure P = Ꞅ A h bar
Centre of Pressure h’ = IG/A hbar + hbar
Total Pressure on inclined plane P = Ꞅ A h bar
Centre of Pressure on inclined Plane h’ = IG Sin2 Θ/ A h bar + h bar
Where Θ = Inclination of the surface with horizontal
For horizontal Plane Θ =0, h’ = h bar
For vertical Planes Θ = 90°, h’ = IG/A hbar + hbar

## Slide 3: Solving Problems on Hydrostatic Forces on Gate
Calculate the total hydrostatic pressure on the gate AB of the vessel shown in Figure. The width of the gate perpendicular to the plane of paper is 1 meter. The liquid in the vessel is water having specific weight as 1000 kgf/m3 .
Solution: Force =Total Pressure P = Ꞅ A h bar =1000x(2x1)x2 = 4000 Kgf
The depth of center of Pressure= (IG/A hbar ) + hbar, = 1/12 x 1 x 23 / (2x1)x2 +2 = 2.17 meter

## Slide 4: Problems on Inclined Plane
Calculate the total pressure and the depth of the centre of pressure on the inclined gate shown in Figure. The width of the gate perpendicular to the plane of paper is one meter.
Total Pressure = P = Ꞅ A h bar = 1000 x (2x1) [1 + 1/√2] = 3420 kgf
Centre of Pressure h’ = IG Sin2 Θ/ A h bar + h bar = 1/12 x1 23 (Sin 45)2 /(2x1) 1.71 + 1.71= 1.807 m

## Slide 5: THANK YOU