## Slide 1: Flow through Pipes discharging from a Reservoir
By
Dr. J. Badshah
University Professor-cum-Chief scientist
Dairy Engineering Department
SGIDT, PATNA
(Basu, Patna)

## Slide 2: Pipe Discharging from a Reservoir
Applying Bernoullis Theorems between A and B
hL
v2/2g E.G.L. hf
H H.G.L.
A B

## Slide 3: Pipe Discharging from a reservoir
Applying Bernoullis Theorems equation to points A ( at the joint with reservoir ) and B (At the end of pipe):
H = hL+ hf + V2/2g, hL = Loss of head at the entrance
hf = Loss due to friction in the entire length
V2/2g = Distance between hydraulic gradient line and energy Gradient line
If the entrance to the pipe is flush with the reservoir,
hL = 0.5 V2/2g and

## Slide 4: Pipe Discharging from a reservoir
Frictional head is given by, hf = f L/D (V2/2g )
H = V2/2g [1.50 + f L/D]
For Long pipes, the term fL/D is very large compared to 1.50, then in such cases, the loss of head at the entrance and exit may be neglected. When the length of pipe is greater than 1000 D, only the friction loss need to be considered.
Numericals will be followed on white board by sharing it.

## Slide 5: Numericals on Pipe Discharging from a reservoir
Water is discharged from a large reservoir to atmosphere through a 10 cm diameter and 500 m long pipe. Find the discharge if the outlet is 15 m below the free surface of water in the reservoir. Assume the entry to the pipe as sharp. Take friction factor f = 0.04.
Solution: H = V2/2g [1.50 + f L/D]
15 = V2/2g [1.50 + 0.04. 500/ 0.10]
Therefore V = 1.21 m/s
And Discharge Q = AV = π/4 x 0.1x0.1x1.21 = 0.0095 cumecs

## Slide 6: Pipe Connecting Two Reservoirs
The liquid flows from the higher reservoir to the lower reservoir. The total losses is equal to the difference of liquid levels in the two reservoir.
If the difference of liquid levels in the two reservoirs = H
H = hL+ hf + V2/2g = 0.5 V2/2g + hf + V2/2g
hL = Loss of head at the entrance
hf = Loss due to friction in the entire length
V2/2g = Distance between hydraulic gradient line and energy Gradient line

## Slide 7: Pipes in series connecting between two reservoirs
Difference in liquid levels between two reservoirs = hL1 + hf1 + hL2 + hf2 + hL3 + hf3 + V3 2 /2g, where
hL1 = Losses at entrance
hL2 = Losses at contraction in figure
hL3 = Losses at enlargement
Hf1 , hf2, hf3 are losses due to friction in three pipes in series
V3 = Velocity in pipe 3
Q1 = Q2 = Q3 and A1V1 = A2V2= A3V3

## Slide 8: .
.
Thank You